## Slide 1: Aruba Networks Outdoor Coverage Planning Tool
Presented by
Marcus Christensen
Channel SE
Nov. 2011
8:30a – 9:30a Pacific

## Slide 2: Module Overview
Overview
Software recommendations
User Workflow
Determining customer requirements
Working up a plan:
  Part 1 in Google Earth
  Part 2 in the Aruba Outdoor Planning tool
  Part 3 back in Google Earth

## Slide 3: Overview

## Slide 4: Overview
Web based
  File Processor
  Model Generator
Procedure
  Generate Google Earth file (.kmz)
  Process it
    RF settings and parameters
  Output new Google Earth file (.kmz)
    RF coverage added
    Mesh visualization models added
Notes: The Aruba Outdoor RF Coverage planner is a web based file processor and model generator. As such, the utility takes a previously created Google Earth file (*.kmz), processes it for the settings and RF parameters, then outputs a new Google Earth file (*.kmz) with the RF coverage and mesh visualization models added.

## Slide 5: Software Recommendations

## Slide 6: Equipment Recommendations
Google Earth Professional
  (Required for Commercial Use)
DirectX and OpenGL compatible Video Acceleration
  (See Google Earth Requirements)
Update Video Drivers (from hardware vendor)
Notes: Since the utility generates 3D graphical models for viewing, the following hardware and software is recommend:
Google Earth Professional Version (Required for Commercial Use)
DirectX and OpenGL compatible Video acceleration (See Google Earth Requirements for minimum)
Updated Video Drivers from laptop/PC hardware vendor

## Slide 7: Google Earth Overview
 | Google Earth | Google Earth Plus | Google Earth Pro
License | Home/Personal | Enhanced Home/Personal | Professional (commercial use)
Price | Free | $20 | $400
Imagery Database | Primary | Primary | Primary
Performance |  | Enhanced | Fastest
Fly to anywhere on the planet | Yes | Yes | Yes
Search for landmarks | Yes | Yes | Yes
Get driving directions | Yes | Yes | Yes
Explore Featured Content | Yes | Yes | Yes
Tilt and rotate in 3D | Yes | Yes | Yes
Printing images | 1000 pixels | 1400 pixels | 4800 pixels
Saving Images | 1000 pixels | 1000 pixels | 4800 pixels
Drawing tools | Yes | Yes | Yes
GPS data import |  | Yes | Yes
Real-time GPS tracking |  | Yes | Yes
Spreadsheet data import |  | 100 points | 2500 points
Local Business Ads | Yes | Optional | Optional
Support | Website only | Website, email (login issues only) | Website, email, chat
Measure area |  |  | Yes
Movie Maker |  |  | Yes
GIS data importing |  |  | Yes
GDT traffic counts data |  |  | $200

## Slide 8: User Workflow

## Slide 9: User Workflow

## Slide 10: Determine Customer Requirements

## Slide 11: Determine Customer Requirements/Gather Site Info
Facility location (address, Lat/Lon, Google Earth placemark
Facility plan (CAD drawing or map)
  Available AP mounting locations
  AP mounting heights
  PNG format
Understanding of customer coverage needs
Expected bearing of directional antennas
  Download the Aruba Antenna Matrix:
    http://www.arubanetworks.com/pdf/products/matrix-antennas.pdf
Desired data rates and services (802.11a/b/g/n)
Client device info (power/antenna gain)
Bridging or Mesh requirements
Availability of Ethernet/Fiber/power
Notes: Prior to starting an outdoor RF plan, the following information will need to be collected from the customer in order to present an effective proposal:
Facility Location (Address or Lat/Lon), or ideally a Google Earth placemark
A facility plan (CAD drawing or map) showing available AP outdoor mounting locations (approximately, or to best of knowledge). All drawings and maps will be converted to png (portable network graphic) or jpeg format for use in the planning tool
A clear understanding of the coverage areas
AP mounting heights for known or expected typical mounting locations
For directional antennas, expected direction from mounting location to coverage area
Desired Data Rates (min and max) and services (.11a/b/G)
Client Device info (power and typical antenna gain if available)
Areas believed to need bridging/mesh links due to lack of available Ethernet or fiber.
Mesh Nodes that will be used exclusively as Portals
Mesh Nodes that will be used as Mesh Points
Mesh Nodes that will be used as Multihop points by design

## Slide 12: Creating the Outdoor Plan in the tool

## Slide 13: Locate Property in Google Earth
Notes: Familiarity with the Google Earth Pro application is necessary in order to proceed. The user is advised to download and install Google Earth and familiarize themselves with the basic functions by using the available help and documentation from Google Earth. (http://earth.google.com). Note that a license for the Pro Version is required to use for commercial purposes.

## Slide 14: Create Project Folder
Select “My Places” and create a new folder for your project
KMZ file must contain a folder named “Locations” below the project folder
“Locations” must contain only placemarks, or folders with placemarks in them
“Locations” must contain at least one placemark
- Organize mesh networks in their own separate folder below the “Locations” folder
Notes: Once the property is in view, create the following folders in the left-hand pane by clicking on “My Places”, then using
Add>Folder
Create a Folder Structure as Shown in the slide. This folder structure is described as follows:
<Project Name>
<Locations>
<Group1>
-Placemarks for Group1
<Group2>
-Placemarks for Group2
<Map Images / Overlays>
Note that subgrouping of locations is optional and not required if there is not a need to subgroup (i.e. all placemarks can be directly under the “Locations” folder for smaller projects)
IMPORTANT TIPS !
The KMZ file must contain a folder named “Locations” with at least one placemark to proceed.
Do not put anything other than placemarks in the “Locations” folder.
If you are planning a point to multipoint mesh, it is helpful to organize the multipoint mesh point with their portals in the same folder under “Locations”
  <Group1>
    Portal Placemark
    Point Placemark
    Point Placemark

## Slide 15: Add Image Overlays (optional)
Detailed image overlays can be placed in Google Earth and can be used as the primary reference for AP placement
Image overlays should be imported into Google Earth as PNG files in order to have transparency control.
Notes: Image overlays such as CAD drawings and facility maps can be very useful to help place locations accurately. Most often, if a scaled CAD drawing of the facility is available, it will be better to place the locations of the APs relative to the drawing and effectively use the Google Earth imagery as supplemental.
In order to have transparency control in Google Earth, image overlays should be converted to “Portable Network Graphic” or “PNG” prior to import into Google Earth. This can be done by any image editing software, but it is recommend to take screenshots of the image and save sections of it as PNG files in Microsoft Paint. Note that any text on the drawing as you zoom in will only be readable to the level that you saved it in the original PNG file. So, for large drawings it is recommended to breakup the drawing into sections and ensure that the desired text is legible in each section using your normal screen resolution before you save the file as a PNG.

## Slide 16: Add Image Overlays (optional)
If you are creating image overlays from screen captures, zoom into the map so that the text is legible.
You may need to capture the map in many sections
Notes: Note that a screenshot of this entire map as shown in the left view would not make the text legible when imported to Google Earth.
Instead, sections of the map are “zoomed in”, as shown in the right view, to make the text legible, then saved as individual PNG files to overlay later in Google Earth.

## Slide 17: Importing the Image Overlay (optional)
When importing the image overlay, the image is usually not at the same scale as the map that is displayed in Google Earth
To scale the image overlay
  Reduce the transparency to approximately 50%
  Use landmarks such as roads, water features, and buildings aid with scaling.
Notes: To import the PNG Images, use the “Add>Image Overlay” function from the top menu bar and specify the file name for the image. This will bring in the image, which is usually not scaled properly.
To scale the image properly to the Google Earth background, it is recommend to do the following:
-Reduce transparency to approximately 50%
-while holding “Shift” key, hover on a corner to get a “+” control. This will uniformly scale the image about the center
-Using landmarks in two directions (roads, water features, etc), scale and align the background image with the imported drawing.

## Slide 18: Example of a Properly Scaled Image Overlay
Notes: The slide shows a properly scaled and placed map background image overlay. You will need to repeat this process until all the desired image overlays are loaded.
Important Tip – After adding, make sure that your image overlays are moved to the “images/overlay folder” and are not in the “Locations” folder. Also it is a good time to double check that both “locations” and “images/overlay” are subfolders under your project folder.

## Slide 19: Add Location Placemarks
Placemarks are locations where APs will be installed
Each placemark should have a unique name
Enter the height of the AP installation relative to the ground
Select “Extend to Ground”
Do not change the placemark icon (it will be changed by planning tool when the KMZ file is processed)
Notes: Be sure to name the placemark as a unique location. In addition, it is recommended at this time to set the altitude of the placemark to the altitude that AP’s can be mounted.
Go to the altitude tab and enter the altitude (in meters) and select “Absolute” or “Relative to Ground” depending on the information available. It is recommended to check “Extend to Ground” as this will drop a vertical line in the 3D view from the elevated placemark to ground level or onto your CAD image. Also, “Relative to Ground” is the recommended default mode for planning purposes.
Important Tip : Setting the altitudes for your locations to the best know value is critical to the accuracy of the modeling. With some antenna types the difference of a few meters altitude can make a large difference in coverage.

## Slide 20: Save the Initial KMZ File
Before saving the KMZ file check your project
Project hierarchy should be:
  My Places
  Project Name (folder – required)
  Locations (folder – required))
  AP Group (optional folder)
  AP Name 1 (placemark – at least one is required)
  AP Name 2 (placemark)
  Mesh AP Group (optional folder)
  Mesh Portal 1 (placemark)
  Mesh Point 1 (placemark)
  Mesh Point 2 (placemark)
  Map Overlays (folder – optional)
  Overlay 1 (image overlay – optional)
  Overlay 2 (image overlay – optional)
Make sure any overlay files are placed in an overlay folder under the project folder
Right click project and select “Save Place As”
After saving the project, delete the project folder from My Places
Notes: Once you have loaded the image overlays and entered and grouped placemarks, the KMZ file is ready to be saved.
To do this, right-click on the top level folder for your project and click a “Save Place As” and give the file a name.
Everything in your project must be contained in folders under your top level folder to be included in the saved file. Folders that are “horizontal” (not nested under your project folder) will not get saved to the file and can lead to errors.
After saving, it is recommend to delete the project folder from “my places” because re-opening it later will create a second instance of the same folder.

## Slide 21: Login to the Outdoor Coverage Planning Tool
https://outdoorplanner.arubanetworks.com
Notes: Once logged in, if your last session was interrupted before completing, or you saved your work in progress you may be asked the following question: “It appears that you have saved work from the last time you used this application. Would you like to restore your old work or start anew?”
You will only want to restore your old work if you intend to continue where you left off during an interrupted or incomplete session (due to browser close, timeout, etc.) and using the previously uploaded kmz file. Most often, you will be uploading a newly created or modified KMZ from your local drive, so should select “Start anew.” To upload your *.kmz file to the utility, proceed after “start anew”.

## Slide 22: Upload the KMZ file
The KMZ file that you created in Google Earth will now be uploaded so that you can modify and process it
Notes: If the file you are uploading is one that has been through the utility before, you will be asked the following question: “The KMZ file you’ve uploaded has been run through this tool before, would you like to restore your old work or start anew?”
If you are working with a file that you only want to make a few modifications to the model (for example change some antennas, etc.) click “restore your old work”. This will initialize the utility with all previous model definitions you had selected. If you select “Start Anew”, this will load the file as if it had never been through the utility before and reset all definitions.

## Slide 23: Define Global Parameters
Specify the proper country
-85 dBm is the recommended Noise Floor
Design margin is also referred to as “Fade Margin”
  Recommended values between 3 dB and 15 dB
  Considered a “design safety” factor
Notes: Country : Select the country where the installation is located. This sets the EIRP limits for each of the available services.
Noise Floor : -85 dBm is the recommended design value as a typical worst case
For known quiet or noisier environments, you can set the noise floor lower or higher.
Design Margin: The design margin is also sometimes called “Fade Margin” and can be considered a general “design safety” factor.
3 dB is the minimum recommended design margin and should be used when clients can be expected to always have a clear line of sight to the access point mounting locations in an obstruction and absorption free environment.
6 dB is recommended when clients typically have a clear line of sight to the access points, but may have minor obstructions like light vegetation. This is the recommended standard design margin for general planning purposes. Note that 6 dB is a design safety factor of 2 in linear distance terms.
10 dB is recommended for environment with heavier vegetation, or crowds or when high gain (>6 dBi antennas) are planned to be used for ground coverage. Note that 10 dB is a design safety factor of 3 in linear distance terms.
15 dB is recommended for areas of heavy vegetation and/or heavy crowds and should only be used when there are known difficulties and obstructions in the path from AP to clients, or if a very high design safety / fade margin is required for the application.
Note that setting the design margin higher will limit the predicted range of the access points. When designing for heavy use areas such as stadiums, this will increase AP density. A design margin above 15 is not recommended because this is beyond the ability of the Access Point to compensate by power reduction should the design margin prove too conservative after implementation. Up to 15 dB is within the typical range of capable AP power reduction via controller and ARM settings.

## Slide 24: Global Parameters
New Features:
  Separate Noise Floor by Band
  Separate Design Margins by Band and Client vs. Mesh
  Select a Default AP to show EIRP Limits
  Click on Bands to Show Band Details (channels)

## Slide 25: Define Client Models
Most accurate if actual client values are known
Program is accurate for client antenna gain up to 3 dBi
As the client antenna gain increases above 3 dBi, the radiation pattern becomes more directional, making the alignment of the client and it’s antenna more critical to the communication with the AP.
Notes: The coverage predicted is most accurate if the client power and gain is known. Typically client devices have a lower power and use a low gain antenna. If clients are unknown or general, the “laptop” client model is a generic one that can be used for most planning situations.
The present coverage graphical representations are accurate for client gains up to approximately 3 dBi. If a client employs a higher gain antenna system, care has to be taken to ensure the client antenna pattern is aligned with the access point antenna pattern. Therefore it is not recommended to use a gain value higher than 3 dBi in the client model unless the client will be aimed and fixed during installation or the user is knowledgeable about how to aim/align the client device antenna.

## Slide 26: Define Locations
Minimal changes should be made to prevent large errors in AP placement
Notes: The locations are loaded and grouped according to your “Locations” folder in the uploaded KMZ file. Locations can be edited if needed on this page, but it is recommended that if extensive adding or editing is needed that this be done in Google Earth and the file re-uploaded. This is because minor errors in lat/lon typing (depending on where in the decimal place) can result in large errors in placement. Typically editing of location information on this screen should be limited to correcting locations to GPS actual readings from on-site or fixing altitude setting errors from the uploaded file. (i.e. neglecting to set altitude is the most common error and can be fixed here).

## Slide 27: Default AP and Antenna Settings
Initially sets all APs and Antennas to these settings
Individual settings can be changed
Available band and mode assignments based on AP type
Channels can be assigned for planning purposes.
Antenna selection based on band selection.
Notes: Set Default AP Model
This will set all APs for this project to the same model. This feature is only for time savings on entry, you can make changes to individual AP selections if desired below.
Set Default Antenna Model
This will set all antennas for this project to the models selected. Again, this just initializes all antennas, individual antennas may be changed later if selected below.

## Slide 28: Group Client Services
Defines setting for all APs in the group
Set Min and Max data rates
Data rates apply to both client and mesh
Mesh band (802.11a or 802.11bg) only affects Mesh Portals and Mesh Points
Mesh Nodes cannot provide client access and mesh communications on the same band
Notes: Group Client Services
Set the Min and Max desired data rates, group client model and specify which radio will be used for Mesh (if applicable)
Revision Note (2.1): This setting presently applies to both client and mesh min and max rates so ensure the settings you choose covers both. If extra models are included that are not desired you can delete them later.
Note that the mesh band selected (802.11A or 802.11BG) will only affect those APs with a mesh role defined (Point or Portal) and other APs at other locations in the group can still be used in that band to provide client coverage.
Revision Note (2.1): At this time, no Aruba AP’s allow simultaneous Mesh and Client access on the same band. So, if you have a location you wish to provide simultaneous mesh and client coverage from the same location on the same band, you will need to have two locations defined (one for client access and one for mesh) in the initial KMZ that you upload.

## Slide 29: Access Point Settings
Name is optional
AP Model and Power Limit – Individual values can be set or modified from the default settings
Radio Role (Client Coverage, Mesh Point, or Mesh Portal)
Directional antenna settings
  Ant. Heading – 0 is North
  Ant. Downtilt – 0 is the Horizon, negative values indicate uptilt
  Addl. Cable Loss – Entered as a dB value
Notes: Name: This is optional. For each access point you may assign a unique name at this time if desired. Note that all AP’s will automatically get the location, antenna, and rate appended to their name in the model so it is not required to give a name in the name field.
AP Model and Power Limit: If not set by the default feature already, or if desired to change, assign an AP Model. The maximum power for individual APs may be reduced if desired.
TIP: You can also use increased design margin if you want to show coverage with reduced power. The difference is that design margin affects both AP and client predicted range, whereas the AP power setting reduces AP power only. If you choose to use the AP power limit feature you will have to reduce the AP power below the client power before you will see any reduction in the predicted coverage.
Radio Roles: Select “Client Coverage”, “Mesh Point”, or “Mesh Portal”. Note that the radio for Mesh Point or Mesh Portal needs to match the band specified in the Group Mesh settings.
TIP: For organization purposes it is recommended to put the portals at the top of each group, but this is not required. You will specify the mesh associations to model, including multihop associations on the next page.
Antenna Model, heading, downtilt and cable loss: Assign an Antenna Model. For directional antennas, the antenna heading can be assigned (0º is North in Google Earth) and any downtilt angle can also be set (0º is the horizon, 10º down from horizon, etc.). Note that Negative downtilt is uptilt and may be entered when appropriate. If an extension cable is used, enter an appropriate cable loss for the expected length of cable.
Tip: For client coverage, you will need to estimate the desired headings from your KMZ file, a spreadsheet is useful when creating your kmz to take down headings wherever you expect to use a sector antenna for client coverage. The utility performs no checks of headings entered for client coverage APs (you can put in anything, so plan ahead!)
Tip: For mesh with directional antennas, the utility will check all headings to ensure beamwidth alignment and will calculate all ideal headings. It is recommended to enter the best estimated heading because the utility will include this in the report once all mesh associations are aligned. If mis-aligned the utility will not let you proceed and you will be given the option to correct to the ideal headings or enter a different heading to correct the alignment.

## Slide 30
Additional Details Available per Radio
  Conducted Power Set
  Antenna Gain (Based on Antenna Model Selected)
  EIRP (Based on all selections)
  Max EIRP (based on Country/AP Model/Band Selected)
Access Points Page

## Slide 31: Mesh Association Page
Mesh Association Page will appear if any Mesh Nodes are defined
Checks that valid connection is possible
Mesh links will appear in the final KMZ file as lines colored according to the associated data rate
Links are checked for
    Valid signal strength at both ends
    Beamwidth alignment (horizontal and vertical)
      Based on headings, altitudes, and antennas selected
    Fresnel Zone and Earth Bulge
    Associated data rate is above minimum rate specified
  Does not check design logic
Notes: After submitting the AP definition page, if you have set any radios to a mesh role (i.e. mesh point or mesh portal) you will proceed to the Mesh Association Page. As an RF planning utility, the purpose of the mesh associations is to check that a valid connection is possible with the distances, antennas, and APs you have selected. If a connection is possible for the association you have selected, the mesh links defined on this page will appear in the final KMZ file as a line that is colored according to the associated data rate of the mesh link. This allows for simultaneous inspection of 3D client coverage and 2D representation of the associated backhaul/mesh.
Each mesh association you create on this page will be checked for the following:
Valid Signal Strengths at both ends of the mesh link
Beamwidth Alignment, both horizontal and vertical based on the headings, altitudes, and antennas selected
Fresnel zone and Earth Bulge for long distance links
Associated Data Rate for the mesh link is above the minimum rate specified
You may defined any associations you want to check and have appear in the final output.
Note: As this utility is primarily for RF planning checks, it does not inspect the logic of your chosen mesh associations. Be sure that the mesh associations you create represent the mesh network you wish to present and are complete / logical. Pre-planning which mesh points and associations are desired to show before starting this utility is recommended.

## Slide 32: New - Mesh Calculation Options
Manual or Automatically associate mesh nodes
Auto association is based on a signal level threshold
Planner will then calculate and display all available links on the same channel based on the threshold

## Slide 33: Mesh Association Page
Each Mesh Point must be linked to a Mesh Portal
For each group, Mesh Portals are listed on the left and all Mesh Nodes (Portals and Points) are listed on the right
Multi-hop nodes can be created by selecting the node on the right and clicking the “+Multi-hop” button.
The Multi-hop node will be added to the list on the left
All nodes are required to be used
All nodes are listed at the far right along with the node status
Nodes can be used more than once
Notes: For Each Group, the Portals are automatically listed on the left and all mesh nodes (Portals and Points) are listed on the right. To create an association, select a node on the right by highlighting it and click on the “Add” button on the left next to the node you wish to create the association.
Multi-hop nodes can be created for a group by selecting the multihop mesh point on the list at the right and clicking the “+Multihop” button. This will put the multihop node into the list at the left and associations for nodes from the right may now be created in the same manner as described above.
As each node is used, a check next to the node appears in the list at the right. Note that not all nodes are required to be used, and any node may be used more than once. However, for each node on the left at least one association must be provided or you should return to the previous page and change the mesh role to “client coverage”.

## Slide 34: Mesh Link Details
Displays the details of each Mesh Link as well any errors
Any errors will generate messages and suggestions to correct the problem
The utility will not let you proceed if you have link errors
Notes: The above checks are shown for each mesh associations. If there are any errors (such as alignment, range, etc.) you will receive error messages and suggestions to correct.
Once your mesh associations are error free, all mesh links you have proposed are checked through as valid and you can submit. The utility will not let you proceed without correcting mesh link errors to ensure that all links shown in the final output file have been validated.

## Slide 35: New – Mesh Display Options
Output Links can now be Colored by Channel or by Throughput
Colors are preset (5 colors) but can be assigned to user preferences
These values can be set by user
User Assigned

## Slide 36: New – Client Model Options
Client Coverage Models may now be generated based on
  Throughput (TCP, Mbps)
    similar to legacy planner rate based models but TCP throughput instead of MCS Rate 0-15
  Signal Levels set by user (e.g. -60 dBm, -65 dBm, etc.)
    “Basic Coverage” or VOIP application analysis
  Channels based on a signal level
    Useful for overlap or interference analysis

## Slide 37: Client Modeling – By Throughput Level
User can set desired Target Levels for each color

## Slide 38
User can set thresholds for each color and model at AP or at Client
Client Modeling – By Signal Level

## Slide 39: Client Modeling – By Channel
User assigns channels to colors and models will be created for signal level threshold at client (i.e. all same size based on signal level, different colors based on channel)

## Slide 40: Processing KMZ File
After submitting the file, a progress bar will indicate the current status

## Slide 41: Download the New File
When the processing has completed, a new KMZ file will be created with the additional information
Right click on the KMZ file and SAVE it to your local drive BEFORE opening it
Also download the input report
The input report includes
  All Inputs for the Model including
    Country
    Design Margin
    Location details (Lat/Lon/altitudes)
    APs and Antennas selected
    Antenna heading, mesh roles and cable loss
  Mesh Checks
  Bill of Materials (AP and antenna counts)
Notes: Note: Due to some potential pitfalls and errors that can occur when viewing and navigating a Google Earth file, it is strongly recommended to save the completed KMZ locally before opening it. This is explained more completely in Appendix A.
You are also given the option to download an input report. You should download and save this also as it provides the following information:
-All Inputs for the Model including
Country
Design Margin
Location details (Lat/Lon/altitudes)
APs and Antennas selected
Antenna heading, mesh roles and cable loss
-Mesh Checks
-Bill of Materials (AP and antenna counts)

## Slide 42: View your new .kmz file
Click on Link to show details (same as legacy)
Shows distance, upstream/downstream TCP estimates and Signal Level (dBm)
From Google Earth, open the new .kmz to view the plan
Complex plans can take several minutes to load

## Slide 43: Example Output
Client Coverage at -65 dBm, color by channel
Mesh Links color by channel (two groups)

## Slide 44: Example Output – View Elevation Profile
Elevation Profile View now Available for Mesh Links

## Slide 45: Example Output – Client Throughput
Colors of 3D Models Represent User Selected Throughput coverage areas (e.g. 60 Mbps, 30 Mbps, etc)

## Slide 46: Example Output – Coverage by Throughput
50 Mbps Model, 2.4 GHz HT20, ANT-2x2-D805

## Slide 47: Tips and Tricks

## Slide 48: Tips and Tricks
Follow the suggested folder structure
Break up large projects into multiple KMZ files
Keep backups
Remove empty folders
Delete unnecessary or uninteresting models
Turn off everything and save the file to speed up loading
An overlay with a scale line on it makes it easier to size/scale the overlay when it is inserted into Google Earth (you can use either a scale line or a section that is of a know length)
Notes: Follow the folder structure: Make sure you have a folder named “Locations” and it is at the top level in your kmz file. You can put subfolders under this folder and it will create groups for you.
Break up the project into multiple kmz files: It may be helpful to break the project up into groups of about 50 APs max. Files have been created with over 120 APs and there is no limit in the utility at this time so what you can manage will vary based on your skill level and system (video/processor).
Keep a Backup: Google Earth is prone to some strange crashes from time to time, particularly if the file is attempted to be saved but all models are not yet loaded. If this happens it can make your kmz unreadable on the next open. So, when you save the kmz file with models, make a backup copy before opening just in case this happens. This is a known issue with Google Earth that doesn’t have a fix for now. You can avoid this by waiting for all spinning icons in the tree at the left to stop spinning before you try to save the file again.
Empty folders: The utility creates some empty folders. Delete them if you don’t need them and resave your file.
Delete Uninteresting Models: Many times after building the model, not everything is interesting. You can delete whole folders of models such as low or high data rates that don’t show anything particularly interesting or individual models and re-save the KMZ. This will not affect you ability to reload the kmz later and restore variables. All “post entry” information that gets added to the kmz file has no effect on the ability to make changes and rerun the file later.
Turn off everything: Viewing large 3D model files can be a challenge for your laptop’s video system. It is generally helpful after the file loads to turn everything off, then inspect coverage by zooming in and turning on locations and data rates of interest one at a time. It is recommend after all models loaded (no more spinning icons) turn off the coverage folders completely and save the file. The next time it loads, the models will be off by default and it will load much faster. You can then turn things on as you want to see them.
Scaling the overlay: If the overlay has a scale on it, by preserving the scale on the overlay you can put down a ruler line in the Google Earth viewer prior to pulling in the drawing. Then when you go to scale you just have to match up the scale on the drawing with the ruler line that you have put down and the drawing is sized correctly. Then it just has to be oriented. If the overlay does not have a scale on it, add one to it if feasible.

## Slide 49: Lab

## Slide 50: Lab
Pre-requisites:
Prior to starting this lab, Google Earth must be installed on your computer. If you do not already have a copy of Google Earth installed, you can go to earth.google.com to purchase Google Earth Pro, Google Earth Plus, or to download a free version.
Remember, if you are using this planning tool for commercial purposes, you will need to purchase Google Earth Pro.
The lab is designed to give you some hands on experience with the Aruba Outdoor Coverage Planning Tool. You are encouraged to experiment and try different features of the product so that you may become more knowledgeable and proficient with the product.

## Slide 51: Lab
Project Requirements:
The customer in this scenario is Ohio State University Airport. The airport would like to provide a minimum of 2 Mb 802.11b coverage to the maintenance operations area of the airport. This area covers most of the paved area outside of the main hangars. The file osu-airport-outline.png shows the area that is to be covered along with some of the key buildings. All of the buildings and hangars to the left of the parking area have Ethernet connections to the airport network that can be used to connect the access points. The maintenance hangars to the right of the parking area do not have Ethernet in them.
Access points attached to these buildings will need to be connected using mesh connections.
Access points and antennas can be mounted to the outside of any of the buildings. All of the buildings are 30 feet tall. If needed, you can install at most a 6 foot mast on the corner of any building. Wireless coverage inside the buildings will be addressed in a future project.

## Slide 52: Steps
1. Locate the property in Google Earth
  Once the property is in view, create the following folders in the left-hand pane by clicking on “My Places” and then Add-Folder (or right-click, Add-Folder)
    <OSU-Airport>
      <Locations>
      <Non-Mesh APs>
      <Mesh APs>
      <Map Images/Overlays>
2. Import an overlay image if desired
  The next step is to insert an overlay image if you have one. This will help you to better understand and interpret the place of the access points.
  Select Add-Image Overlay.

## Slide 53: Steps
2. Import an overlay image if desired
  The next step is to insert an overlay image if you have one. This will help you to better understand and interpret the place of the access points.
  Select Add-Image Overlay.
  Name the image OSU-Airport-Buildings
  Browse to the file osu-airport-outline.png but do not yet click on the OK button (your instructor will provide this file)
  After you have browsed to the file and selected it, you should see it in displayed on Google Earth. You now need to slide the transparency button to the middle to the point where you can see the building overlay, but still see the airport.
  Now grab the “Google Earth – Edit Image Overlay” window and move it to the side so that you can see the overlay on the map.
  The overlay should have green corners and hash marks. You can click and drag on the middle crosshairs to move the overlay. While holding the “Shift” key, you can click on the corner and uniformly scale the image. You do not need to be exact since the overlay is only there to assist you and it has no bearing on the RF plan.
  After you have resized the overlay, move the “Google Earth – Edit Image Overlay” window back to the middle of your screen and click on OK.
  Make sure that your image overlay is in the “Map Images/Overlays” folder.

## Slide 54: Steps
3.Add Location Placemarks
  Select the “Non-Mesh APs” folder by clicking on it.
  Select Add-Placemark
  Name the placemark with a unique name. A name describing its location can be useful, such as “AP – Hangar 4 – West Corner”
  Select the Altitude tab and set the height that you will be mounting the AP. Also click on the “Extend to ground” button.
  Now go to the map and move the placemark to the location where you intend to install the access point.
  Now click on the OK button to accept this placemark.
  Repeat this step, adding additional mesh and non-mesh placemarks on the map.
4. Save the Initial KMZ File
  After you have created the proper folders, placed the overlay file on the map, and created the placemarks, it is now time to save the file as a KMZ.
  Select the OSU-Airport folder
  Right-click on this folder and select “Save Place As”
  Name the file OSU-Airport and save it.
  Confirm that you have saved the file (you can confirm this by selecting File-Open and seeing if the file you just created is there)
  The reason why you just confirmed that the file was save is because you are now going to delete the project folder from “My Places” to prevent two copies from showing up later.
  Select the OSU-Airport folder by clicking on it. Right-click and select delete. Now confirm that you want to delete the folder and it’s descendants by clicking on OK.

## Slide 55: Steps
5.Login to the Outdoor Coverage Planning Tool
  Open a browser and go to https://outdoorplanner.arubanetworks.com
  Login. Register if needed.
6. Upload the Initial KMZ file
  Browse to locate the file that you just created (OSU-Airport.KMZ)
  Click Continue to upload the file into the Outdoor Coverage Planning Tool
7. Define Global Parameters
  Select the country that you are designing the network for, in this case it is USA
  Set the Noise Floor and Design Margin values.
    The Noise floor should be set to -85 dBm
    The Design Margin should be a value between 3 dB and 15 dB

## Slide 56: Steps
8. Define Client Models
  Set the maximum transmitting power level for the laptop or portable devices
  Also select the antenna gain for these devices
  The default settings are typical values and can typically be left unchanged.
9. Modify Access Point Locations
  We do not suggest making changes to the Latitude or Longitude field unless you have updated coordinates from Google Earth or actual coordinates from a GPS
  Check the Names and Altitude of each of the APs to see if you need to make any corrections
  In the bottom left corner, click on the SAVE button
  After the changes have been saved, in the bottom right corner, click on the SUBMIT button
10. Groups and Access Points – Setting default values
  At the top of the Groups and Access Points screen is a section where you can set the default values for:
    AP Model
    Group Client Model
    AP Power
    802.11bg and 802.11a Antenna Models
  Choose the settings that you want to use by default for each of the access points. You will be able to change these values for each individual access point.

## Slide 57: Steps
11. Groups and Access Points – Setting individual values
  The groups and placemarks that you created in Google Earth are listed below the default values section
  In each of the Group Name sections, you need to set the coverage, client, and mesh values for that group of APs
  Then below the Group Name box you will need to set the values for each access point.
    Radio Role – If the access point is acting as a mesh point or a mesh portal, you need to set this value
    If you are installing directional antennas, you need to determine and set the values for the Antenna Model, Heading, Downtilt, and cable loss.
  Remember that these settings need to be carefully planned and configured for every access point that you entered a placemark for.
  After you have made all the necessary changes to each of the access points, click on the SAVE button and then click on the SUBMIT button
12. Defining Mesh Links
  If you defined multiple mesh groups, you will now need to specify which mesh points are associated with which mesh portals.
  In the All Mesh Nodes area on the right, select the mesh points and click on the Add button to add them to a mesh portal
  After you have defined the mesh links, click on the SAVE button and then click on the SUBMIT button

## Slide 58: Steps
13. Mesh Link Details
  The Mesh Link Details window will display the details of the mesh links along with any errors that might exist.
  Carefully examine each of the General Details windows which display the detailed information for each mesh portal and mesh point connection
  If you have any errors, the Outdoor Coverage Planning Tool will not let you continue until you correct your errors.
  Assuming that your design is correct, click on the SUBMIT button
  After you submit the plan, the program will display a progress bar and will indicate when the process is complete.
14. Downloading the new KMZ file
  After the processing has completed, a new KMZ file has been created with the additional information that you added.
  Click on the KMZ icon and save it to your disk
  Right click on the PDF icon and select “Save Target As…” to save the file to your disk. It is useful to keep a copy of the PDF file. It is a summary of the settings, which can be used to review what you did or recreate your work if the KMZ file is deleted or corrupted.
15. View Your New KMZ File
  Now you can go back into Google Earth and view both the wireless links and coverage
  Open Google Earth and open the new KMZ file (depending upon the complexity of the plan, this can take several minutes)
  In Google Earth you will see your plan.
  After the models have been loaded you will see additional folders containing coverage information for 802.11a and 802.11bg
  You will also see a folder representing the mesh links.
  Turn off all of the folder views and then selectively turn them back on so that you can see the different coverage.
  Experiment with the different views. Feel free to go back into the Outdoor Coverage Planning Tool and make design changes. Process the file again, and see how the changes affected the outcome.

## Slide 59: Overlay

## Slide 60
Thank You!