## Slide 1: Roaming Behavior and Client Troubleshooting June 2017
Presented by Andrew Hejnar
Distinguished Engineer
Aruba Customer Engineering
ajh@hpe.com
972-899-2670

## Slide 2: Agenda
Very Quick 802.11 Wireless Networking Refresher
Access Point Planning and Placement
Adaptive Radio Management and Airmatch
Client Roaming
Client Match
Client Troubleshooting (controller-centric)
  There are a lot of slides in this presentation and we are NOT going to cover each in detail. They are there for later reference
This session will be focused on what you need to do your jobs on a daily basis as a wireless network designer, engineer and/or administrator

## Slide 3: 802.11 Wireless Communications Refresher

## Slide 4: 802.11 Wireless Networking Refresher
  Things you probably already know …..and some you don’t
  Thank you Captain Obvious!

## Slide 5: 802.11 Wireless Networking Refresher
Channel 1
  Wireless Networks allow one device to communicate at a time per channel
  Each Wi-Fi channel is in effect a hub that is in the air
Notes:   Only the person with the ball can talk
  When they are done talking everyone else can fight for the ball

## Slide 6
The same channel being re-used in close proximity negates the benefit of the
additional access point (same contention domain/co-channel interference)
Channel 1
Channel 1
Will you guys keep it down???
Blah, Blah, Blah, Blah, Blah, Blah
Meeting 1
Meeting 2
802.11 Wireless Networking Refresher
Notes: If we add another table but are still speaking on the same channel in close proximity, we’ve bought no additional capacity.
The cross talk between the two tables causes things to be repeated, or in the wireless world re-transmitted.
Another bad thing is that meeting 2 can’t hear what exactly is being said in meeting 1 so it can’t pick a good time to interrupt
The louder the speaker’s voice (transmit power) the worse this problem can be
In other words, too many wireless access points can be as bad as too few access points

## Slide 7: 802.11 Wireless Networking Refresher
The solution is to use another channel so that the
communications don’t overlap each other
Channel 1
Channel 6
Blah, Blah, Blah, Blah,
Blah, Blah
Blah, Blah, Blah, Blah, Blah, Blah
Meeting 1
Meeting 2
Notes: Using another channel creates a completely new collision domain and now each meeting can take place without interfering with the other.

## Slide 8: 802.11 Wireless Networking Refresher
Wireless is 3 Dimensional
  Common sense but easy to forget
  The louder the meetings are (transmit power), the worse this gets
Channel 11
Channel 1
Will you keep it down???
Blah, Blah, Blah, Blah
Meeting 3
Meeting 4
2nd Floor
1st Floor
Channel 1
Channel 6
Blah, Blah, Blah, Blah
Blah, Blah, Blah, Blah
Meeting 1
Meeting 2
Interference
Interference
Notes: Try not to stack AP’s on top of each other floor to floor.

## Slide 9: 802.11 Wireless Networking Refresher
There are a finite amount of available channels to communicate on
(US regulatory Domain)
  2.4 GHz – “B/G Band” – 3 Channels
Notes:   Only 3 non-overlapping channels that can be used
  Older technology
  Limited number of channels means more channel overlap and potential same channel interference when in close proximity. This is known as Co-Channel Interference and is another reason that too much access point power is a bad idea
  Travels further than 5 GHz – A because of longer frequency
  Much more co-channel interference because there are only 2 collision domains to work with.

## Slide 10: 802.11 Wireless Networking Refresher
There are a finite number of available channels to communicate on
(US regulatory Domain)
5 GHz Channel Bonding
    Bonding channels means higher throughput but less available channels and thus more co-channel Interference because of channel overlap
  20 MHz Channels
    9 - Non-DFS
    16 - DFS
  40 MHz Channels (802.11n)
    4 - Non-DFS
    8 – DFS
  80 MHz Channels (802.11ac)
    2 - Non-DFS
    4 – DFS
  160 MHz Channels (802.11ac)
    1 - Non-DFS
    1 – DFS
    Remember that the 80/160MHz
    Channel usage is dynamic as opposed to
    40MHz channels which are static

## Slide 11: 802.11 Wireless Networking Refresher
5 GHz Channels – Things you should know and remember
  Channel 144 was added as part of the 802.11ac amendment but some clients may not support it.
  Channels 120-128 were not allowed to be used until very recently by the FCC but are still not sanctioned by the ETSI. Clients may not support them.

## Slide 12: 802.11 Wireless Networking Refresher
5 GHz Channels – Things you should know and remember
  It is a higher frequency so it only travels about 60% of the distance that 2.4 GHz does
  This equates to approximately a 6dB power difference for the client to see the signals at relatively equal power’
  If the 2.4GHz signal is significantly higher the client may connect to it first and have to be band-steered to 5GHz
2.4 GHz @ 12dBm
5 GHz @ 18dBm
-65dBm
-65dBm

## Slide 13: 802.11 Wireless Networking Refresher
5 GHz Channels – Things you should know and remember
  Devices sends probe requests only after seeing access points sending beacons on DFS channels
36 40 44 48 149 153 157 161 165
802.11 Probe Requests
Beacons from access points on DFS Channels
52
56
60
64
100
104
108
112
Notes:   Devices take longer to roam to DFS channels since they only use beacons to look for DFS channel versus sending probe requests for standard channels.

## Slide 14: 802.11 Wireless Networking Refresher
Should I use DFS Channels?
  Are they really needed?
    What are the expectations of throughput?
    Are you planning on using 80MHz channels? Do you really need to?
    If the environment is very dense access point wise, can you just use 20 or 40MHz channels?
    How much attenuation do you have between your APs?
  Do all your devices scan the DFS channels?
  Is the 2.4 GHz spectrum clean enough to support 2.4 GHz fallback for clients that don’t?
  Are you using VoIP and is seamless voice handover as clients roam important?
  What is your tolerance for user complaints and troubleshooting?
  Are you close to an airport?
    Depending on the age of the radar you may get radar detections
      AP must change channel
      If no channel is available then go completely silent on 802.11a in APM mode (monitor)
      B/G will continue to operate normally

## Slide 15: VHT20 Beats VHT40 & VHT80 – 2SS Clients
Chart: Clients
| 5 | 10 | 25 | 50 | 75 | 100
VHT20x4 Up | 557.4452 | 555.7513 | 531.1113 | 523.8234 | 489.7477 | 424.114
VHT20x4 Bidirect | 582.1827 | 576.9935 | 555.5865 | 526.6692 | 489.5024 | 461.0308
VHT40x2 Up | 636.0733 | 622.9533 | 579.3976 | 498.0701 | 466.9353 | 399.0022
VHT40x2 Bidirect | 638.6457 | 587.7706 | 591.9577 | 524.3945 | 486.3872 | 475.5222
VHT80x1 Up | 625.8425 | 618.8909 | 552.5237 | 463.7228 | 335.6741 | 241.8086
VHT80x1 Bidirect | 627.0898 | 594.1712 | 517.323 | 436.8671 | 397.6524 | 239.8219
Down
Up
Bidirect
802.11 Wireless Networking Refresher
Notes:   At the point were there are more than 25 devices per channel it starts to make more sense to user narrower channels
  More collision domains with fewer users per domain means better performance after this threshold is reached.

## Slide 16: 802.11 Wireless Networking Refresher
What channel width should I be using?
  If you are NOT using DFS channels
    80 MHz
      2 channels
      In a 2 AP deployment which really means never
      Too much CCI if there are more than 2 APs
    40 MHz
      4 channels
      Close office space or cubicles with outer offices ringing
      No more than 4 AP’s with line of sight between each other
    20 MHz
      9 channels (some older devices don’t see channel 165)
      Wide open office space with dense AP deployment
      More than 4 AP’s that have line of sight to each other
      Dense cubicles
      Device density with each user having at least 2 devices (laptop, smartphone, tablet, VoIP phone)

## Slide 17: 802.11 Wireless Networking Refresher
What channel width should I be using?
  If you ARE using DFS channels
    80 MHz
      5 channels but some of your devices may not support 3 of them
      Less than 25-30 users per channel
      High AP density to support SNR’s higher than 35 (support the highest 802.11ac data rates)
      Requires close monitoring of your user community for the first month to identify potential issues
      Be prepared to drop back to 40 MHz channels
    40 MHz
      10 channels
      Any deployment where 80MHz channels are problematic because of more than 4 AP’s with line of sight to each other or because of client side support issues
    20 MHz
      22 channels
      Large Public Venues

## Slide 18: 802.11 Wireless Networking Refresher
Transmit Power – Rule of 10’s and 3’s
For every 10dB of gain multiply the power by 10
For every 10dB of loss divide the power by 10
For every 3dB of gain multiply the power by 2
For every 3dB of loss divide the power by 2
  3dBm ----- 2mW
  6dBm ----- 4mW
  9dBm ----- 8mW
  12dBm ----- 16mW
  15dBm ----- 31mW
  18dBm ----- 63mW
  21dBm ----- 125mW
  22dBm ----- 158mW
  22.5dBm -- 177mW
  23dBm ----- 200mW

## Slide 19: 802.11 Wireless Networking Refresher
802.11 is Equivalent to Using Very Sophisticated Walkie-Talkies
Who’s more important here ?
Neither
They are both critical to effective wireless communications
DRIVERS MATTER!!!

## Slide 20: 802.11 Wireless Networking Refresher
You haven’t taken your car to get the oil changed since 2012 and can’t figure out why your engine is smoking?!?!
Client Drivers
  So you just went out and spent $$$ upgrading the wireless network and you are still getting user complaints and you’ve checked everything! ….oh wait a minute, these are walkie talkies right?

## Slide 21: 802.11 Wireless Networking Refresher
  Her being married to him
Having a Brand New/Upgraded Wireless Network with Old Client Drivers is like….

## Slide 22: 802.11 Wireless Networking Refresher
  Remember that wireless devices are like using two way radios
    There is the signal from the AP to the device
    There is the signal from the device to the AP
    The smaller the device, typically the lower the transmit power and the weaker the signal is to the AP
      Laptop – 30 milliwatts
      Old IPad – 12 milliwatts
      Newer Ipad – 50 milliwatts
      Android device 10-13 milliwatts
      Vocera B3000 – 39 milliwatts
      Motorola Handhelds – 12 to 30 milliwatts
    AP’s can transmit at very high power relative to the clients
      Up to 200 milliwatts (and up for outdoor)
  Power Levels
    Usually an absolute measurement
    Anything higher than -65dBm is considered an excellent signal
    Anything higher than -50 to -55dBM would be consider too much signal which can issues by being too “loud” and causing issues with co-channel and adjacent channel interference
    Analogy: It’s best to have both parties speaking in a normal voice versus screaming or whispering

## Slide 23: 802.11 Wireless Networking Refresher
Transmit Power
Using high transmit power on access points doesn’t create significantly increased usable coverage because of the two way nature of communications
Notes:   Just because one party can hear the other doesn’t mean the that the other party can hear the return signal

## Slide 24: 802.11 Wireless Networking Refresher
  Signal to Noise Ratio
  The gap between the received signal and ambient noise floor
Notes:   Relative measurement of the signal to the “noise floor” of the environment
  The “noise floor” is the environmental or ambient noise in the 2.5GHz or 5GHz frequency
  Analogies:
  Library – you can whisper since there is no noise at all
  Office – you have to speak in a normal voice to be heard over the background noise
  Concert – you have to shout to be heard
  Remember that the 2.4 GHz and 5 GHz are unlicensed so any device can use them, adding to the noise floor and/or causing interference
  This noise floor is usually between -85 and -100 dB with 5GHz almost always having a lower noise floor
  The higher the noise floor, the stronger your signal needs to be and the more APs you need
  So if you have a -65 dBm signal at your device and the noise floor is -95dBm then you have a 30 signal to noise ratio which is excellent
  A minimum SNR of 25 will support the highest data rates between a 802.11n client and AP
  A minimum SNR of 35 will support the highest data rates between a 802.11ac client and AP
  Any SNR below that and the client or access point will slowly start to down rate to a lower megabits per second data rate
  This happens rapidly and signal to noise ratios below 20 are practically unusable

## Slide 25: 802.11 Wireless Networking Refresher
  Signal to Noise Ratio
  The lower the signal to noise ratio, the more the device is susceptible to interference
  Remember the two way nature of communications
    AP’s usually transmit at a higher power level than the client(s)
    AP’s are better listeners than clients (what we call receive sensitivity)
      Think of the AP as a dog and a client device as a human
      Some devices have better antennas (ears) than others so they can hear better
    The client may be transmitting at 30 milliwatts and the AP at 60 milliwatts so the signal to noise ratios will be different downstream versus upstream
      The worse this power imbalance the worse the upstream signal to noise ratio, the lower the upstream data rate and the more susceptible the upstream is to interference
      Therefore, the client signal to noise ratio (from client to AP) that the access point sees is almost always the limiting factor as it relates to performance
    Signal to noise ratios below 20 are practically un-useable because of client performance expectations and this is about the point you want your devices to roam to a better AP

## Slide 26: 802.11 Wireless Networking Refresher
  Signal to Noise Ratio Ultimately Determines Downstream and Upstream Data Rates
95db Noise Floor
95 NF Less 65 RSSI = 30 SNR From AP to Client
95 NF Less 77 RSSI = 18 SNR From Client to AP
Extremely BAD Data Rate
Very GOOD Date Rate
Other than the retransmissions and low data rate He has no idea that he’s in a world of hurt here!!!
AP Power
To High
Notes:   There are two data rates
  From the AP to the client
  From the client to the AP
  High access point power >18dBm almost ALWAYS leads to a link imbalance and thus a poor upsteam data rate.
  The client has not idea about this, all it sees is a strong Wi-Fi signal

## Slide 27: 802.11 Wireless Networking Refresher
Down-rating
Notes:   If the client or access point can’t successfully transmit to the other party they “down rate” and try using a slower mbps data rate. This can go down as low as 1, 2 or 5mbps which really means that the signal is all but unusable and will cause major customer satisfaction issues with the network
  Remember that those data rates are really half of the actual rate since wirelss is half duplex
  Once again, bringing the power levels more in balance with each other will sustain higher data rates and make happier users

## Slide 28: 802.11 Wireless Networking Refresher
Down Rating Affects Faster Users on that Channel
Notes:   Remember that each channel is in effect, a hub, and thus a very finite resource.
  It takes much, much longer (airtime) to transmit a frame at 11mbps than it does at 54mbps or even longer relative to a 300mbps data rate
  Having clients connected at lower data rates slows everyone down on that AP since they have to wait for those slow clients to get on and off the channel

## Slide 29: 802.11 Wireless Networking Refresher
Trimming Data Rates
  Why Trim the Lower Rates?
    If the client can’t down rate any further, it must roam
    Has a similar effect to lowering the power in that it effectively shrinks the cell size of each AP
    Get the slower users off the AP to let the faster users better utilize the channel/AP
  Once the user down rates to a value lower 11 or so the connection is almost unusable so it makes sense, especially in typical office environments
  The denser the AP deployment, the more trimming the rates helps
  There are certain older devices that must see the lower data rates in order to connect
  If the customer is using newer devices then it makes sense
    What devices need to see the low data rates for connectivity?
      Older gaming systems
      Older handheld scanners but this is fine since low data rates really don’t affect these devices negatively since they mostly use terminal applications.
      Old VoIP Phones
      Certain medical devices/monitors

## Slide 30: 802.11 Wireless Networking Refresher
Trimming Data Rates
  How much should I trim?
    Typically up to 11mbps and 12mbps respectively but can go as high as 18 or 24 with some experimentation, depending on the client devices
    Certain Android devices need to see the 11mbps data rate
  wlan ssid-profile “Test-GUEST-ssid_prof"
  a-basic-rates 12 18 24
  a-tx-rates 12 18 24 36 48 54
  g-basic-rates 11
  g-tx-rates 11 12 18 24 36 48 54
  g-beacon-rate 18
  a-beacon-rate 18
  Don’t trim data rates in University, Medical Environments or any other connectivity critical environments without careful testing and monitoring

## Slide 31: 802.11 Wireless Networking Refresher
Key Takeaways
  Each Wireless Channel is a contention domain
  A smaller number of wider channels may provide worse throughput than a larger number of narrower channels
  High access point power is not going to solve any issues (max 18dBm) and will actually create more
  More access points is not necessarily the answer
  Consider the clients and access point density when deciding whether or not to use the DFS channels
  There are two data rates, one from the AP to the client and the other from the client to the AP
  Clients and their drivers matter (walkie-talkies)
  Low speed clients slow everyone down on that channel within earshot

## Slide 32: Access Point Planning and Placement

## Slide 33: Influencing Proper Client Roaming with AP Placement
  AP Placement is the single most important predictor of user satisfaction
  AND…..
You Have One Chance to Get It Right!!!
Notes:   AP Placement is the single most important predictor of user satisfaction!!!
  ARM and Airmatch are very effective but it can’t defy the laws of physics and make up for poor AP placements
  Cabling is a very large expense when deploying network devices.
  Make poor AP placement decisions and you are going to live with them for a long time.
  Too many AP’s for the building/users and you are going to be locked into 20 MHz channels if you can’t use the DFS channels
  Too Few AP’s and you are going to create bad coverage areas
  ARM is going to want to put the AP power too high creating near/far issues
  Client match will help with the near/far issues but it takes time to steer clients (typically about 60 seconds once stationary)
  Badly placed AP’s are almost as bad as putting too many AP’s and to few AP’s
  Avoid AP’s having Line of Sight to each other if you can avoid It
  In dense deployments you can’t avoid this most of the time but the fewer AP’s that have LOS to each other, the better.
  Think about the number of channels in each band and how much overlap you have in dense areas
  A few feet can make a big difference in signal quality and the way that ARM reacts
  Don’t stack AP’s on top of each other floor to floor

## Slide 34: Access Point Planning and Placement
Stacking AP’s Floor to Floor Usually Causes Major Issues
  Remember if the client sees AP power within 10-12dB of each other is will randomly select an AP to connect to and it might be the AP on the floor above or below
Since the AP’s are stacked on top of each other there isn’t enough signal strength differentiation so that the client knows which AP to connect to. Sometimes they connect to the AP directly above them and other times they connect to the AP below them. When the client connects to the AP below them the upstream SNR is not that good and they get a lot of re-tranmissions and a lower upstream data rate from the client

## Slide 35: Access Point Planning and Placement
Having a too many AP’s with line of sight to each may cause issues as well
  Remember if the client sees AP power within 10-12dB of each other is will randomly select an AP to connect to
This client can hear 4 AP’s all within a small margin of signal strength so it just randomly selects one.
In addition, the AP can hear 4 other AP’s on the same floor. Remember that there are only 3 available b/g channels so you will have 2 overlapping channels between these 5 AP’s, effectively hobbling the effectiveness of those channels unless you can lower the power of the AP’s to make them “speak at a lower volume”.

## Slide 36: Access Point Planning and Placement
You can’t lower power too much if you only have AP’s in hallways
  Lower the power too much and it will not be enough to reach users in rooms where the signal has to go through walls
  Raise the power enough to penetrate the walls and you have out of control co-channel interference
Now the client can only hear two AP’s and both are equally okay to connect, providing a good user experience.
However, the client in the room can hear an AP but the signal is not high enough to provide a good signal to noise ratio. In addition, because of the client’s position in the room it must penetrate two walls further deteriorating the signal.

## Slide 37: Access Point Planning and Placement
AP’s with line of sight and stacked on top of each other leads to an extremely poor
client experience (aka, the perfect storm)
Stack the AP’s floor to floor and now you’ve just compounded your issues by a factor of X with the power where it needs to be to reach the users in the rooms. The client will randomly select one of the APs to connect to because the power levels are all very similar. If they pick the wrong one, they going to get a very poor user experience. Now the retries may be so high that the client decides it needs to move to a different AP but it may again pick another one that is far away or through the floor.

## Slide 38: Access Point Planning and Placement
With a proper design you can lower the AP power to a point where the clients are
encouraged to connect to the correct AP
  Now the client only will see AP’s that it should connect to at strong signal levels
Put the AP’s in rooms and stagger them floor to floor. This allows you to lower the power enough to where the users will not see the AP’s on the floor above or below at a good enough signal strength to try and connect to. This also improves roaming performance as users don’t select bad roaming candidates to move to while in motion.

## Slide 39: Access Point Planning and Placement
  AP Density
    How many AP’s does it take to cover typical areas without taking user density into account ?
      The higher the downtilt AP is mounted (105, 135, 225) the larger the cone of coverage
      If mounting a true omni (no downtilt) don’t mount too high
      Warehouse (terminal applications and no VoIP)
        1 AP every 7500 to 10,000 sq feet with 50% overlap so an AP every 85 to 100 feet
      Retail (open floors, eg. Grocery Store)
        1 AP every 5000 to 7500 sq feet with 50% overlap so an AP every 70-85 feet
      Open Office Space (open floor/cubes with offices around periphery)
        1 AP every 2500 to 3600 sq feet with 50% overlap so an AP 50-60 feet
      Closed Office Space
        Needs to be walked, depends on construction materials
    Why is more AP density needed
      User Density
      Device Density/Devices per use
      All Wireless Offices

## Slide 40: Access Point Planning and Placement
  AP Density
    What is a dense deployment?
      The most dense deployments are an AP every 1500-1600 sq feet so the AP’s are anywhere between 35-40 feet apart
      This is extreme and you must use 20 MHz channels in the A band to avoid too much CCI if you can’t use the DFS channels
      If you are deploying 802.11ac and you want to use 40 MHz or 80MHz channels you MUST use the DFS channels in dense deployments

## Slide 41: Adaptive Radio Management and Airmatch

## Slide 42: Adaptive Radio Management (ARM)
An Aruba Feature That Automatically Adjusts AP Channels and Power Levels
Each access point listens and builds a view of the RF environment as it see’s it
Each access point makes channel and power decisions completely independently
Notes:   ARM calculations are done by each access point independently
  ARM power increases or decreases in 3dB increments

## Slide 43: Adaptive Radio Management (ARM)
An Aruba Feature That Automatically Adjusts AP Channels and Power Levels
The Aruba ARM technology uses a distributed channel reuse management algorithm where each AP makes decisions independently by sensing its environment and optimizing its local situation. The algorithm is designed so that this iterative process converges quickly on the optimum channel
  ARM uses a distributed channel reuse management algorithm where each AP makes decisions independently by sensing its environment and optimizing its local situation. The algorithm is designed so that this iterative process converges quickly on the optimum channel (client aware is enabled by default)
  So…if the AP doesn’t see any other AP’s on channel 40 it will use channel 40 and set it’s power to the highest value allowed by the ARM profile assigned.
  Remember that high default power can be as high as 200mW creating poor client roaming behavior and as a consequence near/far issues
  Using our channel 40 example, If it sees other AP’s on channel 40 that it’s selected because it deems it to be the least interfering channel, it will balance it power with the other AP on that channel BUT you may end up with one AP at a very high power and the other at a very low power. This is especially true if the neighboring AP sees another AP on channel 40 but the AP that is coming up can’t hear the 3rd AP
  Bottom line, ARM is a great tool but bases it decisions on what each AP sees as neighbors, its not perfect!
  ……….But, you can make it operate better!
  What happens to the channels when you first start up a new system or assign a new ARM profile?
Notes:   This can lead to unintended consequences and may cause a ripple effect
  A couple examples-
    AP-X comes up on channel 165 and sees no other AP’s on that channel so it goes to the maximum power allowed in the ARM profile
    The interference index threshold is reached for AP-X so it changes channels but this channel can now be heard by another AP on the same channel so it thinks it needs to power down

## Slide 44: Adaptive Radio Management (ARM)
Tuning ARM Profiles
  Recommendations on ARM Power Level Starting Points Prior to Testing/Tuning
    B/G – 2.4 GHz
      AP’s 50-55 feet apart/open air - 12dBm to 12dBm
      AP’s closer than 50 feet apart/open air - 6dBm/9dBm
      AP’s closer than 43 feet apart/open air - 3dBm/6dBm
      Chances are that most are going to be at 9dBm (fewer channels/more APs on an individual channel)
      If most of the AP’s go to minimum power after they settle then you might want to lower the values each by 3dBm, especially in denser environments
    A – 5 GHz
      AP’s 50-55 feet apart/open air - 18dBm to 18dBm
      AP’s closer than 50 feet apart/open air 12dBm/12dBm
      AP’s closer than 43 feet apart/open air 9dBm/9dBm
      You want the 5 GHz power 6dB higher than 2.4 GHz to make it more attractive for clients to initially connect to

## Slide 45: Adaptive Radio Management (ARM)
Getting ARM to Settle Quicker
  Arm will not change channels when a client is connected to an AP (client aware, enabled by default)
  When initially deploying an Aruba wireless network it’s a good idea to adjust ARM so that it will settle quicker, otherwise it may take 24 to 48 hours to fully settle, depending on client density
  Using these ARM settings will get it to settle within 2 hours
    Aggressive Settings
    rf arm-profile "default“
      scan-interval 1
      no client-aware
      ideal-coverage-index 5
      acceptable-coverage-index 2
      backoff-time 120
      min-scan-time 2
    Default Settings (don’t forget to revert back to defaults after 2 hours)
    rf arm-profile "default“
      scan-interval 10
      client-aware
      ideal-coverage-index 10
      acceptable-coverage-index 4
      backoff-time 240
      min-scan-time 8

## Slide 46: Airmatch
A Next Generation Aruba Feature That Automatically Adjusts AP Channels, Power Levels and Channels Widths
Replaces ARM in 8.0 and future builds
Each access point listens and reports all channels and the corresponding RSSI’s to the controller
The controller takes this information and builds a plan that is deployed every 24 hours or on demand by the administrator
It works really, really well with almost no tuning
  ARM works well too but requires a lot more tuning
30 Minutes
30 Minutes
30 Minutes
30 Minutes
30 Minutes
24 Hours
24 Hours
24 Hours
24 Hours
24 Hours
Notes:   Power is set in 1dB increments
  Airmatch will almost never set power higher than 18dBm and will almost always maintain a 6dB gap between 5GHz and 2.4GHz

## Slide 47: Airmatch
Next Generation Radio Management Tips and Tricks
With ARM best practice was to disable 80MHz channels in the ARM profile(s)
but with Airmatch this should be done in the wlan ht-ssid profiles
If required, maximum and minimum power levels should be set in the radio profiles NOT in the ARM profiles
Note that the defaults work great and should only be adjusted in special circumstances
Any ARM or radio profile changes require you to run Airmatch manually (or wait for the 24 hour automated run) for the changes to take effect

## Slide 48: Client Roaming

## Slide 49: Client Roaming
Clients are the ultimate decision maker of the best access point to initially connect to, as well as move to, when in motion

## Slide 50: Client Roaming – Properly Designed and Tuned Network
A
Good signal!
Time / distance
Signal Strength

## Slide 51: Client Roaming – Properly Designed and Tuned Network
A
Good signal!
Device starts to move
Time / distance
Signal Strength

## Slide 52: Client Roaming – Properly Designed and Tuned Network
A
Good signal!
Device starts to move
Time / distance
Signal Strength
Probe Threshold Reached
Device Sends out Probe Requests
Notes: Client reaches a vendor specific, secret sauce, signal level and starts to probe to see where he’s going to go next. For this example let’s assume this is -72dBm.
If it supports DFS it will also start to scan the DFS channels it supports for beacons

## Slide 53: Client Roaming – Properly Designed and Tuned Network
A
B
C
D
E
Good signal!
Device starts to move
All AP’s that hear >-85dBm respond (dynamic based on NF)
Time / distance
Signal Strength
E
I
G
H
F
Probe Threshold Reached
Device Sends out Probe Requests
Notes: All the AP’s that hear the probe requests respond to it with a probe response frame.
The client then builds a roaming table of bssid’s that are candidate AP’s to roam to.
If AP’s are seen within -8 to -10dB of each other those are treated as equivalent AP’s in the client’s roaming table and the stronger AP may be below the weaker AP in the client’s table.

## Slide 54: Client Roaming – Properly Designed and Tuned Network
A
B
C
D
E
Good signal!
Device starts to move
All AP’s that hear >-85dBm respond
Roaming threshold reached and device picks an AP in the table built from the probe responses based on signal strength received and/or 802.1k information (if supported)
Time / distance
Signal Strength
E
I
G
H
F
Probe Threshold Reached
Device Sends out Probe Requests
Notes: The client reaches the roam threshold and roams to the top candidate in it’s list. For this example let’s say that is -75dBm.
….and the process repeats itself when the client reaches the probe threshold again

## Slide 55: Client Roaming – AP Power Too High
Signal Strength
B
C
D
Client picks far away AP versus the proper one since the received signal strengths of the probe response were within -10dB of each other. The down stream connection (green line) is okay but the upstream from the client (red line) is garbage leading to down-rating, retransmissions, errors and slowing other users down on that channel for any AP on the same channel within earshot.
Time / distance
Notes: If the AP power is too high the client could connect to a far away AP
This results in a link imbalance and data rate imbalance

## Slide 56: Client Roaming – AP Power Too High
Signal Strength
B
C
D
E
Client picks far away AP versus the proper one since the received signal strengths of the probe response were within -10dB of each other. The down stream connection (green line) is okay but the upstream from the client (red line) is garbage leading to down-rating, retransmissions, errors and slowing other users down on that channel for any AP on the same channel within earshot.
Time / distance
E
I
G
H
F
Device reaches an error threshold and starts looks for another AP to go to by probing and once again may go to a far away AP
J
K
L
M
Notes: Instead of the client reaching a probe threshold where it starts the roaming process it reaches either a retry threshold or error threshold
This triggers a panicked set of probes and scanning for DFS beacons. The client may or may not be able to maintain connectivity at this point.
All the AP’s the hear the client respond

## Slide 57: Client Roaming – AP Power Too High
Signal Strength
B
C
D
E
Client picks far away AP versus the proper one since the received signal strengths of the probe response were within -10dB of each other. The down stream connection (green line) is okay but the upstream from the client (red line) is garbage leading to down-rating, retransmissions, errors and slowing other users down on that channel for any AP on the same channel within earshot.
Time / distance
E
I
G
H
F
Device reaches an error threshold and starts looks for another AP to go to by probing and once again may go to a far away AP
J
K
L
M
Notes: The client roams and the client may get lucky and connect to a relatively close AP but most likely will connect to a far away AP and the same process starts over.
With all the low data rate traffic in the air it will slow down all the users that got lucky and are on a relatively close AP.
With voice SSID’s you could potentially hear choppiness, one way audio and other voice anomalies during roams or even after roaming as you may have roamed to a far away AP
With data clients the performance will just be horrible for the most part.

## Slide 58: 802.11k,v if enabled and if client supports (802.11v iOS 8 and SG5 today)
Neighbor report
Information about other APs to help with handover candidate discovery
AP chan secy key beacon
scope offset
B 6 WPA2 0 45
C 52 WPA2 0 12
D 161 WPA2 0 74
Beacon Report
Client reports how it hears (RSSI) the beacons of other APs
BSSID RSSI
AP B -65
AP D -72
AP E -65
A
BSS Transition Management
AP instructs client to move to another AP
Move to AP D
D
A
Channel Report
AP informs client of channels used by the WLAN
Channel
6
52
161
Overlaps with neighbor report
B
C
D
A
B
C
D
A
Notes: We support neighbor and channel reports for 802.11k
802.11v is used with client match for bss transition messages to tell clients to go to a better bssid

## Slide 59: Directional Antenna Impact on Client Roaming
Directional Antennas…..not that there’s anything wrong with them!
Very Abrubt Cell Edges/No graceful fading of signal
In addition, this signal goes a long distance, they are spotlights!
Notes: Considering how a client roams based on received signal strength directional antennas can have unintended consequences since they have typically have relatively sharp signal edges
While in motion, this means that the client could have a great signal and then that signal could drop off suddenly where the client has to go through it’s probe phase for roaming very suddenly versus having the time gap between the probe phase and actual roam.
This could cause minor issues during roaming
Omni-directional antennas will satisfy 98% of the wireless needs out there.
An AP-275 at 18 feet high can reach out as far as 300-350 feet in an open air environment like a hanger or field house. This is the typical place where directional antennas are needed for client connectivity.

## Slide 60: Client Match

## Slide 61: Client Match
What is it?
  Client Match is a tool to get users to the best AP based on the client Signal to Noise ratio versus simply relying on clients to decide which AP to connect to
  This is measured by signal strength/SNR of the client probe requests as they are heard at the AP’s prior to 6.4.2.3
  In 6.4.2.3 some enhancements were added to also use the following frames to measure client signal strength which is a big step forward
    Block ACK
    Management frames
    Probe Request
    NULL data frame
    Data frame with rate no higher than 36Mbps
  The controller takes the client signals/SNR information and builds a “Virtual Beacon Report”
  Configuration is found under the ARM profile
  Client match is NOT a roaming tool….it takes time to build the VBR and apply actions

## Slide 62: Client Match
What does it do with the “Virtual Beacon Report”?
  The controller takes this information and takes one of three actions provided that certain thresholds are met
    Band Steer
    Sticky
    Load Balance
    MU-MIMO Client Steering

## Slide 63: Client Match
Client Match Events – BandSteer
  Pushing the client to 5 GHz from 2.4 GHz
Yes
Associated on 2.4 GHz
2.4GHz signal is weaker than
-45dBm (cm-band-g-max-signal)
AND Client SNR >18 (cm-sticky-snr)
Stop
Do not start logic flow if only 2.4 GHz probe requests seen
Yes
5 GHz client signal is >-75dBm
(cm-band-a-min-signal)
Stop
Yes
Total number of clients >15 on BOTH radios
No
Stop
No
MOVE CLIENT
Send 802.11v BSS Transition Message (if supported)
(cm-dot11v)
Up to 5 BTM messages
If BTM’s fail or if unsupported by client then
DeAuth and Blacklist for 10 Seconds
(cm-steer-timeout)
Yes
No
ID Clients that are dual band capable by looking at probe req
Stop if 2.4 GHz client signal is stronger than -45dBm
(cm-band-g-max-signal)
No
Yes

## Slide 64: Client Match
Client Match Events – Sticky
  Client is associated to an AP that is not receiving the client’s signal above an SNR threshold
AP Monitors its Attached Clients SNR
Yes
No
X >/= 18 SNR
X = Current AP
(cm-sticky-snr)
Stop and apply bandsteering flow
No
Y > -65 dBm
Y = Neighbor AP (cm-sticky-min-signal)
Stop Logic
Yes
Yes
No
Y > 10 dB SNR
Versus X SNR
(cm-sticky-snr-delta)
Stop Logic
Start Sticky Algorithm
MOVE CLIENT
Send 802.11v BSS Transition Message (if supported)
(cm-dot11v)
Up to 5 BTM messages
If BTM’s fail or if unsupported by client then
DeAuth and Blacklist for 10 Seconds
(cm-steer-timeout)

## Slide 65: Client Match
Client Match Events – Load Balancing
  Steering Clients to Under-loaded Radios
Yes
Actual Channel Load
Number of clients per channel
Do Nothing
No
Radio has more than 30 Clients on radio
(cm-lb-client-thresh)
Target Channel Load
# clients/# Channels
Determine the under-loaded and overloaded radios by comparing the actual per channel and target per channel
Compare
On the overloaded radios, determine the target clients that can be moved >30 SNR on target radio and no worse than 5 dB of the existing AP
(cm-lb-snr-thresh) (cm-lb-signal-delta)
Yes
No
Visit next radio to see if >30SNR and no worse than 5 dB of the existing AP
Yes
No
Visit next radio to see if >30SNR and no worse than 5 dB of the existing AP
Yes
MOVE CLIENT
Send 802.11v BSS Transition Message (if supported)
(cm-dot11v)
Up to 5 BTM messages
If BTM’s fail or if unsupported by client then
DeAuth and Blacklist for 10 Seconds
(cm-steer-timeout)

## Slide 66: Client Match
Client Match Events – MU-MIMO Steering
  Grouping MU-MIMO Capable Clients on the Same Access Points
ID Clients that are MU-MIMO capable
Yes
Does the neighboring AP Have Another MU-MIMO Capable Device Associated
MOVE CLIENT
Send 802.11v BSS Transition Message (if supported)
5 BTM messages and then timeout
OR
DeAuth and Blacklist for 10 Seconds
Is the Client’s SNR >30 on the Neighboring AP
(cm-mu-snr-thresh)
No
No
Stop
Does the AP Have More than 15 Users on the Radio
(cm-mu-client-thresh)
No
Stop
Yes
Yes
No
Evaluate Next Access Point
Yes
Evaluate Next Access Point

## Slide 67: Client Match

## Slide 68: Client Match
Client Match – Tuning
  Client Match forces users to other AP’s typically after they are connected
    In software versions >6.4.2.3 802.11v BSS transition messages are used if the client is 802.11v capable
    Prior to 6.4.2.3 or if the client doesn’t support 802.11v, the mechanism used is a 802.11 de-auth message
    De-auth’s force the user off an AP and can result is a less than desirable user experience in certain circumstances
    Client Match is voice aware and will not issue a de-auth if a client is on a voice call
  Based on this it desirable to have the client connect to the best AP on their own and avoid having Client Match having to guide them to a better AP if possible
  The following default setting should be adjusted to make sure that clients are always bandsteered to the A band if possible
  Client Match Band Steer G Band Max Signal (-dBm) 10  Signal level above which clients on B/G band will not be bandsteered. We always want the client to be bandsteered to the A band if possible so this should be set to 10 to effectively disable. Default is 45.
  Client Match Restriction timeout (sec) 3  When a device is de-auth’ed, all the AP’s except for the AP that we want them to go to temporarily blacklist the client. If a client is very stubborn and won’t go were we want them to we don’t want them disconnected for more than a few seconds. Default is 10
  Client Match Sticky client check SNR (dB) 18-25  Minimum SNR under which a client will declared sticky . Default is 18. The higher the AP density the higher value this should be

## Slide 69: Client Match
Un-Steerable Clients
  Non - IOS
  Controller keeps track of successive steer failures for the respective steer reason to the desired destination radio
  Upon 2 consecutive failed steer attempts the controller notifies the associated AP to mark the client as unsteerable (cm-max-steer-fails)
  AP will not attempt to band steer that client for that specific reason (SLB and Sticky are still in play)
  To view unsupported clients “show ap arm client-match unsupported”
  Default Unsteerable client ageout 2 days (cm-unst-ageout-interval)
  IOS Clients
  IOS clients can get into a state where they will NOT try to reconnect after multiple de-authentications sent by the controller
  To work around this we have implemented a backoff timer for IOS devices that is defaulted to 300 seconds 5 Minutes after an unsuccessful client steer (cm-steer-backoff)
  You will see an “I” flag with a “T” (temporary) if the 2 threshold has not been hit yet

## Slide 70: Client Match
To view the VBR on the controller
Show ap virtual-beacon-report client-mac/ap-name/ip-addr/ip6-addr
  Primary-220
    The client’s signal strength is -51dBm on B/G and -55dBm on A
    The client’s upstream SNR is 89-51 = 38 B/G and 97-55 = 42 on A
  Secondary-220
    The client’s signal strength is -65dBm on B/G and -70dBm on A
    The client’s upstream SNR is 96-65 = 31 B/G and 93-70 = 23 on A

## Slide 71: Client Match
  Looking the client match history for a client
  Show ap arm client-match history/advanced/client-mac<mac>

## Slide 72: Client Troubleshooting

## Slide 73: Client Troubleshooting
Association
Authentication
Network Connectivity
User Role(s)

## Slide 74: Client Troubleshooting
Association
  Is the user associated
  What AP is the user connected to?
    Remember that the user is going to connect on their own to begin with before Client Match steers them anywhere
    Does it makes sense where they are connected to?
      Through walls, floors?
      Farther AP via line of sight?
    The user should connect to the closest unobstructed AP
  Is it the correct/expected AP?
    If not, why not?
  Is Client Match pushing the user to the correct AP after 2-4 minutes?
    If not, why not?

## Slide 75: Client Troubleshooting
Association
  show ap association client-mac <mac address>
  shows a lot of detailed information for a specific user including-
    AP Name the user is connected to
    BSSID the user is connected to
    MAC address
    ESSID
    VLAN-ID – The vlan that the user traffic is being sent on once it hits the distribution system (aka., wired network)
    Tunnel-id - Identification number of the AP’s tunnel.
    Assoc. time - Amount of time the client has associated with the AP, in the format hours:minutes:seconds.
    Band steer moves (T/S) – Tries and Success
    Channel – Channel number
    Channel Frame Retry Rate – A high number indicates a busy channel  Is the channel super busy >50%, why?
    Channel Frame Error Rate – What percentage of traffic is errors  High # needs to be looked at
    Channel Bandwidth Rate(kbps) - at this point in time
    Channel Noise – Noise Floor  Is the noise floor high? > 85 for B/G or >90 for A
    Client Frame Retry Rate – How many frames need to be transmitting as a percentage of all frames
    Client Tx Packets
    Client Rx Packets
    Client Tx Bytes
    Client Rx Bytes
    Client SNR – Noise floor minus the RSSI of the client
  By far the most important piece of information besides the AP the client is connected to
  25 is bare minimum, 30 is a good target
        Below 25 and the client or AP will down rate the connection 802.11n
  > 33-35 is best for AC rates

## Slide 76: Client Troubleshooting
Association
  show ap association client-mac <mac address>
  Other information that is not important in most circumstances –
    Association and Authentication State (802.11) – Remember that there are two types of 802.11 authentication, Open System and Shared Key (aka., WEP). So, this should not be confused with network authentication like 802.1X (which uses 802.11 Open System authentication).
    AID – Association Identifier. A client receives a unique 802.11 association ID when it associates to an AP
    l-int – Number of beacons in the 802.11 listen interval. There are ten beacons sent per second, so a ten-beacon listen interval indicates a listen interval time of 1 second.
    Num assoc – how many users are associated to this BSSID, including the user you are current viewing
    Channel Frame Fragmentation Rate – 802.11 Fragmentation – only an issue is extremely high
    Channel Frame Low Speed Rate - what percentage of traffic is sent at the lowest supported data rate
    Channel Frame Non Unicast Rate – percentage of multicast/broadcast traffic. Note that this may be zero if using multicast optimization and broadcast filter arp/broadcast filter all.
  This command is really useful for doing roaming test and keeping an eye on the SNR for the client and when user roams (based on the AP name changing) in real time. Note that the information contained in the association table (top) of the output (AP Name, bssid, client mac, auth/assoc, assoc. time, flag, etc. is updated real time. However, the information in the lower part of the output labeled as “stats” where you have the two columns, “parameter” and “value” is updated every 60 seconds.

## Slide 77: Client Troubleshooting
Association
  show ap association client-mac <mac address> shows association information only
Notes: Note the key things highlighted

## Slide 78: Client Troubleshooting
Association – Windows
  netsh wlan show interfaces (or all which shows everything)

## Slide 79: Client Troubleshooting
Association – Mac
airport –s and airport –I

## Slide 80: Client Troubleshooting
Association
  show ap debug client-table ap-name Primary-220
  This is a critical command for viewing the upstream data rates from the client to the AP and vice versa
  Remember that data rates are dynamic and will fluctuate
Notes: Note the data rates here where you can see not only the downlink (from AP to client) data rates but also the uplink (from client to AP) data rates.
Note that if a client is idle that it’s uplink data rate may drop down, especially if in power save mode (see PS_State field)

## Slide 81: Client Troubleshooting
Roaming – Where has the client been did the controller do something to force a roam?
  show ap client trail-info <mac>

## Slide 82: Client Troubleshooting
Authentication
  802.1X used as part of WPA2/AES is the source of most authentication issues in wireless networks, especially with client roaming
    Remember that are a LOT of radius transactions (typically 20+) that occur during initial connectivity and/or roaming between access points unless PMK caching or OKC is utilized by the client and AP.
    Server issues
      Where is the radius authentication server? What is the latency to that server?
      Does this radius server have to do a backend authentication requests to another AA repository like Active Directory? What is the latency between the radius front end and backend AA database?
      Are there any timeouts occurring
    Client driver issues
      Key exchanges not happening properly as seen in the “show auth-tracebuf”?
      Other client transactions not happening properly as seen in the “show auth-tracebuf”?

## Slide 83: Client Troubleshooting
Authentication - 802.1X
  802.1X authentication happens when
    The user initially connects
    The user roams between access points
      Pairwise Master Key (PMK) Caching
        Enabled by default and cannot disable but you can disable validation of the PMKID BUT DON’T!!!
        Enables 4 way key exchange versus going through a full authentication
        Is done when a user roams back to an access point that the user has been to in the last 8 hours (timer is configurable)
        Doesn’t always work, key can be invalidated by either party
  From IEEE 802.11i section 8.4.1.2.1 - A STA (AP) can retain PMKs for APs (STAs) in the ESS to which it has previously performed a full IEEE 802.1X authentication. If a STA wishes to roam to an AP for which it has cached one or more PMKSAs, it can include one or more PMKIDs in the RSN information element of its (Re)Association Request frame. An AP whose Authenticator has retained the PMK for one or more of the PMKIDs can skip the 802.1X authentication and proceed with the 4-Way Handshake. The AP shall include the PMKID of the selected PMK in Message 1 of the 4-Way Handshake. If none of the PMKIDs of the cached PMKSAs matches any of the supplied PMKIDs, then the Authenticator shall perform another IEEE 802.1X authentication. Similarly, if the STA fails to send a PMKID, the STA and AP must perform a full IEEE 802.1X authentication.”
      Opportunistic Key Caching (OKC)
        Enabled by default
        Enables 4 way key exchange versus going through a full authentication
        Not all clients support
    Based on all this the radius server MUST be local or available over a very low latency link
      Remember that there are 20+ radius transactions per user authentication if no PMK caching or OKC

## Slide 84: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Radius Authentication Server
    Common issue when radius servers are not local (or even when they are because of overutilization)
    To view radius server timeouts and look for a high percentage of timeouts relative to the overall number of requests
    show aaa authentication-server radius statistics
    (sort of hidden command since if you type show aaa authentication<space>? It won’t show up)
Average response times should be below 100ms and the timeouts should not be incrementing

## Slide 85: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  If the radius server statistics look good but the user is not authenticating properly or having trouble roaming do the following….
  Enable debugging for their mac address
    logging level debugging user-debug <mac address>
  Have them try to authenticate or roam to re-create the issue
  Look at the auth-tracebuf on the controller to see what the issue is
    Show auth-tracebuf | inc <mac address>
    Note that this is a rolling buffer that is FIFO so don’t wait too long to view
    Also, when you are done troubleshooting make sure you disable the debug logging on the controller
      Config t no logging level debugging user-debug <mac address>

## Slide 86: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Viewing the auth-tracebuf – Almost Normal Full 802.1X Authentication
  (XYZ Company) #show auth-tracebuf | include 38:aa:3c:12:dd:32
  May 29 20:16:47 station-down * 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - -
  May 29 20:16:50 station-up * 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - - wpa2 aes
  May 29 20:16:50 eap-id-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 1 5
  May 29 20:16:50 eap-id-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 1 26 northamerica\user-X
  May 29 20:16:50 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 65517 214
  May 29 20:16:50 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65517 90
  May 29 20:16:50 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 2 6
  May 29 20:16:50 eap-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 2 240
  May 29 20:16:50 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65526 466
  May 29 20:16:50 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65526 1188
  May 29 20:16:50 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 3 1096
  May 29 20:16:50 eap-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 3 6
  May 29 20:16:50 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65535 232
  May 29 20:16:50 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65535 1188
  May 29 20:16:50 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 4 1096
  May 29 20:16:50 eap-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 4 6
  May 29 20:16:50 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 3 232
  May 29 20:16:50 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 3 781
  May 29 20:16:50 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 5 693
  May 29 20:16:50 eap-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 5 220
  May 29 20:16:50 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65486 446
  May 29 20:16:50 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65486 153
  May 29 20:16:50 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 6 69
  May 29 20:16:50 eap-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 6 6
  May 29 20:16:50 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 4 232
  May 29 20:16:50 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 4 127
  May 29 20:16:50 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 7 43
  May 29 20:16:50 eap-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 7 96
  May 29 20:16:50 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65475 322
  May 29 20:16:50 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65475 143
  May 29 20:16:50 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 8 59
  May 29 20:16:50 eap-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 8 96
  May 29 20:16:50 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 5 322
  May 29 20:16:50 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 5 159
  May 29 20:16:50 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 9 75
  May 29 20:16:50 eap-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 9 160

## Slide 87: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Viewing the auth-tracebuf – Almost Normal Full 802.1X Authentication Continued
  May 29 20:16:50 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65512 386
  May 29 20:16:50 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 65512 175
  May 29 20:16:50 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 10 91
  May 29 20:16:53 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 10 91 user supplicant timed out here and server had to make another EAP-ID request
  May 29 20:16:53 eap-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 10 80
  May 29 20:16:53 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 6 306
  May 29 20:16:53 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 6 191
  May 29 20:16:53 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 12 107
  May 29 20:16:53 eap-resp → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 12 144
  May 29 20:16:53 rad-req → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 8 370
  May 29 20:16:53 rad-accept <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/RADIUS-2 8 356
  May 29 20:16:53 eap-success <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 12 4
  May 29 20:16:53 station-data-ready * 38:aa:3c:12:dd:32 00:00:00:00:00:00 851 -
  May 29 20:16:53 wpa2-key1 <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - 117
  May 29 20:16:53 wpa2-key2 → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - 135
  May 29 20:16:53 wpa2-key3 <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - 151
  May 29 20:16:53 wpa2-key4 → 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - 95

## Slide 88: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Viewing the auth-tracebuf – Normal Full 802.1X Authentication After Roam
  May 29 20:17:27 station-down * 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - -  User roams here 40 seconds later
  May 29 20:17:27 station-up * 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 - - wpa2 aes
  May 29 20:17:27 eap-id-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 1 5
  May 29 20:17:27 eap-id-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 1 26 northamerica\User-X
  May 29 20:17:27 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 17 214
  May 29 20:17:27 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 17 90
  May 29 20:17:27 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 2 6
  May 29 20:17:27 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 2 240
  May 29 20:17:27 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 19 466
  May 29 20:17:27 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 19 1188
  May 29 20:17:27 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 3 1096
  May 29 20:17:27 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 3 6
  May 29 20:17:27 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 18 232
  May 29 20:17:27 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 18 1188
  May 29 20:17:27 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 4 1096
  May 29 20:17:27 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 4 6
  May 29 20:17:27 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 23 232
  May 29 20:17:27 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 23 1188
  May 29 20:17:27 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 5 1096
  May 29 20:17:27 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 5 6
  May 29 20:17:27 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 27 232
  May 29 20:17:27 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 27 1188
  May 29 20:17:27 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 6 1096
  May 29 20:17:27 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 6 6
  May 29 20:17:27 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 28 232
  May 29 20:17:27 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 28 132
  May 29 20:17:27 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 7 48
  May 29 20:17:27 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 7 220
  May 29 20:17:27 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 26 446
  May 29 20:17:27 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 26 153
  May 29 20:17:27 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 8 69
  May 29 20:17:27 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 8 6
  May 29 20:17:27 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 1 232
  May 29 20:17:27 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 1 127
  May 29 20:17:27 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 9 43
  May 29 20:17:27 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 9 96
  May 29 20:17:27 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 31 322

## Slide 89: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Viewing the auth-tracebuf – Normal Full 802.1X Authentication After Roam
  May 29 20:17:27 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 31 322
  May 29 20:17:27 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 31 143
  May 29 20:17:27 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 10 59
  May 29 20:17:28 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 10 96
  May 29 20:17:28 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 65528 322
  May 29 20:17:28 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 65528 159
  May 29 20:17:28 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 11 75
  May 29 20:17:28 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 11 160
  May 29 20:17:28 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 25 386
  May 29 20:17:28 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 25 175
  May 29 20:17:28 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 12 91
  May 29 20:17:28 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 12 80
  May 29 20:17:28 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 33 306
  May 29 20:17:28 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 33 191
  May 29 20:17:28 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 14 107
  May 29 20:17:28 eap-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 14 144
  May 29 20:17:28 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 30 370
  May 29 20:17:28 rad-accept <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8/Radius-2 30 356
  May 29 20:17:28 eap-success <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 14 4
  May 29 20:17:28 station-data-ready * 38:aa:3c:12:dd:32 00:00:00:00:00:00 851 -
  May 29 20:17:28 wpa2-key1 <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 - 117
  May 29 20:17:28 wpa2-key2 -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 - 117
  May 29 20:17:28 wpa2-key3 <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 - 151
  May 29 20:17:28 wpa2-key4 -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 - 95
  All good with this exchange and user roam

## Slide 90: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Viewing the auth-tracebuf – PMK Caching After Roaming Back to Original BSSID
  May 29 20:18:04 station-down * 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 - -  User roams here 36 seconds later
  May 29 20:18:04 station-up * 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - - wpa2 aes
  May 29 20:18:04 station-data-ready * 38:aa:3c:12:dd:32 00:00:00:00:00:00 851 -
  May 29 20:18:04 wpa2-key1 <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - 117
  May 29 20:18:04 wpa2-key2 -> 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - 135
  May 29 20:18:04 wpa2-key3 <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - 151
  May 29 20:18:04 wpa2-key4 -> 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - 95
  Note the abbreviated authentication since PMK caching has kicked in here

## Slide 91: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Viewing the auth-tracebuf – User Supplicant Not Responding to EAP-ID Request
May 29 20:21:17 station-down * 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - -  User roams here
May 29 20:21:17 station-up * 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - - wpa2 aes
May 29 20:21:17 eap-id-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 1 5  Appears that the AP no longer has the PMK cached so a full re-auth is started
May 29 20:21:17 eap-id-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 1 26 northamerica\User-X
May 29 20:21:17 rad-req -> 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 65425 214
May 29 20:21:17 rad-resp <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc/Radius-2 65425 90
May 29 20:21:17 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 2 6
May 29 20:21:21 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 2 6  Houston we have a problem…the client is not responding to the eap requests, see the next 3 requests and the timestamps. Our timeout (which is configurable) is 5 seconds by default which is more than enough time.
May 29 20:21:24 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 2 6
May 29 20:21:27 eap-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 2 6
May 29 20:21:30 eap-failure <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 2 4 server timeout  Remember that these EAP messages are between the client and the server so the server decides to timeout and force the client to try again.
May 29 20:21:30 eap-failure <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 3 4 station timeout  The station didn’t respond to the last message so it’s timed out and the process starts over
May 29 20:21:30 eap-id-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 3 5
May 29 20:21:33 eap-id-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 3 5
May 29 20:21:36 eap-id-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc 4 5
May 29 20:21:36 station-down * 38:aa:3c:12:dd:32 d8:c7:c8:96:70:bc - -
May 29 20:21:36 station-up * 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 - - wpa2 aes
May 29 20:21:36 eap-id-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 1 5
May 29 20:21:39 eap-id-req <- 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 1 5
May 29 20:21:39 eap-id-resp -> 38:aa:3c:12:dd:32 d8:c7:c8:96:4b:b8 1 26 northamerica\User-X  On the next try the user responds to the second EAP ID request and then things proceed normally.
  Note that this ended up to be a client driver/supplicant issue that was reported to the appropriate manufacturer

## Slide 92: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Viewing the auth-tracebuf – Bad Client Driver
  (7200-xyz) #show auth-tracebuf | include 3c:a9:f4:32:da:bc
  Jan 29 07:04:36 station-down * 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - -
  Jan 29 07:14:55 station-up * 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - - wpa2 aes
  Jan 29 07:14:55 eap-id-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 1 5
  Jan 29 07:14:57 eap-start -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - -
  Jan 29 07:14:57 eap-id-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 1 5
  Jan 29 07:14:59 eap-id-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 1 5
  Jan 29 07:15:00 eap-id-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 1 11 nmdq87
  Jan 29 07:15:00 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 65515 211
  Jan 29 07:15:00 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65515 77
  Jan 29 07:15:00 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 45 6
  Jan 29 07:15:00 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 45 227
  Jan 29 07:15:00 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65516 458
  Jan 29 07:15:00 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65516 1089
  Jan 29 07:15:00 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 46 1012
  Jan 29 07:15:00 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 46 6
  Jan 29 07:15:00 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65517 237
  Jan 29 07:15:00 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65517 1085
  Jan 29 07:15:00 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 47 1008
  Jan 29 07:15:00 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 47 6
  Jan 29 07:15:00 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65518 237
  Jan 29 07:15:00 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65518 1085
  Jan 29 07:15:00 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 48 1008
  Jan 29 07:15:00 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 48 6
  Jan 29 07:15:00 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65519 237
  Jan 29 07:15:00 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65519 1085
  Jan 29 07:15:00 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 49 1008
  Jan 29 07:15:00 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 49 6
  Jan 29 07:15:00 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65520 237
  Jan 29 07:15:00 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65520 266
  Jan 29 07:15:00 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 50 195
  Jan 29 07:15:00 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 50 1310
  Jan 29 07:15:00 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65521 1551
  Jan 29 07:15:00 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65521 77
  Jan 29 07:15:00 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 51 6
  Jan 29 07:15:00 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 51 895
  Jan 29 07:15:00 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65522 1132

## Slide 93: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Viewing the auth-tracebuf – Bad Client Driver
  Jan 29 07:15:00 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65522 140
  Jan 29 07:15:00 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 52 69
  Jan 29 07:15:00 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 52 6
  Jan 29 07:15:00 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65523 237
  Jan 29 07:15:00 rad-accept <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 65523 204
  Jan 29 07:15:00 eap-success <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 52 4
  Jan 29 07:15:00 wpa2-key1 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - 117
  Jan 29 07:15:00 wpa2-key2 -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - 117
  Jan 29 07:15:00 wpa2-key3 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - 151
  Jan 29 07:15:00 wpa2-key4 -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - 95
  Jan 29 07:15:28 station-down * 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - -
  Jan 29 07:15:30 station-up * 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - - wpa2 aes
  Jan 29 07:15:30 wpa2-key1 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 117
  Jan 29 07:15:30 wpa2-key2 -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 135
  Jan 29 07:15:30 wpa2-key3 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 151
  Jan 29 07:15:30 wpa2-key4 -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 95
  Jan 29 07:23:53 station-down * 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - -
  Jan 29 07:23:53 station-up * 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - - wpa2 aes
  Jan 29 07:23:53 eap-id-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 1 5
  Jan 29 07:23:54 eap-start -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - -
  Jan 29 07:23:54 eap-id-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 1 5
  Jan 29 07:23:57 eap-id-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 1 5
  Jan 29 07:23:57 eap-id-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 1 11 nmdq87
  Jan 29 07:23:57 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 3 211
  Jan 29 07:23:57 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 3 77
  Jan 29 07:23:57 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 81 6
  Jan 29 07:23:57 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 81 227
  Jan 29 07:23:57 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 4 458
  Jan 29 07:23:57 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 4 1089
  Jan 29 07:23:57 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 82 1012
  Jan 29 07:23:57 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 82 6
  Jan 29 07:23:57 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 5 237
  Jan 29 07:23:57 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 5 1085
  Jan 29 07:23:57 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 83 1008
  Jan 29 07:23:57 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 83 6
  Jan 29 07:23:57 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 6 237
  Jan 29 07:23:57 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 6 1085

## Slide 94: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Viewing the auth-tracebuf – Bad Client Driver
  Jan 29 07:23:57 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 84 1008
  Jan 29 07:23:57 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 84 6
  Jan 29 07:23:57 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 7 237
  Jan 29 07:23:57 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 7 1085
  Jan 29 07:23:57 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 85 1008
  Jan 29 07:23:57 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 85 6
  Jan 29 07:23:57 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 8 237
  Jan 29 07:23:57 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 8 266
  Jan 29 07:23:57 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 86 195
  Jan 29 07:23:57 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 86 1310
  Jan 29 07:23:57 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 9 1551
  Jan 29 07:23:57 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 9 77
  Jan 29 07:23:57 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 87 6
  Jan 29 07:23:57 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 87 895
  Jan 29 07:23:57 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 10 1132
  Jan 29 07:23:57 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 10 140
  Jan 29 07:23:57 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 88 69
  Jan 29 07:23:57 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 88 6
  Jan 29 07:23:57 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 11 237
  Jan 29 07:23:57 rad-accept <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0/Radius-2 11 204
  Jan 29 07:23:57 eap-success <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 88 4
  Jan 29 07:23:57 wpa2-key1 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - 117
  Jan 29 07:23:57 wpa2-key2 -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - 117
  Jan 29 07:23:57 wpa2-key3 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - 151
  Jan 29 07:23:57 wpa2-key4 -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - 95
  Jan 29 07:24:25 station-down * 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:c0 - -
  Jan 29 07:24:27 station-up * 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - - wpa2 aes
  Jan 29 07:24:27 wpa2-key1 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 117
  Jan 29 07:24:28 wpa2-key1 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 117
  Jan 29 07:24:29 wpa2-key2 -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 135
  Jan 29 07:24:29 wpa2-key3 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 151
  Jan 29 07:24:29 wpa2-key4 -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 95
  Jan 29 07:25:36 station-up * 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - - wpa2 aes
  Jan 29 07:25:36 eap-id-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 2 5
  Jan 29 07:25:37 eap-start -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - -
  Jan 29 07:25:37 eap-id-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 2 5
  Jan 29 07:25:37 eap-id-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 2 11 nmdq87

## Slide 95: Client Troubleshooting
Authentication – Troubleshooting 802.1X Auth Issues
  Viewing the auth-tracebuf – Bad Client Driver
  Jan 29 07:25:37 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 96 6
  Jan 29 07:25:38 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 96 895
  Jan 29 07:25:38 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0/Radius-2 28 1132
  Jan 29 07:25:38 rad-resp <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0/Radius-2 28 140
  Jan 29 07:25:38 eap-req <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 97 69
  Jan 29 07:25:38 eap-resp -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 97 6
  Jan 29 07:25:38 rad-req -> 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0/Radius-2 29 237
  Jan 29 07:25:38 rad-accept <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0/Radius-2 29 204
  Jan 29 07:25:38 eap-success <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 97 4
  Jan 29 07:25:38 wpa2-key1 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 117
  Jan 29 07:25:39 wpa2-key1 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 117
  Jan 29 07:25:41 wpa2-key1 <- 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0 - 117
  Jan 29 07:25:44 station-down * 3c:a9:f4:32:da:bc 9c:1c:12:8a:75:d0
  Ubuntu Linux Driver Issue with Intel 6300
  Resolution was to disable 40 MHz channels on the client

## Slide 96: Client Troubleshooting
Network Connectivity
  DHCP
    Is the server getting overloaded?
      DHCP NACKs happen during roams (client checking to make sure it can still use the address)
    Is the controller the DHCP server?
      If greater than X number of clients then an external DHCP needs to be used
    Use debug logging on the controller for DHCP
      conf t logging level debugging network subcat dhcp
  Is the DHCP relay working properly?
  User VLAN
    Is the user vlan being switched/routed properly?

## Slide 97: Client Troubleshooting
Network Connectivity – DHCP Normal Release/Renew
  Viewing DHCP requests in the controller after enabling debug logging
  show log network 100 (| inc dhcp)

## Slide 98: Client Troubleshooting
Network Connectivity – DHCP Normal Roam
  Viewing DHCP requests in the controller after enabling debug logging
  show log network 100 (| inc dhcp)

## Slide 99: Client Troubleshooting
User Role(s)
  What user roles are assigned to the user both pre-authentication (captive portal) and post authentication? Do the respective roles have the correct ACLs?
  show user mac <mac>

## Slide 100: Client Troubleshooting
User Role(s) – What ACLS are applied?
Show rights <role name>

## Slide 101: Client Troubleshooting
User Role(s) – Is the user hitting the correct ACL
Show datapath session | inc <user ip address>
or
Show datapath session | include "Source IP,Flags,no syn,set ToS,mirror,Real-Time,Deep inspect,Media Deep,Application Firewall,<user ip>” to show column headers and flag definitions

## Slide 102: What we covered
802.11 Wireless Networking
Access Point Planning and Placement
Adaptive Radio Management (ARM)
Client Roaming
Client Match in Detail
Client Troubleshooting

## Slide 103
Notes: Make networks mobility-defined instead of fixed