## Slide 1: EVPN VXLAN
Symmetric IRB
L3 Distributed-Gateway
VSX Logical VTEP
DCN iBGP
Campus-to-DC eBGP Border Gateway IVRL
Aruba Switching TME

## Slide 2
Leaf1-A
Leaf1-B
Leaf2-A
Leaf2-B
Spine-1
iBGP RR
Spine-2
iBGP RR
L2 link
L3 link
DC Topology
AS 65001
VRF1
VRF2
VLAN 10
VLAN 10
VLAN 12
VLAN 20
VLAN 11
VLAN 20
VSX VTEP1
VSX VTEP2
Tenant | VRF name | VLAN | SVI | Subnet | L2VNI | L3VNI
Tenant 1 | VRF1 | 10 | 10 | 10.1.10.0/24 | 10010 | 100001
 |  | 11 | 11 | 10.1.11.0/24 | 10011 | 
 |  | 12 | 12 | 10.1.12.0/24 | 10012 | 
Tenant 2 | VRF2 | 20 | 20 | 10.2.20.0/24 | 10020 | 100002
VRF SERVICES
Core-2
iBGP RR
AS 65100
Border Leaf
Campus
DC
Notes: VSX VTEP1 represents a unique logical VTEP consisting of Leaf1-A and Leaf1-B

## Slide 3
Leaf1-A
Leaf1-B
Leaf2-A
Leaf2-B
Spine-1
iBGP RR
Spine-2
iBGP RR
L2 link
L3 link
Routing Design
AS 65001
VRF1
VRF2
VLAN 10
VLAN 10
VLAN 12
VLAN 20
VLAN 11
VLAN 20
VSX VTEP1
VSX VTEP2
Tenant | VRF name | VLAN | SVI | Subnet | L2VNI | L3VNI
Tenant 1 | VRF1 | 10 | 10 | 10.1.10.0/24 | 10010 | 100001
 |  | 11 | 11 | 10.1.11.0/24 | 10011 | 
 |  | 12 | 12 | 10.1.12.0/24 | 10012 | 
Tenant 2 | VRF2 | 20 | 20 | 10.2.20.0/24 | 10020 | 100002
VRF SERVICES
Core-2
iBGP RR
AS 65100
Border Leaf
Campus
DC
VLAN 2
VLAN 2
IVRL
IVRL
eBGP SERVICES
eBGP SERVICES
VLAN 1156
eBGP SERVICES
VLAN 1150
iBGP SERVICES
iBGP EVPN
iBGP EVPN
iBGP EVPN
iBGP EVPN
iBGP EVPN
iBGP EVPN
iBGP EVPN
iBGP EVPN
Notes: VSX VTEP1 represents a unique logical VTEP consisting of Leaf1-A and Leaf1-B

## Slide 4
VSX VTEP2
L1: 192.168.11.5
VSX VTEP1
L1: 192.168.11.3
VLAN 12 / VNI 10012 / SVI 12 / 10.1.12.0/24
VRF1 / VNI 100001
VRF2 / VNI 100002
VLAN 10 / VNI 10010 / SVI 10 / 10.1.10.0/24
VLAN 11 / VNI 10011 / SVI 11 / 10.1.11.0/24
L3 VNI
L2 VNI
VLAN 20 / VNI 10020 / SVI 20 / 10.2.20.0/24
VNIs Logical View
L2VNI / L3VNI per Tenant
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
vubu3 10.2.20.10
00:50:56:8e:32:e8
vubu4 10.1.11.10
00:50:56:8e:4d:9c
vubu6 10.2.20.11
00:50:56:8e:6b:d8
SERVICES VRF
Campus
Cores
SERVICES VRF link attach
IVRL on Border Leaf
6300-4
192.168.199.2
AS 65001
AS 65001

## Slide 5
8325-1
15.136.40.237
8325-2
15.136.40.238
8325-3
15.136.40.233
8325-4
15.136.40.234
6300-5
15.136.40.245
6300-6
15.136.40.246
2930-3
2930-4
2930-2
5700-1
15.136.40.196
2930-1
L2 link
L3 link
Physical Set-up
VLAN 10
VLAN 10
VLAN 12
VLAN 20
VLAN 11
VLAN 20
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
vubu3 10.2.20.10
00:50:56:8e:32:e8
vubu4 10.1.11.10
00:50:56:8e:4d:9c
vubu6 10.2.20.11
00:50:56:8e:6b:d8
Notes/Warnings on the demo context:
  This set-up is for demo only.
  6300 as a spine is only for lab/demo purpose and not for production (it was not tested and is not currently supported as a spine as not a use-case)
  Servers should be directly connected to 8325 TORs. Intermediate switches are used here for lab optimization to maximize the number of hosts with LACP.
8400-2
15.136.40.236
6300-4
(simulating a server)
15.136.40.244
8400-1
15.136.40.235

## Slide 6
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
ESXi: 15.136.40.25
vmnic0
vmnic1
vmnic3
vmnic2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
vmnic6
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
vmnic0
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
ESXi: 15.136.40.23
ESXi: 15.136.40.24
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
ESXi: 15.136.40.25
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
ESXi: 15.136.40.27
VLAN 11
ESXi: 15.136.40.27
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
1/1/22
PCAP
15.136.40.98 #6
1/1/22
PCAP
15.136.40.98 #2
PCAP
15.136.40.98 #3
PCAP
15.136.40.98 #4
1/1/40
1/1/40
1/1/40
Set-up Details
VLAN 2
VLAN 2
1/3/1
1/8/1
1/3/1
1/8/1
LAG200
8400-2
15.136.40.236
L0: 192.168.2.2
1/3/3
1/3/3
1/1/51
1/1/51
1/3/3
1/3/3
6300-4
15.136.40.244
1/1/9
Details are given to better understand the output of the following show commands
  L0 and L1 IP addresses
  Virtual Machine IP and MAC addresses
  Interconnectivity subnet
  Traffic capture capability
ESXi: 15.136.40.27
vubu7 : 192.168.3.242/29
vmnic3
1/1/1
192.168.3.240/29
192.168.4.0/31
192.168.4.2/31
8400-1
15.136.40.235
L0: 192.168.2.1

## Slide 7
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
vmnic0
vmnic1
vmnic3
vmnic2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
vmnic6
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
vmnic0
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
1/1/22
VLAN 2
VLAN 2
1/3/1
1/8/1
1/3/1
1/8/1
LAG200
8400-2
15.136.40.236
L0: 192.168.2.2
1/3/3
1/3/3
1/1/51
1/1/51
1/3/3
1/3/3
6300-4
15.136.40.244
1/1/9
192.168.4.0/31
192.168.4.2/31
8400-1
15.136.40.235
L0: 192.168.2.1

## Slide 8: Configuration
Spines
VSX VTEP Leafs
VSX VTEP Border Leaf add-on

## Slide 9: DC Spines Configuration
Underlay ROPs, loopbacks
OSPF underlay routing
iBGP Route-Reflectors for EVPN AF

## Slide 10
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Spine-1 Configuration
192.168.110.0/31
Spine-1
ROPs to Leafs / Loopback
VLAN 2
VLAN 2
interface 1/1/25
no shutdown
mtu 9198
routing
ip mtu 9198
ip address 192.168.3.0/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
interface 1/1/26
no shutdown
mtu 9198
routing
ip mtu 9198
ip address 192.168.3.2/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
interface 1/1/27
no shutdown
mtu 9198
routing
ip mtu 9198
ip address 192.168.3.4/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
interface 1/1/28
no shutdown
mtu 9198
routing
ip mtu 9198
ip address 192.168.3.6/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
interface loopback 0
ip address 192.168.1.1/32
ip ospf 1 area 0.0.0.0
L3 Link to Leaf1-A (8325-1)
L3 Link to Leaf1-B (8325-2)
L3 Link to Leaf2-A (8325-3)
L3 Link to Leaf2-B (8325-4)

## Slide 11
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Spine-1 Configuration
192.168.110.0/31
Spine-1
Routing
VLAN 2
VLAN 2
router ospf 1
router-id 192.168.1.1
! optional
max-metric router-lsa include-stub on-startup 300
passive-interface default
!
area 0.0.0.0
router bgp 65001
bgp router-id 192.168.1.1
! optional
trap-enable
bgp fast-external-fallover
bgp log-neighbor-changes
bgp deterministic-med
bgp always-compare-med
!
neighbor leaf peer-group
neighbor leaf remote-as 65001
neighbor leaf description Leaf RR clients
! optional
neighbor leaf password ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
neighbor leaf fall-over
!
neighbor leaf update-source loopback 0
neighbor 192.168.1.3 peer-group leaf
neighbor 192.168.1.4 peer-group leaf
neighbor 192.168.1.5 peer-group leaf
neighbor 192.168.1.6 peer-group leaf
address-family l2vpn evpn
neighbor leaf route-reflector-client
neighbor leaf send-community extended
neighbor 192.168.1.3 activate
neighbor 192.168.1.4 activate
neighbor 192.168.1.5 activate
neighbor 192.168.1.6 activate
exit-address-family
If used, must be the same in the BGP domain
Optional best practices
iBGP peering between loopbacks
Spines are iBGP RR
Extended community is required for EVPN NLRI

## Slide 12
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Spine-2 Configuration
192.168.110.0/31
Spine-2
ROPs to Leafs / Loopback
VLAN 2
VLAN 2
interface 1/1/25
no shutdown
mtu 9198
routing
ip mtu 9198
ip address 192.168.3.8/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
interface 1/1/26
no shutdown
mtu 9198
routing
ip mtu 9198
ip address 192.168.3.10/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
interface 1/1/27
no shutdown
mtu 9198
routing
ip mtu 9198
ip address 192.168.3.12/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
interface 1/1/28
no shutdown
mtu 9198
routing
ip mtu 9198
ip address 192.168.3.14/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
interface loopback 0
ip address 192.168.1.2/32
ip ospf 1 area 0.0.0.0
L3 Link to Leaf1-A (8325-1)
L3 Link to Leaf1-B (8325-2)
L3 Link to Leaf2-A (8325-3)
L3 Link to Leaf2-B (8325-4)

## Slide 13
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Spine-2 Configuration
192.168.110.0/31
Routing
Spine-2
VLAN 2
VLAN 2
router ospf 1
router-id 192.168.1.2
! optional
max-metric router-lsa include-stub on-startup 300
passive-interface default
!
area 0.0.0.0
router bgp 65001
bgp router-id 192.168.1.2
! optional
trap-enable
bgp fast-external-fallover
bgp log-neighbor-changes
bgp deterministic-med
bgp always-compare-med
!
neighbor leaf peer-group
neighbor leaf remote-as 65001
neighbor leaf description Leaf RR clients
! optional
neighbor leaf password ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
neighbor leaf fall-over
!
neighbor leaf update-source loopback 0
neighbor 192.168.1.3 peer-group leaf
neighbor 192.168.1.4 peer-group leaf
neighbor 192.168.1.5 peer-group leaf
neighbor 192.168.1.6 peer-group leaf
address-family l2vpn evpn
neighbor leaf route-reflector-client
neighbor leaf send-community extended
neighbor 192.168.1.3 activate
neighbor 192.168.1.4 activate
neighbor 192.168.1.5 activate
neighbor 192.168.1.6 activate
exit-address-family

## Slide 14: DC Leafs Configuration
VSX / Servers VSX LAGs
Underlay ROPs, Loopbacks, transit VLAN
VRFs and EVPN
Servers SVIs, DHCP
VXLAN Tunnel, VLAN-to-VNI mapping, L3VNI per VRF
OSPF underlay routing
iBGP EVPN AF
iBGP IPv4 AF for Route-Type 5

## Slide 15
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-A Configuration
192.168.110.0/31
Leaf1-A
VSX Configuration / VLANs
vrf KA
!
interface lag 256
vsx-sync vlans
no shutdown
description ISL
no routing
vlan trunk native 1 tag
vlan trunk allowed all
lacp mode active
interface 1/1/41
no shutdown
vrf attach KA
description 8325-2 1/1/41 for keepalive
ip address 192.168.0.0/31
interface 1/1/49
no shutdown
mtu 9198
description VSX ISL link
lag 256
interface 1/1/50
no shutdown
mtu 9198
description VSX ISL link
lag 256
!
vsx
system-mac 02:00:00:00:01:00
inter-switch-link lag 256
role primary
keepalive peer 192.168.0.1 source 192.168.0.0 vrf KA
vsx-sync aaa bgp copp-policy dhcp-relay dns evpn l2-vlan-mac-cfg-mode mclag-interfaces qos-global route-map sflow-global snmp ssh stp-global time vsx-global
!
vlan 2
vsx-sync
vlan 10
vsx-sync
vlan 11
vsx-sync
vlan 20
vsx-sync
VLAN 2
VLAN 2
ISL LAG for VSX ISLP
Keepalive circuit (optional, alternative: routed KA)
ISL physical links
Transit VLAN between VSX nodes for IGP continuity
Servers VLANs
Follow best practices for system-mac value
Notes: Warning: vsx-sync ospf must be disabled to allow ospf configuration on different VLANs on VSX secondary of 8325-2.

## Slide 16
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-A Configuration
192.168.110.0/31
Leaf1-A
VSX LAGs to Servers
interface lag 1 multi-chassis
no shutdown
description 2930-3
no routing
vlan trunk native 1
vlan trunk allowed 10-11
lacp mode active
hash l4-src-dst
!
interface lag 2 multi-chassis
no shutdown
description 2930-4
no routing
vlan trunk native 1
vlan trunk allowed 20
lacp mode active
!
interface 1/1/1
no shutdown
mtu 9000
description Link to 2930-3 (49) - LAG 1 member
lag 1
!
interface 1/1/2
no shutdown
mtu 9000
description Link to 2930-3 (49) - LAG 2 member
lag 2
VLAN 2
VLAN 2
VSX LAG to servers (vubu2, vubu4)
VSX LAG to server (vubu3)
Optional L4 hashing
Links to servers

## Slide 17
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-A Configuration
192.168.110.0/31
Leaf1-A
ROPs to Spines / Loopbacks / Transit VLAN
interface 1/1/23
no shutdown
mtu 9198
ip mtu 9198
ip address 192.168.3.1/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
interface 1/1/24
no shutdown
mtu 9198
ip mtu 9198
ip address 192.168.3.9/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
!
interface loopback 0
ip address 192.168.1.3/32
ip ospf 1 area 0.0.0.0
!
interface loopback 1
ip address 192.168.11.3/32
ip ospf 1 area 0.0.0.0
!
interface vlan 2
ip mtu 9198
ip address 192.168.3.200/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf cost 50
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
Shared anycast Loopback1 of the VSX logical VTEP pair
Unique Loopback0 on each node
Transit VLAN SVI between VSX nodes for IGP continuity
VLAN 2
VLAN 2
L3 Link to Spine-1 (6300-5)
L3 Link to Spine-2 (6300-6)

## Slide 18
Leaf Configuration
VRF Route Distinguisher consideration and recommendation
vrf VRF1
rd 192.168.1.3:1
route-target export 65001:1 evpn
route-target import 65001:1 evpn
vrf VRF2
rd 192.168.1.3:2
route-target export 65001:2 evpn
route-target import 65001:2 evpn
Unique RD per CX node in the VSX Cluster
Provide clear and distinct NLRI sourcing information.
Distinct NLRI advertised by VSX primary and VSX secondary: iBGP Route-Reflector will reflect these 2 distinct entries.
Common RD per CX node in the VSX Cluster
NLRI sourcing information is diluted.
Same NLRI advertised by VSX primary and VSX secondary: iBGP Route-Reflector will reflect only the best route which is from the lowest router-ID (ex: VSX primary).
Leaf1-A
vrf VRF1
rd 192.168.1.4:1
route-target export 65001:1 evpn
route-target import 65001:1 evpn
vrf VRF2
rd 192.168.1.4:2
route-target export 65001:2 evpn
route-target import 65001:2 evpn
Leaf1-B
vrf VRF1
rd 192.168.11.3:1
route-target export 65001:1 evpn
route-target import 65001:1 evpn
vrf VRF2
rd 192.168.11.3:2
route-target export 65001:2 evpn
route-target import 65001:2 evpn
Leaf1-A
vrf VRF1
rd 192.168.11.3:1
route-target export 65001:1 evpn
route-target import 65001:1 evpn
vrf VRF2
rd 192.168.11.3:2
route-target export 65001:2 evpn
route-target import 65001:2 evpn
Leaf1-B
[L0_IP:VRF_ID]
[L1_IP:VRF_ID]

## Slide 19
Leaf Configuration
VRF Route Distinguisher consideration and recommendation
Unique RD per CX node in the VSX Cluster
For the same destination prefix (ex: 10.1.10.0/24), there are 2 distinct NLRIs that are selected and reflected per logical VSX VTEP, one per RD.
Common RD per CX node in the VSX Cluster
For the same destination prefix (ex: 10.1.10.0/24), there are 2 identical routes coming from each VSX nodes. Spine route-reflector selects the best route (route coming from the lowest router-ID) and reflects this single selected route to other RR clients.
best
Unique RD
Same RD

## Slide 20: MP-BGP L2VPN EVPN route-type 5
Spine-1: RT5 – IP prefix route (subnet advertisement)
6300F-5-spine1# show bgp l2vpn evpn route-type 5
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Total number of entries 8
RT5
All leaf switches have unique VRF RD
(VSX primary RD and VSX secondary RD are different)
Single unique RT5 entry from each leaf VTEP
sourcing the same subnet
RT5 RD = VTEP_L0:VRF-ID
Unique RD

## Slide 21: MP-BGP L2VPN EVPN route-type 5
Spine-1: RT5 – IP prefix route (subnet advertisement)
6300F-5-spine1# show bgp l2vpn evpn route-type 5
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Total number of entries 8
RT5
When Leaf2-A and Leaf2-B have same VRF RD
If Leaf2-A and Leaf2-B have same VRF RD
then there is an election of a best route among two entries advertised from each logical VSX VTEP:
One entry coming from VSX primary (preferred due to lowest router-ID)
One entry coming from VSX secondary
best
RT5 RD = VTEP_L1:VRF-ID
Same RD example

## Slide 22
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-A Configuration
192.168.110.0/31
Leaf1-A
VRFs / EVPN / Common VRF RD option
vrf VRF1
rd 192.168.11.3:1
route-target export 65001:1 evpn
route-target import 65001:1 evpn
vrf VRF2
rd 192.168.11.3:2
route-target export 65001:2 evpn
route-target import 65001:2 evpn
!
evpn
vlan 10
rd auto
route-target export 65001:10
route-target import 65001:10
redistribute host-route
vlan 11
rd auto
route-target export 65001:11
route-target import 65001:11
redistribute host-route
vlan 20
rd auto
route-target export auto
route-target import auto
redistribute host-route
VLAN 2
VLAN 2
RD is common per VRF between VSX nodes Recommendation value: [L1:VRF_ID]
RT can be set to [AS_number:VLAN_ID]
RT proposal: [AS_number:VRF_ID]
RD auto is: [VTEP_L1:VLAN_ID]
redistribute host-route is used to advertise /32 host routes to remote VTEPs
Example: 10.1.10.10/32 is connected to Leaf1-A/Leaf1-B
10.1.12.10/32 is connected to Leaf2-A/Leaf2-B
This command is required as the same subnet is spread across multiple VTEPs.
Without host routes, a remote VTEP would not be aware of the correct destination VTEP to send traffic to.
RT can be set to auto
Host-route injection

## Slide 23
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-A Configuration
192.168.110.0/31
Leaf1-A
VRFs / EVPN / Distinct VRF RD option
vrf VRF1
rd 192.168.1.3:1
route-target export 65001:1 evpn
route-target import 65001:1 evpn
vrf VRF2
rd 192.168.1.3:2
route-target export 65001:2 evpn
route-target import 65001:2 evpn
!
evpn
vlan 10
rd auto
route-target export 65001:10
route-target import 65001:10
redistribute host-route
vlan 11
rd auto
route-target export 65001:11
route-target import 65001:11
redistribute host-route
vlan 20
rd auto
route-target export auto
route-target import auto
redistribute host-route
VLAN 2
VLAN 2
RD is unique per VRF for each VSX nodes Recommendation value: [L0:VRF_ID]
RT can be set to [AS_number:VLAN_ID]
RT proposal: [AS_number:VRF_ID]
RD auto is: [VTEP_L1:VLAN_ID]
redistribute host-route is used to advertise /32 host routes to remote VTEPs
Example: 10.1.10.10/32 is connected to Leaf1-A/Leaf1-B
10.1.12.10/32 is connected to Leaf2-A/Leaf2-B
This command is required as the same subnet is spread across multiple VTEPs.
Without host routes, a remote VTEP would not be aware of the correct destination VTEP to send traffic to.
RT can be set to auto
Host-route injection

## Slide 24
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-A Configuration
192.168.110.0/31
Leaf1-A
Endpoint SVIs / DHCP relay
interface vlan 10
vsx-sync active-gateways
vrf attach VRF1
ip mtu 9000
ip address 10.1.10.1/24
active-gateway ip mac 12:00:00:00:01:00
active-gateway ip 10.1.10.1
ip helper-address 192.168.3.242 vrf default
!
interface vlan 11
vsx-sync active-gateways
vrf attach VRF1
ip mtu 9000
ip address 10.1.11.1/24
active-gateway ip mac 12:00:00:00:01:00
active-gateway ip 10.1.11.1
!
interface vlan 20
vsx-sync active-gateways
vrf attach VRF2
description overlapping_subnet_test
ip mtu 9000
ip addess 10.2.20.1/24 or ip address 10.1.10.1/24
active-gateway ip mac 12:00:00:00:01:00
active-gateway ip 10.2.20.1 or active-gateway ip 10.1.10.1
ip helper-address 192.168.3.242 vrf default
!
ip source-interface dhcp_relay interface loopback0
dhcp-relay option 82 source-interface
VLAN 2
VLAN 2
Per VRF SVI
SVI IP = AG IP
Configuration simplification with same IP address for both SVI and Active Gateway is available since 10.6. In 10.5, SVI IP address was different from the anycast Active Gateway IP address.
Follow best practices for AG MAC value
DHCP relay in underlay VRF
DHCP relay sourcing
The dhcp-relay commands ensure that VTEP DHCP relay communication uses Lo0 to DHCP server and DHCP-relay option 82, sub-option 5, 11 and 151 are sent to the DHCP server using Lo0 IP address.
SVI10 10.1.10.2
SVI10 10.1.10.3
SVI10 10.1.10.4
SVI10 10.1.10.5
For overlapping subnet test
Notes: SVI IP = AG IP provides simplification and better IPAM.
SVI IP != AG IP provides easier troubleshooting while sourcing traffic from the SVI IP that is not common to all VTEPs.

## Slide 25
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-A Configuration
192.168.110.0/31
Leaf1-A
VXLAN interface / Virtual-MAC
interface vxlan 1
source ip 192.168.11.3
vxlan-counters aggregate
no shutdown
vni 10010
vlan 10
vni 10011
vlan 11
vni 10020
vlan 20
vni 100001
routing
vrf VRF1
vni 100002
routing
vrf VRF2
!
virtual-mac 02:00:00:00:01:00
VLAN 2
VLAN 2
Optional counters for VXLAN statistics
1-to-1 VLAN-VNI mapping
virtual-mac is required for symmetric IRB Distributed L3 Gateways deployments.
This is used as the Destination Router MAC for L3VNI routing to reach the egress VTEP router.
On VSX logical VTEPs, the value should be the same for both nodes of the VSX logical VTEP pair. Different virtual-macs should be used for other VTEPs or VSX VTEP pairs.
VXLAN tunnel source IP = anycast shared Loopback1
L3 VNI associated to vrf VRF1
VTEP virtual-MAC for L3VNI functionality
Virtual-MAC 02:00:00:00:01:00
Virtual-MAC 02:00:00:00:02:00
L3 VNI associated to vrf VRF2
L3VNI is optional. Deployment might not necessary required routing. For instance, L3 overlay
Routing might be done in some cases by a pair of Firewalls.

## Slide 26
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-A Configuration
192.168.110.0/31
Leaf1-A
Routing
router ospf 1
router-id 192.168.1.3
max-metric router-lsa include-stub on-startup 300
passive-interface default
trap-enable
area 0.0.0.0
!
ip prefix-list endpoint-VRF1 seq 10 permit 10.1.0.0/16 le 32
ip prefix-list endpoint-VRF2 seq 10 permit 10.2.0.0/16 le 32
route-map connected-bgp-VRF1 permit seq 10
match ip address prefix-list endpoint-VRF1
route-map connected-bgp-VRF2 permit seq 10
match ip address prefix-list endpoint-VRF2
!
router bgp 65001
bgp router-id 192.168.1.3
trap-enable
bgp fast-external-fallover
bgp log-neighbor-changes
bgp deterministic-med
bgp always-compare-med
neighbor spine-RR peer-group
neighbor spine-RR remote-as 65001
neighbor spine-RR description Spine and RR peer-group
neighbor spine-RR password ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
neighbor spine-RR fall-over
neighbor spine-RR update-source loopback 0
neighbor 192.168.1.1 peer-group spine-RR
neighbor 192.168.1.2 peer-group spine-RR
address-family l2vpn evpn
neighbor spine-RR send-community extended
neighbor 192.168.1.1 activate
neighbor 192.168.1.2 activate
exit-address-family
!
vrf VRF1
bgp router-id 192.168.1.3
address-family ipv4 unicast
redistribute connected route-map connected-bgp-VRF1
exit-address-family
!
vrf VRF2
bgp router-id 192.168.1.3
address-family ipv4 unicast
redistribute connected route-map connected-bgp-VRF2
exit-address-family
VLAN 2
VLAN 2
If used, must be the same in the BGP domain
best practice for HA during reboot
iBGP peering between loopbacks
Extended community is required
Control for RT5 route injection
Used to advertise EVPN Type 5 IP prefix routes

## Slide 27
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-B Configuration
192.168.110.0/31
Leaf1-B
VSX Configuration / VLANs
vrf KA
!
interface lag 256
vsx-sync vlans
no shutdown
description ISL
no routing
vlan trunk native 1 tag
vlan trunk allowed all
lacp mode active
interface 1/1/41
no shutdown
vrf attach KA
description 8325-1 1/1/41 for keepalive
ip address 192.168.0.1/31
interface 1/1/49
no shutdown
mtu 9198
description VSX ISL link
lag 256
interface 1/1/50
no shutdown
mtu 9198
description VSX ISL link
lag 256
!
vsx
system-mac 02:00:00:00:01:00
inter-switch-link lag 256
role primary
keepalive peer 192.168.0.0 source 192.168.0.1 vrf KA
vsx-sync aaa bgp copp-policy dhcp-relay dns evpn l2-vlan-mac-cfg-mode mclag-interfaces qos-global route-map sflow-global snmp ssh stp-global time vsx-global
!
vlan 2
vsx-sync
vlan 10
vsx-sync
vlan 11
vsx-sync
vlan 20
vsx-sync
VLAN 2
VLAN 2
Notes: Warning: vsx-sync ospf must be disabled to allow ospf configuration on different VLANs on VSX secondary of 8325-2.

## Slide 28
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-B Configuration
192.168.110.0/31
VSX LAGs to Servers
interface lag 1 multi-chassis
no shutdown
description 2930-3
no routing
vlan trunk native 1
vlan trunk allowed 10-11
lacp mode active
hash l4-src-dst
!
interface lag 2 multi-chassis
no shutdown
description 2930-4
no routing
vlan trunk native 1
vlan trunk allowed 20
lacp mode active
!
interface 1/1/1
no shutdown
mtu 9000
description Link to 2930-3 (50) - LAG 1 member
lag 1
!
interface 1/1/2
no shutdown
mtu 9000
description Link to 2930-3 (50) - LAG 2 member
lag 2
VLAN 2
VLAN 2
Leaf1-B

## Slide 29
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-B Configuration
192.168.110.0/31
ROPs to Spines / Loopbacks / Transit VLAN
interface 1/1/23
no shutdown
mtu 9198
ip mtu 9198
ip address 192.168.3.3/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
interface 1/1/24
no shutdown
mtu 9198
ip mtu 9198
ip address 192.168.3.11/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
!
interface loopback 0
ip address 192.168.1.4/32
ip ospf 1 area 0.0.0.0
!
interface loopback 1
ip address 192.168.11.3/32
ip ospf 1 area 0.0.0.0
!
interface vlan 2
ip mtu 9198
ip address 192.168.3.201/31
ip ospf 1 area 0.0.0.0
no ip ospf passive
ip ospf cost 50
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
VLAN 2
VLAN 2
Leaf1-B
Shared anycast Loopback1 of the VSX logical VTEP pair

## Slide 30
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-B Configuration
192.168.110.0/31
VRFs / EVPN
vrf VRF1
rd 192.168.1.4:1
route-target export 65001:1 evpn
route-target import 65001:1 evpn
vrf VRF2
rd 192.168.1.4:2
route-target export 65001:2 evpn
route-target import 65001:2 evpn
!
evpn
vlan 10
rd auto
route-target export 65001:10
route-target import 65001:10
redistribute host-route
vlan 11
rd auto
route-target export 65001:11
route-target import 65001:11
redistribute host-route
vlan 20
rd auto
route-target export auto
route-target import auto
redistribute host-route
VLAN 2
VLAN 2
Leaf1-B
RD is common per VRF between VSX nodes Recommendation value: [L1:VRF_ID]
RD auto is: [VTEP_L1:VLAN_ID]

## Slide 31
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-B Configuration
192.168.110.0/31
Endpoint SVIs / DHCP relay
interface vlan 10
vsx-sync active-gateways
vrf attach VRF1
ip mtu 9000
ip address 10.1.10.1/24
active-gateway ip mac 12:00:00:00:01:00
active-gateway ip 10.1.10.1
ip helper-address 192.168.3.242 vrf default
!
interface vlan 11
vsx-sync active-gateways
vrf attach VRF1
ip mtu 9000
ip address 10.1.11.1/24
active-gateway ip mac 12:00:00:00:01:00
active-gateway ip 10.1.11.1
!
interface vlan 20
vsx-sync active-gateways
vrf attach VRF2
description overlapping_subnet_test
ip mtu 9000
ip address 10.2.20.1/24
active-gateway ip mac 12:00:00:00:01:00
active-gateway ip 10.2.20.1
ip helper-address 192.168.3.242 vrf default
!
ip source-interface dhcp_relay interface loopback0
dhcp-relay option 82 source-interface
VLAN 2
VLAN 2
Leaf1-B
Unique SVI IP per switch

## Slide 32
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-B Configuration
192.168.110.0/31
VXLAN interface / Virtual-MAC
interface vxlan 1
source ip 192.168.11.3
vxlan-counters aggregate
no shutdown
vni 10010
vlan 10
vni 10011
vlan 11
vni 10020
vlan 20
vni 100001
routing
vrf VRF1
vni 100002
routing
vrf VRF2
!
virtual-mac 02:00:00:00:01:00
VLAN 2
VLAN 2
Leaf1-B
VXLAN tunnel source IP = anycast shared Loopback1
Same VTEP virtual-MAC between the VSX primary and the VSX secondary
Virtual-MAC 02:00:00:00:02:00
Virtual-MAC 02:00:00:00:01:00

## Slide 33
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-B Configuration
192.168.110.0/31
Routing
router ospf 1
router-id 192.168.1.4
max-metric router-lsa include-stub on-startup 300
passive-interface default
trap-enable
area 0.0.0.0
!
ip prefix-list endpoint-VRF1 seq 10 permit 10.1.0.0/16 le 32
ip prefix-list endpoint-VRF2 seq 10 permit 10.2.0.0/16 le 32
route-map connected-bgp-VRF1 permit seq 10
match ip address prefix-list endpoint-VRF1
route-map connected-bgp-VRF2 permit seq 10
match ip address prefix-list endpoint-VRF2
!
router bgp 65001
bgp router-id 192.168.1.4
trap-enable
bgp fast-external-fallover
bgp log-neighbor-changes
bgp deterministic-med
bgp always-compare-med
neighbor spine-RR peer-group
neighbor spine-RR remote-as 65001
neighbor spine-RR description Spine and RR peer-group
neighbor spine-RR password ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
neighbor spine-RR fall-over
neighbor spine-RR update-source loopback 0
neighbor 192.168.1.1 peer-group spine-RR
neighbor 192.168.1.2 peer-group spine-RR
address-family l2vpn evpn
neighbor spine-RR send-community extended
neighbor 192.168.1.1 activate
neighbor 192.168.1.2 activate
exit-address-family
!
vrf VRF1
bgp router-id 192.168.1.4
address-family ipv4 unicast
redistribute connected route-map connected-bgp-VRF1
exit-address-family
!
vrf VRF2
bgp router-id 192.168.1.4
address-family ipv4 unicast
redistribute connected route-map connected-bgp-VRF2
exit-address-family
VLAN 2
VLAN 2
Leaf1-B
Most BGP configuration inherited through vsx-sync
best practice for HA during reboot

## Slide 34: DC Border Leafs
Additional Configuration
SERVICES VRF
IPv4 IVRL (Inter VRFs Route Leaking)
ROPs, SERVICES VRF Transit VLAN

## Slide 35
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Border Leaf1-A Configuration
192.168.110.0/31
VRFs: SERVICES VRF, Route-Target import/export
VLAN 2
VLAN 2
Security for inter-VRF traffic is usually enforced on devices connecting the Border Leafs:
In this example, ACL can be applied on Campus 8400-1 or 8400-2
It could be transparent Firewalls between Border Leafs and Campus Cores.
Instead of 8400 Cores, it could be L3 Firewalls directly connecting Border Leafs.
1/1/51
1/1/51
vrf SERVICES
rd 192.168.1.3:5
address-family ipv4 unicast
route-target export 65001:5
route-target import 65001:1
route-target import 65001:2
exit-address-family
!
vrf VRF1
rd 192.168.1.3:1
route-target export 65001:1 evpn
route-target import 65001:1 evpn
address-family ipv4 unicast
route-target export 65001:1
route-target import 65001:5
exit-address-family
!
vrf VRF2
rd 192.168.1.3:2
route-target export 65001:2 evpn
route-target import 65001:2 evpn
address-family ipv4 unicast
route-target export 65001:2
route-target import 65001:5
!
Exporting VRF1
SERVICES VRF used for default route
Exporting SERVICES
Importing VRF1, VRF2
Importing SERVICES
Exporting VRF2
Importing SERVICES
Border Leaf
Leaf1-A

## Slide 36
eBGP SERVICES
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Border Leaf1-A Configuration
192.168.110.0/31
ROP, SERVICES VRF Transit VLAN/SVI
VLAN 2
VLAN 2
1/1/51
1/1/51
interface 1/1/51
no shutdown
mtu 9198
vrf attach SERVICES
description 8400-1 1/3/3
ip address 192.168.4.1/31
!
vlan 1150
vsx-sync
description overlay SERVICES VRF transit VLAN for border leaf
!
interface vlan 1150
vrf attach SERVICES
ip mtu 9198
ip address 192.168.150.0/31
!
ip aspath-list campus-as seq 10 permit .$
!
route-map border permit seq 10
match aspath-list campus-as
!
router bgp 65001
<…omitted for example…>
vrf SERVICES
bgp router-id 192.168.1.3
trap-enable
bgp fast-external-fallover
bgp log-neighbor-changes
neighbor campus-core-RR peer-group
neighbor campus-core-RR remote-as 65100
neighbor campus-core-RR description border-leaf peering with Campus core route-reflectors
neighbor vsx_peer peer-group
neighbor vsx_peer remote-as 65001
neighbor vsx_peer description vsx-peer iBGP peering for resiliency
neighbor 192.168.4.0 vsx-sync-exclude
neighbor 192.168.4.0 peer-group campus-core-RR
neighbor 192.168.150.1 vsx-sync-exclude
neighbor 192.168.150.1 peer-group vsx_peer
address-family ipv4 unicast
neighbor campus-core-RR send-community both
neighbor campus-core-RR soft-reconfiguration inbound
neighbor vsx_peer next-hop-self
neighbor vsx_peer route-map border in
neighbor vsx_peer route-map border out
neighbor vsx_peer send-community standard
neighbor vsx_peer soft-reconfiguration inbound
neighbor 192.168.4.0 activate
neighbor 192.168.150.1 activate
exit-address-family
Transit SVI
Border Leaf
Leaf1-A
VLAN 1150
iBGP SERVICES
L3 Link to Core-1 (8400-1)
Transit VLAN between border VSX peers
Campus peering
VSX peering
Filter out routes originated on the VTEP from EVPN to IPv4 AF

## Slide 37
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Border Leaf1-B Configuration
192.168.110.0/31
VRFs: SERVICES VRF, Route-Target import/export
VLAN 2
VLAN 2
1/1/51
1/1/51
vrf SERVICES
rd 192.168.1.4:5
address-family ipv4 unicast
route-target export 65001:5
route-target import 65001:1
route-target import 65001:2
exit-address-family
!
vrf VRF1
rd 192.168.1.4:1
route-target export 65001:1 evpn
route-target import 65001:1 evpn
address-family ipv4 unicast
route-target export 65001:1
route-target import 65001:5
exit-address-family
!
vrf VRF2
rd 192.168.1.4:2
route-target export 65001:2 evpn
route-target import 65001:2 evpn
address-family ipv4 unicast
route-target export 65001:2
route-target import 65001:5
!
Border Leaf
Leaf1-B

## Slide 38
eBGP SERVICES
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Border Leaf1-B Configuration
192.168.110.0/31
ROP, SERVICES VRF Transit VLAN/SVI
VLAN 2
VLAN 2
1/1/51
1/1/51
interface 1/1/51
no shutdown
mtu 9198
vrf attach SERVICES
description 8400-2 1/3/3
ip address 192.168.4.3/31
!
vlan 1150
vsx-sync
description overlay SERVICES VRF transit VLAN for border leaf
!
interface vlan 1150
vrf attach SERVICES
ip mtu 9198
ip address 192.168.150.1/31
!
ip aspath-list campus-as seq 10 permit .$
!
route-map border permit seq 10
match aspath-list campus-as
!
router bgp 65001
<…omitted for example…>
vrf SERVICES
bgp router-id 192.168.1.4
trap-enable
bgp fast-external-fallover
bgp log-neighbor-changes
neighbor campus-core-RR peer-group
neighbor campus-core-RR remote-as 65100
neighbor campus-core-RR description border-leaf peering with Campus core route-reflectors
neighbor vsx_peer peer-group
neighbor vsx_peer remote-as 65001
neighbor vsx_peer description vsx-peer iBGP peering for resiliency
neighbor 192.168.4.2 vsx-sync-exclude
neighbor 192.168.4.2 peer-group campus-core-RR
neighbor 192.168.150.0 vsx-sync-exclude
neighbor 192.168.150.0 peer-group vsx_peer
address-family ipv4 unicast
neighbor campus-core-RR send-community both
neighbor campus-core-RR soft-reconfiguration inbound
neighbor vsx_peer next-hop-self
neighbor vsx_peer route-map border in
neighbor vsx_peer route-map border out
neighbor vsx_peer send-community standard
neighbor vsx_peer soft-reconfiguration inbound
neighbor 192.168.4.2 activate
neighbor 192.168.150.0 activate
exit-address-family
Border Leaf
VLAN 1150
iBGP SERVICES
Leaf1-B

## Slide 39: Campus Cores Configuration
SERVICES VRF, ROPs, Loopbacks
Transit VLAN/SVI, OSPF
iBGP peering with other RR
eBGP peering with DC Border Leaf
Default route

## Slide 40
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
vmnic0
vmnic1
vmnic3
vmnic2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
vmnic6
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
vmnic0
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
1/1/22
VLAN 2
VLAN 2
1/3/1
1/8/1
1/3/1
1/8/1
LAG200
8400-2
15.136.40.236
L0: 192.168.2.2
L10: 192.168.200.5
1/3/3
1/3/3
1/1/51
1/1/51
1/3/3
1/3/3
6300-4
15.136.40.244
1/1/9
192.168.4.0/31
192.168.4.2/31
8400-1
15.136.40.235
L0: 192.168.2.1
L10: 192.168.200.1
Core-1 Configuration
VRF / ROPs to Leafs / Loopback / OSPF
vrf SERVICES
!
vlan 1156
description SERVICES transit VLAN
!
interface lag 200
no shutdown
no routing
vlan trunk native 1
vlan trunk allowed 1156
lacp mode active
!
interface 1/3/1
no shutdown
mtu 9198
lag 200
!
interface 1/3/3
no shutdown
mtu 9198
vrf attach SERVICES
description 8325-1 1/1/51
ip address 192.168.4.0/31
!
interface 1/8/1
no shutdown
mtu 9198
lag 200
!
interface loopback 0
ip address 192.168.2.1/32
ip ospf 1 area 0.0.0.0
!
interface loopback 10
vrf attach SERVICES
ip address 192.168.200.1/30
ip ospf 15 area 0.0.0.0
!
interface vlan 1156
vrf attach SERVICES
ip mtu 9198
ip address 192.168.156.0/31
ip ospf 15 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY17dlU3LitKLwE+4EU4v8nuBQAAABt51nkM
router ospf 15 vrf SERVICES
router-id 192.168.2.1
max-metric router-lsa include-stub on-startup
passive-interface default
graceful-restart restart-interval 660
area 0.0.0.0
L3 link to DC border-leaf 8325-1 for SERVICES VRF
Core-1
SERVICES VRF (ex: containing default route)
Campus IGP and DC IGP are separated. No OSPF peering between Campus and DC.
SERVICES transit VLAN
Interconnection to Core-2
LAG to Core-2
Interconnection to Core-2
SERVICES VRF Transit SVI
eBGP SERVICES
eBGP SERVICES
VLAN 1156
eBGP SERVICES
SERVICES VRF Loopback

## Slide 41: Core-1 Configuration
1/1/49
1/1/49
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/25
1/1/26
1/1/23
1/1/1
1/1/2
49
50
192.168.3.0/31
192.168.0.0/31
LAG 1
VLAN 2
1/3/1
1/8/1
1/3/1
1/8/1
LAG200
8400-2
15.136.40.236
L0: 192.168.2.2
L10: 192.168.200.5
1/3/3
1/3/3
1/1/51
1/1/51
1/3/3
1/3/3
6300-4
15.136.40.244
1/1/9
192.168.4.0/31
192.168.4.2/31
8400-1
15.136.40.235
L0: 192.168.2.1
L10: 192.168.200.1
Core-1
eBGP SERVICES
eBGP SERVICES
VLAN 1156
eBGP SERVICES
ip prefix-list default seq 10 permit 0.0.0.0/32
!
route-map campus-dc permit seq 10
match ip address prefix-list default
route-map campus-dc deny seq 20
!
router bgp 65100
bgp router-id 192.168.2.1
trap-enable
bgp fast-external-fallover
bgp log-neighbor-changes
bgp deterministic-med
bgp always-compare-med
bgp cluster-id 192.168.2.0
< snip – default VRF BGP peering configuration >
…
vrf SERVICES
bgp router-id 192.168.2.1
trap-enable
bgp fast-external-fallover
bgp log-neighbor-changes
neighbor DC-border peer-group
neighbor DC-border remote-as 65001
neighbor DC-border description peering with DC border leafs
neighbor RR peer-group
neighbor RR remote-as 65100
neighbor RR description peering with other RR
neighbor RR password ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY17dlU3LitKLwE+4EU4v8nuBQAAABt51nkM
neighbor RR fall-over
neighbor RR update-source loopback 10
neighbor 192.168.4.1 peer-group DC-border
neighbor 192.168.200.5 peer-group RR
address-family ipv4 unicast
neighbor DC-border default-originate
neighbor DC-border route-map campus-dc out
neighbor DC-border send-community standard
neighbor DC-border soft-reconfiguration inbound
neighbor RR next-hop-self
neighbor RR send-community standard
neighbor RR soft-reconfiguration inbound
neighbor 192.168.4.1 activate
neighbor 192.168.200.5 activate
redistribute connected
redistribute static
exit-address-family
!
ip route 0.0.0.0/0 192.168.199.2 vrf SERVICES
BGP Routing
Default route injection for testing
eBGP to DC border-leaf
Originating Default route
iBGP to Core-2
Next-hop-self to iBGP peers
Outbound filtering for default only
Default route prefix
Default route only route-map

## Slide 42
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
vmnic0
vmnic1
vmnic3
vmnic2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
vmnic6
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
vmnic0
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
1/1/22
VLAN 2
VLAN 2
1/3/1
1/8/1
1/3/1
1/8/1
LAG200
8400-2
15.136.40.236
L0: 192.168.2.2
L10: 192.168.200.5
1/3/3
1/3/3
1/1/51
1/1/51
1/3/3
1/3/3
6300-4
15.136.40.244
1/1/9
192.168.4.0/31
192.168.4.2/31
8400-1
15.136.40.235
L0: 192.168.2.1
L10: 192.168.200.1
Core-2 Configuration
VRF / ROPs to Leafs / Loopback / IGP
vrf SERVICES
!
vlan 1156
description SERVICES transit VLAN
!
interface lag 200
no shutdown
no routing
vlan trunk native 1
vlan trunk allowed 1156
lacp mode active
!
interface 1/3/1
no shutdown
mtu 9198
lag 200
!
interface 1/3/3
no shutdown
mtu 9198
vrf attach SERVICES
description 8325-2 1/1/51
ip address 192.168.4.2/31
!
interface 1/8/1
no shutdown
mtu 9198
lag 200
!
interface loopback 0
ip address 192.168.2.2/32
ip ospf 1 area 0.0.0.0
!
interface loopback 10
vrf attach SERVICES
ip address 192.168.200.5/30
ip ospf 15 area 0.0.0.0
!
interface vlan 1156
vrf attach SERVICES
ip mtu 9198
ip address 192.168.156.1/31
ip ospf 15 area 0.0.0.0
no ip ospf passive
ip ospf network point-to-point
ip ospf authentication message-digest
ip ospf message-digest-key 1 md5 ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY0p5vpa77xnpPQEngEkpWjWBQAAAIouj7OC
router ospf 15 vrf SERVICES
router-id 192.168.2.1
max-metric router-lsa include-stub on-startup
passive-interface default
graceful-restart restart-interval 660
area 0.0.0.0
SERVICES VRF Loopback
L3 link to DC border-leaf 8325-2 for SERVICES VRF
SERVICES VRF (ex: containing default route)
Campus IGP and DC IGP are separated. No OSPF peering between Campus and DC.
SERVICES transit VLAN
Interconnection to Core-1
LAG to Core-1
Interconnection to Core-1
SERVICES VRF Transit SVI
eBGP SERVICES
eBGP SERVICES
VLAN 1156
eBGP SERVICES
Core-2

## Slide 43: Core-2 Configuration
1/1/49
1/1/49
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/25
1/1/26
1/1/23
1/1/1
1/1/2
49
50
192.168.3.0/31
192.168.0.0/31
LAG 1
VLAN 2
1/3/1
1/8/1
1/3/1
1/8/1
LAG200
8400-2
15.136.40.236
L0: 192.168.2.2
L10: 192.168.200.5
1/3/3
1/3/3
1/1/51
1/1/51
1/3/3
1/3/3
6300-4
15.136.40.244
1/1/9
192.168.4.0/31
192.168.4.2/31
8400-1
15.136.40.235
L0: 192.168.2.1
L10: 192.168.200.1
Core-1
eBGP SERVICES
eBGP SERVICES
VLAN 1156
eBGP SERVICES
ip prefix-list default seq 10 permit 0.0.0.0/32
!
route-map campus-dc permit seq 10
match ip address prefix-list default
route-map campus-dc deny seq 20
!
router bgp 65100
bgp router-id 192.168.2.2
trap-enable
bgp fast-external-fallover
bgp log-neighbor-changes
bgp deterministic-med
bgp always-compare-med
bgp cluster-id 192.168.2.0
< snip – default VRF BGP peering configuration >
…
vrf SERVICES
bgp router-id 192.168.2.2
trap-enable
bgp fast-external-fallover
bgp log-neighbor-changes
neighbor DC-border peer-group
neighbor DC-border remote-as 65001
neighbor DC-border description peering with DC border leafs
neighbor RR peer-group
neighbor RR remote-as 65100
neighbor RR description peering with other RR
neighbor RR password ciphertext AQBapUbZyuMyDkoDN0zeQbI8qY17dlU3LitKLwE+4EU4v8nuBQAAABt51nkM
neighbor RR fall-over
neighbor RR update-source loopback 10
neighbor 192.168.4.1 peer-group DC-border
neighbor 192.168.200.5 peer-group RR
address-family ipv4 unicast
neighbor DC-border default-originate
neighbor DC-border route-map campus-dc out
neighbor DC-border send-community standard
neighbor DC-border soft-reconfiguration inbound
neighbor RR next-hop-self
neighbor RR send-community standard
neighbor RR soft-reconfiguration inbound
neighbor 192.168.4.3 activate
neighbor 192.168.200.1 activate
redistribute connected
redistribute static
exit-address-family
!
BGP Routing
eBGP to DC border-leaf
Originating Default route
iBGP to Core-2
Next-hop-self to iBGP peers
Outbound filtering for default only
Default route prefix
Default route only route-map

## Slide 44: Configuration files
All devices

## Slide 45
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Configuration files
192.168.110.0/31
Double-click on CFG file
VLAN 2
VLAN 2
Leaf1-B
Leaf2-B
Leaf2-A
Spine-1
Spine-2
1/3/1
1/8/1
1/3/1
1/8/1
LAG200
8400-2
15.136.40.236
L0: 192.168.2.2
1/3/3
1/3/3
1/1/51
1/1/51
1/3/3
1/3/3
6300-4
15.136.40.244
1/1/9
192.168.4.0/31
192.168.4.2/31
8400-1
15.136.40.235
L0: 192.168.2.1
Leaf1-A
Core-2
Core-1

## Slide 46: Connectivity
Spines: show LLDP
6300F-5-spine1# show lldp neighbors
LLDP Neighbor Information
=========================
Total Neighbor Entries : 4
Total Neighbor Entries Deleted : 1
Total Neighbor Entries Dropped : 0
Total Neighbor Entries Aged-Out : 1
LOCAL-PORT CHASSIS-ID PORT-ID PORT-DESC TTL SYS-NAME
------------------------------------------------------------------------------------------
1/1/25 54:80:28:fd:f3:00 1/1/23 1/1/23 120 8325-1
1/1/26 54:80:28:fc:5c:00 1/1/23 1/1/23 120 8325-2
1/1/27 54:80:28:fc:ac:00 1/1/23 1/1/23 120 8325-3
1/1/28 54:80:28:fd:42:00 1/1/23 1/1/23 120 8325-4
6300F-6-spine2# show lldp neighbors
LLDP Neighbor Information
=========================
Total Neighbor Entries : 4
Total Neighbor Entries Deleted : 3
Total Neighbor Entries Dropped : 0
Total Neighbor Entries Aged-Out : 3
LOCAL-PORT CHASSIS-ID PORT-ID PORT-DESC TTL SYS-NAME
------------------------------------------------------------------------------------------
1/1/25 54:80:28:fd:f3:00 1/1/24 1/1/24 120 8325-1
1/1/26 54:80:28:fc:5c:00 1/1/24 1/1/24 120 8325-2
1/1/27 54:80:28:fc:ac:00 1/1/24 1/1/24 120 8325-3
1/1/28 54:80:28:fd:42:00 1/1/24 1/1/24 120 8325-4

## Slide 47: Underlay OSPF routing
Spine-1
6300F-5-spine1# show ip ospf neighbors
OSPF Process ID 1 VRF default
==============================
Total Number of Neighbors: 4
Neighbor ID Priority State Nbr Address Interface
-------------------------------------------------------------------------
192.168.1.3 n/a FULL 192.168.3.1 1/1/25
192.168.1.4 n/a FULL 192.168.3.3 1/1/26
192.168.1.5 n/a FULL 192.168.3.5 1/1/27
192.168.1.6 n/a FULL 192.168.3.7 1/1/28
6300F-5-spine1# show ip route ospf
Displaying ipv4 routes selected for forwarding
'[x/y]' denotes [distance/metric]
192.168.1.2/32, vrf default
via 192.168.3.7, [110/8], ospf
via 192.168.3.5, [110/8], ospf
192.168.1.3/32, vrf default
via 192.168.3.1, [110/10], ospf
192.168.1.4/32, vrf default
via 192.168.3.3, [110/10], ospf
192.168.1.5/32, vrf default
via 192.168.3.5, [110/4], ospf
192.168.1.6/32, vrf default
via 192.168.3.7, [110/4], ospf
192.168.3.8/31, vrf default
via 192.168.3.7, [110/18], ospf
via 192.168.3.5, [110/18], ospf
192.168.3.10/31, vrf default
via 192.168.3.7, [110/18], ospf
via 192.168.3.5, [110/18], ospf
192.168.3.12/31, vrf default
via 192.168.3.5, [110/8], ospf
192.168.3.14/31, vrf default
via 192.168.3.7, [110/8], ospf
192.168.3.200/31, vrf default
via 192.168.3.3, [110/60], ospf
via 192.168.3.1, [110/60], ospf
192.168.3.202/31, vrf default
via 192.168.3.7, [110/54], ospf
via 192.168.3.5, [110/54], ospf
192.168.11.3/32, vrf default
via 192.168.3.3, [110/10], ospf
via 192.168.3.1, [110/10], ospf
192.168.11.5/32, vrf default
via 192.168.3.7, [110/4], ospf
via 192.168.3.5, [110/4], ospf
ECMP to logical VTEP anycast IP

## Slide 48: Underlay OSPF routing
Spine-2
6300F-6-spine2# show ip ospf neighbors
OSPF Process ID 1 VRF default
==============================
Total Number of Neighbors: 4
Neighbor ID Priority State Nbr Address Interface
-------------------------------------------------------------------------
192.168.1.3 n/a FULL 192.168.3.9 1/1/25
192.168.1.4 n/a FULL 192.168.3.11 1/1/26
192.168.1.5 n/a FULL 192.168.3.13 1/1/27
192.168.1.6 n/a FULL 192.168.3.15 1/1/28
6300F-6-spine2# show ip route ospf
Displaying ipv4 routes selected for forwarding
'[x/y]' denotes [distance/metric]
192.168.1.1/32, vrf default
via 192.168.3.13, [110/8], ospf
via 192.168.3.15, [110/8], ospf
192.168.1.3/32, vrf default
via 192.168.3.9, [110/10], ospf
192.168.1.4/32, vrf default
via 192.168.3.11, [110/10], ospf
192.168.1.5/32, vrf default
via 192.168.3.13, [110/4], ospf
192.168.1.6/32, vrf default
via 192.168.3.15, [110/4], ospf
192.168.3.0/31, vrf default
via 192.168.3.13, [110/18], ospf
via 192.168.3.15, [110/18], ospf
192.168.3.2/31, vrf default
via 192.168.3.13, [110/18], ospf
via 192.168.3.15, [110/18], ospf
192.168.3.4/31, vrf default
via 192.168.3.13, [110/8], ospf
192.168.3.6/31, vrf default
via 192.168.3.15, [110/8], ospf
192.168.3.200/31, vrf default
via 192.168.3.11, [110/60], ospf
via 192.168.3.9, [110/60], ospf
192.168.3.202/31, vrf default
via 192.168.3.13, [110/54], ospf
via 192.168.3.15, [110/54], ospf
192.168.3.240/29, vrf default
via 192.168.3.13, [110/108], ospf
via 192.168.3.15, [110/108], ospf
192.168.11.3/32, vrf default
via 192.168.3.11, [110/10], ospf
via 192.168.3.9, [110/10], ospf
192.168.11.5/32, vrf default
via 192.168.3.13, [110/4], ospf
via 192.168.3.15, [110/4], ospf
DHCP relay server

## Slide 49: Underlay OSPF routing
Leaf1-A
8325-1# show ip ospf neighbors
OSPF Process ID 1 VRF default
==============================
Total Number of Neighbors: 3
Neighbor ID Priority State Nbr Address Interface
-------------------------------------------------------------------------
192.168.1.1 n/a FULL 192.168.3.0 1/1/23
192.168.1.2 n/a FULL 192.168.3.8 1/1/24
192.168.1.4 n/a FULL 192.168.3.201 vlan2
8325-1# show ip route ospf
Displaying ipv4 routes selected for forwarding
'[x/y]' denotes [distance/metric]
192.168.1.1/32, vrf default
via 192.168.3.0, [110/10], ospf
192.168.1.2/32, vrf default
via 192.168.3.8, [110/10], ospf
192.168.1.4/32, vrf default
via 192.168.3.8, [110/20], ospf
via 192.168.3.0, [110/20], ospf
192.168.1.5/32, vrf default
via 192.168.3.8, [110/14], ospf
via 192.168.3.0, [110/14], ospf
192.168.1.6/32, vrf default
via 192.168.3.8, [110/14], ospf
via 192.168.3.0, [110/14], ospf
192.168.3.2/31, vrf default
via 192.168.3.0, [110/20], ospf
192.168.3.4/31, vrf default
via 192.168.3.0, [110/14], ospf
192.168.3.6/31, vrf default
via 192.168.3.0, [110/14], ospf
192.168.3.10/31, vrf default
via 192.168.3.8, [110/20], ospf
192.168.3.12/31, vrf default
via 192.168.3.8, [110/14], ospf
192.168.3.14/31, vrf default
via 192.168.3.8, [110/14], ospf
192.168.3.202/31, vrf default
via 192.168.3.8, [110/64], ospf
via 192.168.3.0, [110/64], ospf
192.168.3.240/29, vrf default
via 192.168.3.0, [110/110], ospf
192.168.11.5/32, vrf default
via 192.168.3.8, [110/14], ospf
via 192.168.3.0, [110/14], ospf
DHCP relay server
Anycast L1 VSX VTEP2

## Slide 50: Underlay OSPF routing
Leaf1-B
8325-2# show ip ospf neighbors
OSPF Process ID 1 VRF default
==============================
Total Number of Neighbors: 3
Neighbor ID Priority State Nbr Address Interface
-------------------------------------------------------------------------
192.168.1.1 n/a FULL 192.168.3.2 1/1/23
192.168.1.2 n/a FULL 192.168.3.10 1/1/24
192.168.1.3 n/a FULL 192.168.3.200 vlan2
8325-2# show ip route ospf
Displaying ipv4 routes selected for forwarding
'[x/y]' denotes [distance/metric]
192.168.1.1/32, vrf default
via 192.168.3.2, [110/10], ospf
192.168.1.2/32, vrf default
via 192.168.3.10, [110/10], ospf
192.168.1.3/32, vrf default
via 192.168.3.2, [110/20], ospf
via 192.168.3.10, [110/20], ospf
192.168.1.5/32, vrf default
via 192.168.3.2, [110/14], ospf
via 192.168.3.10, [110/14], ospf
192.168.1.6/32, vrf default
via 192.168.3.2, [110/14], ospf
via 192.168.3.10, [110/14], ospf
192.168.3.0/31, vrf default
via 192.168.3.2, [110/20], ospf
192.168.3.4/31, vrf default
via 192.168.3.2, [110/14], ospf
192.168.3.6/31, vrf default
via 192.168.3.2, [110/14], ospf
192.168.3.8/31, vrf default
via 192.168.3.10, [110/20], ospf
192.168.3.12/31, vrf default
via 192.168.3.10, [110/14], ospf
192.168.3.14/31, vrf default
via 192.168.3.10, [110/14], ospf
192.168.3.202/31, vrf default
via 192.168.3.2, [110/64], ospf
via 192.168.3.10, [110/64], ospf
192.168.3.240/29, vrf default
via 192.168.3.2, [110/110], ospf
192.168.11.5/32, vrf default
via 192.168.3.2, [110/14], ospf
via 192.168.3.10, [110/14], ospf
DHCP relay server

## Slide 51: Underlay OSPF routing
Leaf2-A
8325-3# show ip ospf neighbors
OSPF Process ID 1 VRF default
==============================
Total Number of Neighbors: 3
Neighbor ID Priority State Nbr Address Interface
-------------------------------------------------------------------------
192.168.1.1 n/a FULL 192.168.3.4 1/1/23
192.168.1.2 n/a FULL 192.168.3.12 1/1/24
192.168.1.6 n/a FULL 192.168.3.203 vlan2
8325-3# show ip route ospf
Displaying ipv4 routes selected for forwarding
'[x/y]' denotes [distance/metric]
192.168.1.1/32, vrf default
via 192.168.3.4, [110/4], ospf
192.168.1.2/32, vrf default
via 192.168.3.12, [110/4], ospf
192.168.1.3/32, vrf default
via 192.168.3.4, [110/14], ospf
via 192.168.3.12, [110/14], ospf
192.168.1.4/32, vrf default
via 192.168.3.4, [110/14], ospf
via 192.168.3.12, [110/14], ospf
192.168.1.6/32, vrf default
via 192.168.3.4, [110/8], ospf
via 192.168.3.12, [110/8], ospf
192.168.3.0/31, vrf default
via 192.168.3.4, [110/14], ospf
192.168.3.2/31, vrf default
via 192.168.3.4, [110/14], ospf
192.168.3.6/31, vrf default
via 192.168.3.4, [110/8], ospf
192.168.3.8/31, vrf default
via 192.168.3.12, [110/14], ospf
192.168.3.10/31, vrf default
via 192.168.3.12, [110/14], ospf
192.168.3.14/31, vrf default
via 192.168.3.12, [110/8], ospf
192.168.3.200/31, vrf default
via 192.168.3.4, [110/64], ospf
via 192.168.3.12, [110/64], ospf
192.168.3.240/29, vrf default
via 192.168.3.4, [110/104], ospf
192.168.11.3/32, vrf default
via 192.168.3.4, [110/14], ospf
via 192.168.3.12, [110/14], ospf
DHCP relay server

## Slide 52: Underlay OSPF routing
Leaf2-B
8325-4# show ip ospf neighbors
OSPF Process ID 1 VRF default
==============================
Total Number of Neighbors: 3
Neighbor ID Priority State Nbr Address Interface
-------------------------------------------------------------------------
192.168.1.1 n/a FULL 192.168.3.6 1/1/23
192.168.1.2 n/a FULL 192.168.3.14 1/1/24
192.168.1.5 n/a FULL 192.168.3.202 vlan2
8325-4# show ip route ospf
Displaying ipv4 routes selected for forwarding
'[x/y]' denotes [distance/metric]
192.168.1.1/32, vrf default
via 192.168.3.6, [110/4], ospf
192.168.1.2/32, vrf default
via 192.168.3.14, [110/4], ospf
192.168.1.3/32, vrf default
via 192.168.3.6, [110/14], ospf
via 192.168.3.14, [110/14], ospf
192.168.1.4/32, vrf default
via 192.168.3.6, [110/14], ospf
via 192.168.3.14, [110/14], ospf
192.168.1.5/32, vrf default
via 192.168.3.6, [110/8], ospf
via 192.168.3.14, [110/8], ospf
192.168.3.0/31, vrf default
via 192.168.3.6, [110/14], ospf
192.168.3.2/31, vrf default
via 192.168.3.6, [110/14], ospf
192.168.3.4/31, vrf default
via 192.168.3.6, [110/8], ospf
192.168.3.8/31, vrf default
via 192.168.3.14, [110/14], ospf
192.168.3.10/31, vrf default
via 192.168.3.14, [110/14], ospf
192.168.3.12/31, vrf default
via 192.168.3.14, [110/8], ospf
192.168.3.200/31, vrf default
via 192.168.3.6, [110/64], ospf
via 192.168.3.14, [110/64], ospf
192.168.3.240/29, vrf default
via 192.168.3.6, [110/104], ospf
192.168.11.3/32, vrf default
via 192.168.3.6, [110/14], ospf
via 192.168.3.14, [110/14], ospf
DHCP relay server

## Slide 53: BGP sessions

## Slide 54: MP-BGP sessions
Spine-1
6300F-5-spine1# show bgp all-vrf all summary
VRF : default
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.1
Peers : 4 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Address-family : IPv4 Unicast
-----------------------------
Address-family : IPv6 Unicast
-----------------------------
Address-family : L2VPN EVPN
-----------------------------
Neighbor Remote-AS MsgRcvd MsgSent Up/Down Time State AdminStatus
192.168.1.3 65001 6066 7095 00h:01m:43s Established Up
192.168.1.4 65001 5994 7168 00h:01m:47s Established Up
192.168.1.5 65001 5940 7094 00h:01m:51s Established Up
192.168.1.6 65001 5946 6944 00h:01m:56s Established Up
All VSX nodes have their own control-plane

## Slide 55: MP-BGP sessions
Spine-2
6300F-6-spine2# show bgp all-vrf all summary
VRF : default
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.2
Peers : 4 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Address-family : IPv4 Unicast
-----------------------------
Address-family : IPv6 Unicast
-----------------------------
Address-family : L2VPN EVPN
-----------------------------
Neighbor Remote-AS MsgRcvd MsgSent Up/Down Time State AdminStatus
192.168.1.3 65001 6075 7116 00h:02m:31s Established Up
192.168.1.4 65001 6014 7171 00h:02m:35s Established Up
192.168.1.5 65001 5947 7085 00h:02m:39s Established Up
192.168.1.6 65001 5963 6979 00h:02m:44s Established Up
All VSX nodes have their own control-plane

## Slide 56: MP-BGP sessions
Leaf1-A
8325-1# show bgp all-vrf all summary
VRF : default
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.3
Peers : 2 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Confederation Id : 0
Address-family : IPv4 Unicast
-----------------------------
Address-family : IPv6 Unicast
-----------------------------
Address-family : L2VPN EVPN
-----------------------------
Neighbor Remote-AS MsgRcvd MsgSent Up/Down Time State AdminStatus
192.168.1.1 65001 139 108 01h:16m:30s Established Up
192.168.1.2 65001 137 110 01h:16m:25s Established Up
VRF : SERVICES
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.3
Peers : 2 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Confederation Id : 0
Address-family : IPv4 Unicast
-----------------------------
Neighbor Remote-AS MsgRcvd MsgSent Up/Down Time State AdminStatus
192.168.4.0 65100 94 94 01h:16m:32s Established Up
192.168.150.1 65001 92 92 01h:16m:25s Established Up
Address-family : IPv6 Unicast
-----------------------------
VRF : VRF1
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.3
Peers : 0 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Confederation Id : 0
Address-family : IPv4 Unicast
-----------------------------
Address-family : IPv6 Unicast
-----------------------------
VRF : VRF2
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.3
Peers : 0 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Confederation Id : 0
Address-family : IPv4 Unicast
-----------------------------
Address-family : IPv6 Unicast
-----------------------------
Each VSX node peers with all spines
VSX peer for SERVICES VRF
Campus Core peer for SERVICES VRF

## Slide 57: MP-BGP sessions
Leaf1-B
8325-2# show bgp all-vrf all summary
VRF : default
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.4
Peers : 2 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Confederation Id : 0
Address-family : IPv4 Unicast
-----------------------------
Address-family : IPv6 Unicast
-----------------------------
Address-family : L2VPN EVPN
-----------------------------
Neighbor Remote-AS MsgRcvd MsgSent Up/Down Time State AdminStatus
192.168.1.1 65001 149 112 01h:19m:38s Established Up
192.168.1.2 65001 153 111 01h:19m:34s Established Up
VRF : SERVICES
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.4
Peers : 2 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Confederation Id : 0
Address-family : IPv4 Unicast
-----------------------------
Neighbor Remote-AS MsgRcvd MsgSent Up/Down Time State AdminStatus
192.168.4.2 65100 103 98 01h:19m:47s Established Up
192.168.150.0 65001 96 96 01h:19m:40s Established Up
Address-family : IPv6 Unicast
-----------------------------
VRF : VRF1
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.4
Peers : 0 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Confederation Id : 0
Address-family : IPv4 Unicast
-----------------------------
Address-family : IPv6 Unicast
-----------------------------
VRF : VRF2
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.4
Peers : 0 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Confederation Id : 0
Address-family : IPv4 Unicast
-----------------------------
Address-family : IPv6 Unicast
-----------------------------
Each VSX node peers with all spines
VSX peer for SERVICES VRF
Campus Core peer for SERVICES VRF

## Slide 58: MP-BGP sessions
Campus Cores
8400-1# show bgp vrf SERVICES all summary
VRF : SERVICES
BGP Summary
-----------
Local AS : 65100 BGP Router Identifier : 192.168.2.1
Peers : 2 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Address-family : IPv4 Unicast
-----------------------------
Neighbor Remote-AS MsgRcvd MsgSent Up/Down Time State AdminStatus
192.168.4.1 65001 12951 12931 17h:25m:31s Established Up
192.168.200.5 65100 11688 11675 00m:01w:00d Established Up
Address-family : IPv6 Unicast
-----------------------------
Core-1
8400-2# show bgp vrf SERVICES all summary
VRF : SERVICES
BGP Summary
-----------
Local AS : 65100 BGP Router Identifier : 192.168.2.1
Peers : 2 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Address-family : IPv4 Unicast
-----------------------------
Neighbor Remote-AS MsgRcvd MsgSent Up/Down Time State AdminStatus
192.168.4.1 65001 12951 12931 17h:25m:31s Established Up
192.168.200.5 65100 11688 11675 00m:01w:00d Established Up
Address-family : IPv6 Unicast
-----------------------------
Core-2
Leaf1-A peering
Core-2 peering
Leaf1-A peering
Core-1 peering

## Slide 59: BGP EVPN route-types

## Slide 60: BGP decision tree reminder
Step | BGP attribute / criteria | Attribute type | Comment
1 | next hop reachability |  | Next-hop in routing table (ex: in OSPF)
2 | highest weight | proprietary | local to router
3 | highest local-preference | discretionary | Globally defined within the AS. Default LP=100
4 | router originated |  | route locally originated by itself (like redistribution or route leaking)
5 | shortest AS-PATH length | Mandatory | Can be skipped with bgp bestpath as-path ignore. Selection can be stopped with bgp bestpath as-path multipath-relax
6 | lowest origin type | Mandatory | IGP < EGP < incomplete
7 | lowest Multi-Exit-Discriminator | Optional non-transitive | MEDs are compared if routes came from the same remote AS or if bgp always-compare-med is enabled
8 | eBGP preferred over iBGP or confederation |  | confederation paths are treated as iBGP
9 | lowest IGP cost to the BGP next-hop |  | closest IGP neighbor

## Slide 61: BGP decision tree reminder
Cont.
Step | BGP attribute / criteria | Attribute type | Comment
10 | Oldest eBGP route | N/A | most stable path
11 | lowest router ID OR lowest originator ID (in case of RR) | Mandatory | 
12 | lowest cluster list length | Optional non-transitive | 
13 | lowest BGP peer IP address |  | IPv6 is preferred over IPv4

## Slide 62: MP-BGP L2VPN EVPN peering
Spine-1 and Spine-2 peering uptime
6300F-5-spine1# show bgp l2vpn evpn summary
VRF : default
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.1
Peers : 4 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Neighbor Remote-AS MsgRcvd MsgSent Up/Down Time State AdminStatus
192.168.1.3 65001 11583 11561 03d:01h:11m Established Up
192.168.1.4 65001 11551 11602 06d:22h:55m Established Up
192.168.1.5 65001 11556 11593 06d:22h:23m Established Up
192.168.1.6 65001 11555 11609 06d:22h:23m Established Up
RT2
6300F-6-spine2# show bgp l2vpn evpn summary
VRF : default
BGP Summary
-----------
Local AS : 65001 BGP Router Identifier : 192.168.1.1
Peers : 4 Log Neighbor Changes : Yes
Cfg. Hold Time : 180 Cfg. Keep Alive : 60
Neighbor Remote-AS MsgRcvd MsgSent Up/Down Time State AdminStatus
192.168.1.3 65001 11600 11596 03d:01h:13m Established Up
192.168.1.4 65001 11562 11585 05d:01h:37m Established Up
192.168.1.5 65001 11567 11618 05d:01h:36m Established Up
192.168.1.6 65001 11568 11642 05d:01h:36m Established Up
BGP peering has been reset on purpose to show use-case with VSX primary having uptime lower than secondary. Following data are captured after convergence.
Notes: BGP peering has been reset on purpose to show use-case with VSX primary having uptime lower than secondary. Following data are captured after convergence.

## Slide 63: MP-BGP L2VPN EVPN route-type 3
Spine-1: RT3 - inclusive multicast route
6300F-5-spine1# show bgp l2vpn evpn route-type 3
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Total number of entries 12
RT3
used for automatic discovery of VTEPs and dynamic establishment of VXLAN tunnels.
best
Two RT3 entries from each logical VSX VTEP:
One entry coming from VSX primary (preferred due to lowest router-ID)
One entry coming from VSX secondary
best
VNI 10010
RT3 RD = VTEP_L1:VLAN-ID
Same RD

## Slide 64: MP-BGP L2VPN EVPN route-type 3
Leaf1-A (VSX lowest router-ID)
8325-1# show bgp l2vpn evpn route-type 3
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.3
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Total number of entries 9
RT3
One single RT3 entry per VNI on local VTEP, locally originated, best.
No other entries because this entry is originated from the VSX node having the lowest router-ID. It is the best route (decision tree up to router-ID criteria) reflected by Route-Reflectors and not reflected back to the sourcing RR-client.
Two RT3 entries per VNI from remote VTEP:
One entry reflected from RR1 (Spine-1) (preferred due to RR1 lowest originator-ID)
One entry reflected from RR2 (Spine-2)
best
best
VNI 10010
RT3 RD = VTEP_L1:VLAN-ID
Same RD

## Slide 65: MP-BGP L2VPN EVPN route-type 3
Leaf1-B (VSX highest router-ID)
8325-2# show bgp l2vpn evpn route-type 3
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.4
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Total number of entries 15
RT3
RT3 entry locally originated on the local VTEP, best
Two RT3 entries per VNI from remote VTEP:
One entry reflected from RR1 (Spine-1) (preferred due to RR1 lowest originator-ID)
One entry reflected from RR2 (spine-2)
best
best
VNI 10010
RT3 entry from the VSX peer (with lowest router-ID) of same the logical VSX VTEP, reflected by RR1 (Spine-1)
RT3 entry from the VSX peer (with lowest router-ID) of same the logical VSX VTEP, reflected by RR2 (spine-2)
RT3 RD = VTEP_L1:VLAN-ID
Same RD
Same RD

## Slide 66: EVPN route-type 2
Spine-1: RT2 – MAC/IP route (hosts)
6300F-5-spine1# sh bgp l2vpn evpn route-type 2
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 72
RT2
RT2 RD = VTEP_L1:VLAN-ID
best
Two RT2 entries from each logical VSX VTEP:
One entry coming from VSX primary (preferred due to lowest router-ID)
One entry coming from VSX secondary
Same RD
MAC only route-type 2: mandatory
MAC-IP route-type 2: optional
Notes: The MAC and IP, type-2 route is optional and advertised separately from the MAC only type-2 route, which is mandatory.
This is covering cases like ARP clearance, or aging, that will remove MAC-IP while keeping the MAC only route.

## Slide 67: EVPN route-type 2
Spine-1: RT2 – MAC/IP route (hosts)
6300F-5-spine1# sh bgp l2vpn evpn route-type 2
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Total number of entries 60
RT2
RT2 RD = VTEP_L1:VLAN-ID
best
Two RT2 entries from each logical VSX VTEP:
One entry coming from VSX primary (preferred due to lowest router-ID)
One entry coming from VSX secondary
Same RD
MAC only route-type 2: mandatory
MAC-IP route-type 2: optional
Notes: Without VRF2 L3VNI

## Slide 68: EVPN route-type 2
Leaf1-A: RT2 – MAC/IP route (hosts)
8325-1# sh bgp l2vpn evpn route-type 2
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 54
RT2
One single RT2 entry per VNI on local VTEP, locally originated, best.
No other entries because this entry is originated from the VSX node having the lowest router-ID. It is the best route (decision tree up to router-ID criteria) reflected by Route-Reflectors and not reflected back to the sourcing RR-client.
best

## Slide 69: EVPN route-type 2
Leaf1-A: RT2 – MAC/IP route (hosts)
8325-1# sh bgp l2vpn evpn route-type 2
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Total number of entries 45
RT2
One single RT2 entry per VNI on local VTEP, locally originated, best.
No other entries because this entry is originated from the VSX node having the lowest router-ID. It is the best route (decision tree up to router-ID criteria) reflected by Route-Reflectors and not reflected back to the sourcing RR-client.
best
Notes: Without VRF2 L3VNI

## Slide 70: EVPN route-type 2
Leaf1-B: RT2 – MAC/IP route (hosts)
8325-1# sh bgp l2vpn evpn route-type 2
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 90
best
RT3 entry locally originated on the local VTEP, best
RT3 entry from the VSX peer (with lowest router-ID) of same the logical VSX VTEP, reflected by RR1 (Spine-1)
RT3 entry from the VSX peer (with lowest router-ID) of same the logical VSX VTEP, reflected by RR2 (spine-2)
More entries than on lowest router-ID VSX peer
Notes: Please highlight the increase of number of entries due to BGP received routes from RR.

## Slide 71: EVPN route-type 2
Leaf1-B: RT2 – MAC/IP route (hosts)
8325-1# sh bgp l2vpn evpn route-type 2
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Total number of entries 75
RT2
best
RT3 entry locally originated on the local VTEP, best
RT3 entry from the VSX peer (with lowest router-ID) of same the logical VSX VTEP, reflected by RR1 (Spine-1)
RT3 entry from the VSX peer (with lowest router-ID) of same the logical VSX VTEP, reflected by RR2 (spine-2)
More entries than on lowest router-ID VSX peer
Notes: Without VRF2 L3VNI

## Slide 72: Common VRF RD Option
Per VSX logical VTEP
Impact on RT5

## Slide 73: MP-BGP L2VPN EVPN route-type 5
Spine-1: RT5 – IP prefix route (subnet advertisement)
6300F-5-spine1# show bgp l2vpn evpn route-type 5
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Total number of entries 15
RT5
Leaf1-A and Leaf1-B have the same VRF RD.
There is an election of a best route among two entries advertised from each logical VSX VTEP:
One entry coming from VSX primary (preferred due to lowest router-ID)
One entry coming from VSX secondary
best
RT5 RD = VTEP_L1:VRF-ID
best
Leaf2-A and Leaf2-B have the same VRF RD.
There is an election of a best route among two entries advertised from each logical VSX VTEP:
One entry coming from VSX primary (preferred due to lowest router-ID)
One entry coming from VSX secondary
Same RD
Same RD
When Leaf2-A and Leaf2-B have same VRF RD

## Slide 74: MP-BGP L2VPN EVPN route-type 5
8325-1# show bgp l2vpn evpn route-type 5
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.3
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
* [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Total number of entries 12
best
best
Leaf1-A: RT5 – IP prefix route (subnet advertisement)
RT5
For RT5 10.1.10.0/24:
1 RIB entry for the local VSX VTEP
2 RIB entries for the remote VSX VTEP
One single RT5 entry per VNI on the local VTEP, locally originated, best.
No other entries to compete for route election because no other candidate ECMP route.
RT5 RD = VTEP_L1:VRF-ID
Same RD
RT5 entry from the remote VTEP VSX primary (selected by RR due to lowest router-ID, reflected by RR1 (Spine-1). Elected as best due to lowest RR originator-ID (Spine-1).
RT5 entry from the remote VTEP VSX primary (selected by RR due to lowest router-ID, reflected by RR2 (Spine-2). Not selected due to highest RR originator-ID (Spine-2).
When Leaf2-A and Leaf2-B have same VRF RD

## Slide 75: MP-BGP L2VPN EVPN route-type 5
Leaf1-B: RT5 – IP prefix route (subnet advertisement)
8325-2# show bgp l2vpn evpn route-type 5
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.3
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Total number of entries 19
RT5
RT3 entry locally originated on the local VTEP, best
Two RT3 entries per VNI from remote VSX VTEP:
One entry reflected from RR1 (Spine-1) (preferred due to RR1 lowest originator-ID)
One entry reflected from RR2 (spine-2)
best
best
RT3 entry from the VSX peer (with lowest router-ID) of same the logical VSX VTEP, reflected by RR1 (Spine-1)
RT3 entry from the VSX peer (with lowest router-ID) of same the logical VSX VTEP, reflected by RR2 (spine-2)
Same RD
Same RD
RT5 RD = VTEP_L1:VRF-ID
When Leaf2-A and Leaf2-B have same VRF RD

## Slide 76: Distinct VRF RD Option
On each CX nodes
Impact on RT5

## Slide 77: MP-BGP L2VPN EVPN route-type 5
Spine-1: RT5 – IP prefix route (subnet advertisement)
6300F-5-spine1# show bgp l2vpn evpn route-type 5
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Total number of entries 16
RT5
Single unique RT5 entry from each leaf VTEP
sourcing the same subnet
RT5 RD = VTEP_L0:VRF-ID
Unique RD
When all leaf switches have unique VRF RD
(VSX primary RD and VSX secondary RD are different)

## Slide 78: MP-BGP L2VPN EVPN route-type 5
8325-1# sh bgp l2 evpn route-type 5
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.3
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:2 (L3VNI 100002)
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Total number of entries 27
best
best
best
Leaf1-A: RT5 – IP prefix route (subnet advertisement)
RT5
For RT5 10.1.10.0/24:
3 RIB entries for the local VSX VTEP
4 RIB entries for the remote VSX VTEP
One single RT5 entry per VNI on the local VTEP, locally originated, best.
No other entries to compete for route election because no other candidate ECMP route.
RT5 entry from the VSX peer (different RT5 RD) of same the logical VSX VTEP (same NH_IP), reflected by RR1 (Spine-1)
RT5 entry from the VSX peer (different RT5 RD) of same the logical VSX VTEP (same NH_IP), reflected by RR2 (spine-2)
RT5 RD = VTEP_L0:VRF-ID
Unique RD
RT5 entry from the remote VTEP VSX primary (different RT5 RD and different NH_IP), reflected by RR1 (Spine-1). Best (lowest originator-ID).
RT5 entry from the remote VTEP VSX primary (different RT5 RD and different NH_IP), reflected by RR1 (Spine-2)
RT5 entry from the remote VTEP VSX secondary (different RT5 RD and different NH_IP), reflected by RR1 (Spine-1). Best (lowest originator-ID).
RT5 entry from the remote VTEP VSX primary (different RT5 RD and different NH_IP), reflected by RR1 (Spine-2)
Election in this group
Election in this group
2 different routes (different RD) candidate for ECMP (same Next-Hop)
When all leaf switches have unique VRF RD
(VSX primary RD and VSX secondary RD are different)

## Slide 79: MP-BGP L2VPN EVPN route-type 5
8325-1# sh bgp l2 evpn route-type 5
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.3
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Total number of entries 14
best
best
best
Leaf1-A: RT5 – IP prefix route (subnet advertisement)
RT5
For RT5 10.1.10.0/24:
3 RIB entries for the local VSX VTEP
4 RIB entries for the remote VSX VTEP
One single RT5 entry per VNI on the local VTEP, locally originated, best.
No other entries to compete for route election because no other candidate ECMP route.
RT5 entry from the VSX peer (different RT5 RD) of same the logical VSX VTEP (same NH_IP), reflected by RR1 (Spine-1)
RT5 entry from the VSX peer (different RT5 RD) of same the logical VSX VTEP (same NH_IP), reflected by RR2 (spine-2)
RT5 RD = VTEP_L0:VRF-ID
Unique RD
RT5 entry from the remote VTEP VSX primary (different RT5 RD and different NH_IP), reflected by RR1 (Spine-1). Best (lowest originator-ID).
RT5 entry from the remote VTEP VSX primary (different RT5 RD and different NH_IP), reflected by RR1 (Spine-2)
RT5 entry from the remote VTEP VSX secondary (different RT5 RD and different NH_IP), reflected by RR1 (Spine-1). Best (lowest originator-ID).
RT5 entry from the remote VTEP VSX primary (different RT5 RD and different NH_IP), reflected by RR1 (Spine-2)
Election in this group
Election in this group
2 different routes (different RD) candidate for ECMP (same Next-Hop)
When all leaf switches have unique VRF RD
(VSX primary RD and VSX secondary RD are different)
Notes: Without default IVRL

## Slide 80: MP-BGP L2VPN EVPN route-type 5
Leaf1-B: RT5 – IP prefix route (subnet advertisement)
8325-2# sh bgp l2 evpn route-type 5
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.3
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:2 (L3VNI 100002)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Total number of entries 27
RT5
RT5 RD = VTEP_L0:VRF-ID
When all leaf switches have unique VRF RD
(VSX primary RD and VSX secondary RD are different)

## Slide 81: MP-BGP L2VPN EVPN route-type 5
Leaf1-B: RT5 – IP prefix route (subnet advertisement)
8325-2# sh bgp l2 evpn route-type 5
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.3
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Total number of entries 14
RT5
RT5 RD = VTEP_L0:VRF-ID
When all leaf switches have unique VRF RD
(VSX primary RD and VSX secondary RD are different)
Notes: Without IVRL

## Slide 82: BGP EVPN VNI / VTEP

## Slide 83: Common VRF RD Option
Per VSX logical VTEP
Impact on RT5

## Slide 84: MP-BGP L2VPN EVPN VNI
Spine-1
6300F-5-spine1# show bgp l2vpn evpn vni 10010
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Total number of entries 16
6300F-5-spine1# show bgp l2vpn evpn vni 10011
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Total number of entries 8
6300F-5-spine1# show bgp l2vpn evpn vni 100001
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Total number of entries 34
RT5
RT2/3
RT2
L2VNI
L3VNI

## Slide 85: MP-BGP L2VPN EVPN VNI
Leaf1-A
6300F-5-spine1# show bgp l2vpn evpn vni 10010
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Total number of entries 12
6300F-5-spine1# show bgp l2vpn evpn vni 10011
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Total number of entries 4
6300F-5-spine1# show bgp l2vpn evpn vni 100001
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Total number of entries 25
RT2/3
L2VNI
L3VNI
RT5
RT2

## Slide 86: MP-BGP L2VPN EVPN VNI
Leaf1-A
6300F-5-spine1# show bgp l2vpn evpn vni 10010
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Total number of entries 12
6300F-5-spine1# show bgp l2vpn evpn vni 10011
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Total number of entries 4
6300F-5-spine1# show bgp l2vpn evpn vni 100001
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:1 (L3VNI 100001)
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Total number of entries 24
RT2/3
L2VNI
L3VNI
RT5
RT5
RT2
RT2
Notes: 10.5 – sorting of routes not the same than in 10.6

## Slide 87: MP-BGP L2VPN EVPN VTEP
Spine-1
Display EVPN routes from one specific VTEP show bgp l2vpn evpn vtep <ip_address>
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Total number of entries 48
6300F-5-spine1# show bgp l2vpn evpn vtep 192.168.11.3
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?

## Slide 88: MP-BGP L2VPN EVPN VTEP VNI route-type
Spine-1
Display EVPN routes from one specific VTEP for a given L3VNI, for RT2 (hosts) show bgp l2vpn evpn vtep <ip_add> vni <vni> route-type <2|5>
6300F-5-spine1# show bgp l2vpn evpn vtep 192.168.11.3 vni 100001 route-type 2
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Total number of entries 12

## Slide 89: Distinct VRF RD Option
On each CX nodes
Impact on RT5

## Slide 90: MP-BGP L2VPN EVPN VNI
Spine-1
6300F-5-spine1# show bgp l2vpn evpn vni 10010
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Total number of entries 16
6300F-5-spine1# show bgp l2vpn evpn vni 10011
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Total number of entries 8
6300F-5-spine1# show bgp l2vpn evpn vni 100001
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Total number of entries 34
RT5
RT2
RT2
L2VNI
L3VNI

## Slide 91: MP-BGP L2VPN EVPN VNI
Spine-1
6300F-5-spine1# show bgp l2vpn evpn vni 10010
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Total number of entries 16
6300F-5-spine1# show bgp l2vpn evpn vni 10011
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Total number of entries 8
6300F-5-spine1# show bgp l2vpn evpn vni 100001
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Total number of entries 32
RT5
RT2
RT2
Notes: Without IVRL

## Slide 92: MP-BGP L2VPN EVPN VNI
Leaf1-A
6300F-5-spine1# show bgp l2vpn evpn vni 10010
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Total number of entries 12
6300F-5-spine1# show bgp l2vpn evpn vni 10011
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Total number of entries 4
6300F-5-spine1# show bgp l2vpn evpn vni 100001
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Total number of entries 35
RT5
subnet
RT2/3
L2VNI
L3VNI
RT2
hosts

## Slide 93: MP-BGP L2VPN EVPN VTEP
Spine-1
Display EVPN routes from one specific VTEP show bgp l2vpn evpn vtep <ip_address>
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Total number of entries 52
6300F-5-spine1# show bgp l2vpn evpn vtep 192.168.11.3
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?

## Slide 94: BGP EVPN routes

## Slide 95: Common VRF RD Option
Per VSX logical VTEP
Impact on RT5

## Slide 96: MP-BGP L2VPN EVPN Routes
6300F-5-spine1# show bgp l2vpn evpn
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Spine-1
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 96

## Slide 97: MP-BGP L2VPN EVPN Routes
6300F-5-spine1# show bgp l2vpn evpn extcommunity
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Ext-Community
----------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:10
* i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:10
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:10
* i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:10
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:11
* i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:11
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:12
* i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:12
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:268445476
* i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:268445476
Spine-1 – with extended communities
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:268445476
* i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:268445476
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 65001:1,02:00:00:00:01:00
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 65001:1,02:00:00:00:01:00
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 65001:1,02:00:00:00:01:00
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 65001:1,02:00:00:00:01:00
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 65001:1,02:00:00:00:01:00
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 65001:1,02:00:00:00:01:00
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 65001:1,02:00:00:00:02:00
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 65001:1,02:00:00:00:02:00
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 65001:1,02:00:00:00:02:00
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 65001:1,02:00:00:00:02:00
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 65001:2,02:00:00:00:01:00
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 65001:2,02:00:00:00:01:00
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 65001:2,02:00:00:00:01:00
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 65001:2,02:00:00:00:01:00
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 65001:2,02:00:00:00:02:00
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 65001:2,02:00:00:00:02:00
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
Total number of entries 96

## Slide 98: MP-BGP L2VPN EVPN Routes
Leaf1-A
8325-1# show bgp l2vpn evpn
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.3
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 72

## Slide 99: MP-BGP L2VPN EVPN Routes
Leaf1-B
8325-2# show bgp l2vpn evpn
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.4
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?

## Slide 100: MP-BGP L2VPN EVPN Routes
Leaf1-B
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 120

## Slide 101: MP-BGP L2VPN EVPN Routes
Leaf2-A
8325-3# show bgp l2vpn evpn
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.5
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 72

## Slide 102: MP-BGP L2VPN EVPN Routes
Leaf2-B
8325-4# sh bgp l2vpn evpn
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.6
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?

## Slide 103: MP-BGP L2VPN EVPN Routes
Leaf2-B
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 120

## Slide 104: Distinct VRF RD Option
On each CX nodes
Impact on RT5

## Slide 105: MP-BGP L2VPN EVPN Routes
6300F-5-spine1# sh bgp l2vpn evpn
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Metric LocPrf Weight Path
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Spine-1
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 100

## Slide 106: MP-BGP L2VPN EVPN Routes
6300F-5-spine1# show bgp l2vpn evpn extcommunity
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.1
Network Nexthop Ext-Community
----------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:10
* i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:10
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:10
* i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:10
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:11
* i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:11
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:12
* i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:12
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:268445476
* i [3]:[0]:[192.168.11.3] 192.168.11.3 65001:268445476
Spine-1 – with extended communities
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:268445476
* i [3]:[0]:[192.168.11.5] 192.168.11.5 65001:268445476
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 65001:1,02:00:00:00:01:00
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 65001:1,02:00:00:00:01:00
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 65001:1,02:00:00:00:01:00
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 65001:1,02:00:00:00:01:00
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 65001:1,02:00:00:00:01:00
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 65001:1,02:00:00:00:01:00
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 65001:1,02:00:00:00:02:00
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 65001:1,02:00:00:00:02:00
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 65001:1,02:00:00:00:02:00
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 65001:1,02:00:00:00:02:00
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 65001:1,65001:10,02:00:00:00:01:00
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 65001:1,65001:11,02:00:00:00:01:00
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 65001:1,65001:10,02:00:00:00:02:00
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 65001:1,65001:12,02:00:00:00:02:00
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 65001:2,02:00:00:00:01:00
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 65001:2,02:00:00:00:01:00
Route Distinguisher: 192.168.1.4:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 65001:2,02:00:00:00:01:00
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 65001:2,02:00:00:00:01:00
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 65001:2,02:00:00:00:02:00
Route Distinguisher: 192.168.1.6:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 65001:2,02:00:00:00:02:00
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 65001:2,65001:268445476,02:00:00:00:01:00
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 65001:2,65001:268445476,02:00:00:00:02:00
Total number of entries 100

## Slide 107: MP-BGP L2VPN EVPN Routes
8325-1# sh bgp l2vpn evpn
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.3
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Leaf1-A
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:2 (L3VNI 100002)
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 90

## Slide 108: MP-BGP L2VPN EVPN Routes
Leaf1-B
8325-2# sh bgp l2 evpn
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.4
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*> [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
*>i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?

## Slide 109: MP-BGP L2VPN EVPN Routes
Leaf1-B
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:2 (L3VNI 100002)
*> [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 132

## Slide 110: MP-BGP L2VPN EVPN Routes
Leaf2-A
8325-3# sh bgp l2 evpn
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.5
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:2 (L3VNI 100002)
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 92

## Slide 111: MP-BGP L2VPN EVPN Routes
8325-4# sh bgp l2vpn evpn
Status codes: s suppressed, d damped, h history, * valid, > best, = multipath,
i internal, e external S Stale, R Removed
Origin codes: i - IGP, e - EGP, ? - incomplete
EVPN Route-Type 2 prefix: [2]:[ESI]:[EthTag]:[MAC]:[OrigIP]
EVPN Route-Type 3 prefix: [3]:[EthTag]:[OrigIP]
EVPN Route-Type 5 prefix: [5]:[ESI]:[EthTag]:[IPAddrLen]:[IPAddr]
VRF : default
Local Router-ID 192.168.1.6
Network Nexthop Metric LocPrf Weight Path
------------------------------------------------------------------------------------------------------------
Route Distinguisher: 192.168.11.3:10 (L2VNI 10010)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:10 (L2VNI 10010)
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L2VNI 10011)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L2VNI 10012)
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Leaf2-B
Route Distinguisher: 192.168.11.3:20 (L2VNI 10020)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
*>i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
* i [3]:[0]:[192.168.11.3] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L2VNI 10020)
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
*> [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
* i [3]:[0]:[192.168.11.5] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:1 (L3VNI 100001)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.11.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:1 (L3VNI 100001)
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:1 (L3VNI 100001)
*> [5]:[0]:[0]:[24]:[10.1.10.0] 192.168.11.5 0 100 0 ?
*> [5]:[0]:[0]:[24]:[10.1.12.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:10 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:61:91]:[10.1.10.10] 192.168.11.3 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
* [2]:[0]:[0]:[00:50:56:8e:61:91]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.3:11 (L3VNI 100001)
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[10.1.11.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:4d:9c]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.11.1] 192.168.11.3 0 100 0 ?

## Slide 112: MP-BGP L2VPN EVPN Routes
Route Distinguisher: 192.168.11.5:10 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[10.1.10.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:86:2d:79]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.10.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.5:12 (L3VNI 100001)
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[10.1.12.10] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:80:53:54]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.1.12.1] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.3:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.4:2 (L3VNI 100002)
*>i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[0]:[0.0.0.0] 192.168.11.3 0 100 0 ?
*>i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.1.5:2 (L3VNI 100002)
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
* i [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.1.6:2 (L3VNI 100002)
*> [5]:[0]:[0]:[24]:[10.2.20.0] 192.168.11.5 0 100 0 ?
Route Distinguisher: 192.168.11.3:20 (L3VNI 100002)
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[10.2.20.10] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:32:e8]:[] 192.168.11.3 0 100 0 ?
*>i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.3 0 100 0 ?
Route Distinguisher: 192.168.11.5:20 (L3VNI 100002)
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[10.2.20.11] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[00:50:56:8e:6b:d8]:[] 192.168.11.5 0 100 0 ?
*> [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
* i [2]:[0]:[0]:[12:00:00:00:01:00]:[10.2.20.1] 192.168.11.5 0 100 0 ?
Total number of entries 134
Leaf2-B

## Slide 113: VRF routes

## Slide 114: VRF1 IP routes
Leaf1-A
8325-1# show ip route vrf VRF1
Displaying ipv4 routes selected for forwarding
'[x/y]' denotes [distance/metric]
0.0.0.0/0, vrf VRF1
via 192.168.4.0[vrf SERVICES], [200/0], bgp
10.1.10.0/24, vrf VRF1
via vlan10, [0/0], connected
10.1.10.1/32, vrf VRF1
via vlan10, [0/0], local
10.1.10.11/32, vrf VRF1
via 192.168.11.5[vrf default], [200/0], bgp, encap vxlan, l3vni 100001
10.1.11.0/24, vrf VRF1
via vlan11, [0/0], connected
10.1.11.1/32, vrf VRF1
via vlan11, [0/0], local
10.1.12.0/24, vrf VRF1
via 192.168.11.5[vrf default], [200/0], bgp, encap vxlan, l3vni 100001
10.1.12.1/32, vrf VRF1
via 192.168.11.5[vrf default], [200/0], bgp, encap vxlan, l3vni 100001
10.1.12.10/32, vrf VRF1
via 192.168.11.5[vrf default], [200/0], bgp, encap vxlan, l3vni 100001

## Slide 115: VRF1 IP routes
Leaf2-A
8325-3# show ip route vrf VRF1
Displaying ipv4 routes selected for forwarding
'[x/y]' denotes [distance/metric]
0.0.0.0/0, vrf VRF1
via 192.168.11.3[vrf default], [200/0], bgp, encap vxlan, l3vni 100001
10.1.10.0/24, vrf VRF1
via vlan10, [0/0], connected
10.1.10.1/32, vrf VRF1
via vlan10, [0/0], local
10.1.10.10/32, vrf VRF1
via 192.168.11.3[vrf default], [200/0], bgp, encap vxlan, l3vni 100001
10.1.11.0/24, vrf VRF1
via 192.168.11.3[vrf default], [200/0], bgp, encap vxlan, l3vni 100001
10.1.11.1/32, vrf VRF1
via 192.168.11.3[vrf default], [200/0], bgp, encap vxlan, l3vni 100001
10.1.11.10/32, vrf VRF1
via 192.168.11.3[vrf default], [200/0], bgp, encap vxlan, l3vni 100001
10.1.12.0/24, vrf VRF1
via vlan12, [0/0], connected
10.1.12.1/32, vrf VRF1
via vlan12, [0/0], local

## Slide 116: VRF1 ARP
Leaf1-A
8325-1# show arp vrf VRF1
IPv4 Address MAC Port Physical Port State VRF
-----------------------------------------------------------------------------------------------10.1.11.10 00:50:56:8e:4d:9c vlan11 lag1 reachable VRF1
10.1.10.10 00:50:56:8e:61:91 vlan10 lag1 reachable VRF1
10.1.10.11 00:50:56:86:2d:79 vlan10 vxlan1(192.168.11.5) permanent VRF1
Total Number Of ARP Entries Listed- 3.
------------------------------------------------------------------------------------------------

## Slide 117: VXLAN Tunnels

## Slide 118
VXLAN Tunnels
Leaf1-A
8325-1# show interface vxlan 1
Interface vxlan1 is up
Admin state is up
Description:
Underlay VRF: default
Destination UDP port: 4789
VTEP source IPv4 address: 192.168.11.3
VNI Routing VLAN VRF VTEP Peers Origin
---------- ------------ ------ ------------ ----------------- --------
10010 disabled 10 -- 192.168.11.5 evpn
10011 disabled 11 -- -- --
10020 disabled 20 -- 192.168.11.5 evpn
100001 enabled -- VRF1 192.168.11.5 evpn
100002 enabled -- VRF2 192.168.11.5 evpn
Aggregate Statistics
--------------------
Decap:
27 input packets 3078 bytes
87 broadcast packets 9918 bytes
0 drop packets
Encap:
55424 output packets 5672314 bytes
273 BUM packets 82446 bytes
0 drop packets
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
Leaf1-A

## Slide 119
VXLAN Tunnels
Leaf1-A
8325-1# show interface vxlan vni
VNI : 10010 VLAN : 10
Routing : disabled VRF : --
VNI-Status : operational
VNI : 10011 VLAN : 11
Routing : disabled VRF : --
VNI-Status : operational
VNI : 10020 VLAN : 20
Routing : disabled VRF : --
VNI-Status : operational
VNI : 100001 VLAN : --
Routing : enabled VRF : VRF1
VNI-Status : operational
VNI : 100002 VLAN : --
Routing : enabled VRF : VRF2
VNI-Status : operational
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
8325-1# show interface vxlan vteps detail
Destination : 192.168.11.5
Source : 192.168.11.3
Origin : evpn
VRF : default
Status : operational
Nexthops
========
IP-ADDRESS INTERFACE NEXTHOP-MAC
--------------- ---------- --------------------
192.168.3.8 1/1/24 88:3a:30:93:bc:00
192.168.3.0 1/1/23 88:3a:30:93:ca:40
Leaf1-A

## Slide 120
VXLAN Tunnels
Leaf1-A
8325-1# show interface vxlan vtep
Source Destination Origin Status VNI Routing VLAN VRF
---------------- ---------------- ------------ --------------------- --------- --------- ----- ------
192.168.11.3 192.168.11.5 evpn operational 10010 disabled 10 --
192.168.11.3 192.168.11.5 evpn operational 10020 disabled 20 --
192.168.11.3 192.168.11.5 evpn operational 100001 enabled -- VRF1
192.168.11.3 192.168.11.5 evpn operational 100002 enabled -- VRF2
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
8325-1# show interface vxlan vni vteps
VNI : 10010 VLAN : 10
Routing : disabled VRF : --
VNI-Status : operational
VTEPS
=====
Origin Source Destination VRF VTEP-STATUS
----------- ---------------- ---------------- ----------- ----------------
evpn 192.168.11.3 192.168.11.5 default operational
VNI : 10011 VLAN : 11
Routing : disabled VRF : --
VNI-Status : operational
VNI : 10020 VLAN : 20
Routing : disabled VRF : --
VNI-Status : operational
VTEPS
=====
Origin Source Destination VRF VTEP-STATUS
----------- ---------------- ---------------- ----------- ----------------
evpn 192.168.11.3 192.168.11.5 default operational
VNI : 100001 VLAN : --
Routing : enabled VRF : VRF1
VNI-Status : operational
VTEPS
=====
Origin Source Destination VRF VTEP-STATUS
----------- ---------------- ---------------- ----------- ----------------
evpn 192.168.11.3 192.168.11.5 default operational
Leaf1-A

## Slide 121
VXLAN Tunnels
Leaf2-B
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
8325-4# sh interface vxlan 1
Interface vxlan1 is up
Admin state is up
Description:
Underlay VRF: default
Destination UDP port: 4789
VTEP source IPv4 address: 192.168.11.5
VNI Routing VLAN VRF VTEP Peers Origin
---------- ------------ ------ ------------ ----------------- --------
10010 disabled 10 -- 192.168.11.3 evpn
10012 disabled 12 -- -- --
10020 disabled 20 -- 192.168.11.3 evpn
100001 enabled -- VRF1 192.168.11.3 evpn
100002 enabled -- VRF2 192.168.11.3 evpn
Leaf2-B

## Slide 122
VXLAN Tunnels
Leaf2-B
8325-4# sh interface vxlan vni
VNI : 10010 VLAN : 10
Routing : disabled VRF : --
VNI-Status : operational
VNI : 10012 VLAN : 12
Routing : disabled VRF : --
VNI-Status : operational
VNI : 10020 VLAN : 20
Routing : disabled VRF : --
VNI-Status : operational
VNI : 100001 VLAN : --
Routing : enabled VRF : VRF1
VNI-Status : operational
VNI : 100002 VLAN : --
Routing : enabled VRF : VRF2
VNI-Status : operational
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
8325-4# sh interface vxlan vteps detail
Destination : 192.168.11.3
Source : 192.168.11.5
Origin : evpn
VRF : default
Status : operational
Nexthops
========
IP-ADDRESS INTERFACE NEXTHOP-MAC
--------------- ---------- --------------------
192.168.3.6 1/1/23 88:3a:30:93:ca:40
192.168.3.14 1/1/24 88:3a:30:93:bc:00
Leaf2-B

## Slide 123
VXLAN Tunnels
Leaf2-B
8325-4# sh interface vxlan vteps
Source Destination Origin Status VNI Routing VLAN VRF
---------------- ---------------- ------------ --------------------- --------- --------- ----- ------
192.168.11.5 192.168.11.3 evpn operational 10010 disabled 10 --
192.168.11.5 192.168.11.3 evpn operational 10020 disabled 20 --
192.168.11.5 192.168.11.3 evpn operational 100001 enabled -- VRF1
192.168.11.5 192.168.11.3 evpn operational 100002 enabled -- VRF2
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
8325-4# sh interface vxlan vni vteps
VNI : 10010 VLAN : 10
Routing : disabled VRF : --
VNI-Status : operational
VTEPS
=====
Origin Source Destination VRF VTEP-STATUS
----------- ---------------- ---------------- ----------- ----------------
evpn 192.168.11.5 192.168.11.3 default operational
VNI : 10012 VLAN : 12
Routing : disabled VRF : --
VNI-Status : operational
VNI : 10020 VLAN : 20
Routing : disabled VRF : --
VNI-Status : operational
VTEPS
=====
Origin Source Destination VRF VTEP-STATUS
----------- ---------------- ---------------- ----------- ----------------
evpn 192.168.11.5 192.168.11.3 default operational
VNI : 100001 VLAN : --
Routing : enabled VRF : VRF1
VNI-Status : operational
VTEPS
=====
Origin Source Destination VRF VTEP-STATUS
----------- ---------------- ---------------- ----------- ----------------
evpn 192.168.11.5 192.168.11.3 default operational
Leaf2-B

## Slide 124
VTEP Router-MAC
EVPN vtep-neighbor
8325-1# show evpn vtep-neighbor all-vrfs
VTEP-IP L3VNI MAC VRF State
---------------------------------------------------------------------------------
192.168.11.5 100001 02:00:00:00:02:00 VRF1 Up
192.168.11.5 100002 02:00:00:00:02:00 VRF2 Up
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
192.168.110.0/31
VLAN 2
VLAN 2
8325-4# show evpn vtep-neighbor all-vrfs
VTEP-IP L3VNI MAC VRF State
---------------------------------------------------------------------------------
192.168.11.3 100002 02:00:00:00:01:00 VRF2 Up
192.168.11.3 100001 02:00:00:00:01:00 VRF1 Up
Virtual-MAC 02:00:00:00:01:00
Virtual-MAC 02:00:00:00:02:00

## Slide 125
L2VNI / L3VNI Summary
show evpn evi summary
8325-1# show evpn evi summary
L2VNI VLAN Status
-------------------------------------
10010 10 Up
10011 11 Up
10020 20 Up
L3VNI VRF Status
-------------------------------------
100001 VRF1 Up
100002 VRF2 Up
EVPN instances : 5
EVPN instances Up : 5
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
192.168.110.0/31
VLAN 2
VLAN 2
Virtual-MAC 02:00:00:00:01:00
Virtual-MAC 02:00:00:00:02:00
8325-4# sh evpn evi summary
L2VNI VLAN Status
-------------------------------------
10010 10 Up
10012 12 Up
10020 20 Up
L3VNI VRF Status
-------------------------------------
100001 VRF1 Up
100002 VRF2 Up
EVPN instances : 5
EVPN instances Up : 5

## Slide 126
L2VNI / L3VNI Detail
Leaf2-A: show evpn evi detail
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
192.168.110.0/31
VLAN 2
VLAN 2
Virtual-MAC 02:00:00:00:01:00
Virtual-MAC 02:00:00:00:02:00
8325-3# show evpn evi detail
L2VNI : 10010
Route Distinguisher : 192.168.11.5:10
VLAN : 10
Status : up
RT Import : 65001:10
RT Export : 65001:10
Local MACs : 3
Remote MACs : 3
Peer VTEPs : 1
Peer-VTEP-Address Remote-MACs
------------------------------------------------------
192.168.11.3 3
L2VNI : 10012
Route Distinguisher : 192.168.11.5:12
VLAN : 12
Status : up
RT Import : 65001:12
RT Export : 65001:12
Local MACs : 3
Remote MACs : 0
Peer VTEPs : 0
Peer-VTEP-Address Remote-MACs
------------------------------------------------------
L2VNI : 10020
Route Distinguisher : 192.168.11.5:20
VLAN : 20
Status : up
RT Import : 65001:268445476
RT Export : 65001:268445476
Local MACs : 3
Remote MACs : 2
Peer VTEPs : 1
Peer-VTEP-Address Remote-MACs
------------------------------------------------------
192.168.11.3 2
L3VNI : 100001
Route Distinguisher : 192.168.1.5:1
VRF : VRF1
Status : up
RT Import : 65001:1
RT Export : 65001:1
Local Type-5 Routes : 2
Remote Type-5 Routes : 6
Peer VTEPs : 1
Peer-VTEP-Address Remote-Routes
------------------------------------------------------
192.168.11.3 6
L3VNI : 100002
Route Distinguisher : 192.168.1.5:2
VRF : VRF2
Status : up
RT Import : 65001:2
RT Export : 65001:2
Local Type-5 Routes : 1
Remote Type-5 Routes : 4
Peer VTEPs : 1
Peer-VTEP-Address Remote-Routes
------------------------------------------------------
192.168.11.3 4

## Slide 127: VLAN / MAC / EVPN

## Slide 128
VLAN
8325-1# show vlan
---------------------------------------------------------------------------------------------------
VLAN Name Status Reason Type Interfaces
---------------------------------------------------------------------------------------------------
1 DEFAULT_VLAN_1 up ok default lag256
2 VLAN2 up ok static lag256
10 VLAN10 up ok static lag1,lag256,vxlan1
11 VLAN11 up ok static lag1,lag256,vxlan1
20 VLAN20 up ok static lag2,lag256,vxlan1
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
VLAN 2
VLAN 2
8325-4# show vlan
---------------------------------------------------------------------------------------------------
VLAN Name Status Reason Type Interfaces
---------------------------------------------------------------------------------------------------
1 DEFAULT_VLAN_1 up ok default lag256
2 VLAN2 up ok static lag256
10 VLAN10 up ok static lag37,lag256,vxlan1
12 VLAN12 up ok static lag39,lag256,vxlan1
20 VLAN20 up ok static lag7,lag256,vxlan1

## Slide 129
MAC
Leaf1-A
8325-1# show mac-address-table
MAC age-time : 300 seconds
Number of MAC addresses : 10
MAC Address VLAN Type Port
--------------------------------------------------------------
54:80:28:fc:5c:00 1 dynamic lag256
54:80:28:fc:5c:00 2 dynamic lag256
00:50:56:86:2d:79 10 evpn vxlan1(192.168.11.5)
00:50:56:8e:61:91 10 dynamic lag1
54:80:28:fc:5c:00 10 dynamic lag256
00:50:56:8e:4d:9c 11 dynamic lag1
54:80:28:fc:5c:00 11 dynamic lag256
00:50:56:8e:6b:d8 20 evpn vxlan1(192.168.11.5)
00:50:56:8e:32:e8 20 dynamic lag2
54:80:28:fc:5c:00 20 dynamic lag256
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
VLAN 2
VLAN 2
8325-1# show mac-address-table detail
MAC age-time : 300 seconds
Number of MAC addresses : 10
MAC Address VLAN Type Port Age Denied never_ageout
---------------------------------------------------------------------------------------------
54:80:28:fc:5c:00 1 dynamic lag256 300 false false
54:80:28:fc:5c:00 2 dynamic lag256 300 false false
00:50:56:86:2d:79 10 evpn vxlan1 300 false true
00:50:56:8e:61:91 10 dynamic lag1 300 false false
54:80:28:fc:5c:00 10 dynamic lag256 300 false false
00:50:56:8e:4d:9c 11 dynamic lag1 300 false false
54:80:28:fc:5c:00 11 dynamic lag256 300 false false
00:50:56:8e:6b:d8 20 evpn vxlan1 300 false true
00:50:56:8e:32:e8 20 dynamic lag2 300 false false
54:80:28:fc:5c:00 20 dynamic lag256 300 false false

## Slide 130
EVPN MAC-IP
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
8325-1# show evpn mac-ip
Flags: Local(L), Remote(R), Sticky bit(S)
EVI MAC IP Next-hop Seq-Num Flags
--------------------------------------------------------------------------------------
10010 00:50:56:86:2d:79 vxlan1(192.168.11.5) 8 R
10010 00:50:56:86:2d:79 10.1.10.11 vxlan1(192.168.11.5) 8 R
10010 00:50:56:8e:61:91 4 L
10010 00:50:56:8e:61:91 10.1.10.10 4 L
10010 12:00:00:00:01:00 10.1.10.1 0 L
10011 00:50:56:8e:4d:9c 0 L
10011 00:50:56:8e:4d:9c 10.1.11.10 0 L
10011 12:00:00:00:01:00 10.1.11.1 0 L
10020 00:50:56:8e:32:e8 4 L
10020 00:50:56:8e:32:e8 10.2.20.10 4 L
10020 00:50:56:8e:6b:d8 vxlan1(192.168.11.5) 6 R
10020 00:50:56:8e:6b:d8 10.2.20.11 vxlan1(192.168.11.5) 6 R
10020 12:00:00:00:01:00 10.2.20.1 0 L
MACs : 8
Remote MACs : 2
8325-3# show evpn mac-ip
Flags: Local(L), Remote(R), Sticky bit(S)
EVI MAC IP Next-hop Seq-Num Flags
--------------------------------------------------------------------------------------
10010 00:50:56:86:2d:79 8 L
10010 00:50:56:86:2d:79 10.1.10.11 8 L
10010 00:50:56:8e:61:91 vxlan1(192.168.11.3) 4 R
10010 00:50:56:8e:61:91 10.1.10.10 vxlan1(192.168.11.3) 4 R
10010 12:00:00:00:01:00 10.1.10.1 vxlan1(192.168.11.3) 0 R
10012 00:50:56:80:53:54 0 L
10012 00:50:56:80:53:54 10.1.12.10 0 L
10012 12:00:00:00:01:00 10.1.12.1 0 L
10020 00:50:56:8e:32:e8 vxlan1(192.168.11.3) 4 R
10020 00:50:56:8e:32:e8 10.2.20.10 vxlan1(192.168.11.3) 4 R
10020 00:50:56:8e:6b:d8 6 L
10020 00:50:56:8e:6b:d8 10.2.20.11 6 L
10020 12:00:00:00:01:00 10.2.20.1 vxlan1(192.168.11.3) 0 R
MACs : 8
Remote MACs : 4

## Slide 131: Traffic Capture
L2VNI
L3VNI
L3VNI to External Networks

## Slide 132: L2VNI

## Slide 133
VSX VTEP2
L1: 192.168.11.5
VSX VTEP1
L1: 192.168.11.3
VLAN 12 / VNI 10012 / SVI 12 / 10.1.12.0/24
VRF1 / VNI 100001
VRF12 / VNI 100002
VLAN 10 / VNI 10010 / SVI 10 / 10.1.10.0/24
VLAN 11 / VNI 10011 / SVI 11 / 10.1.11.0/24
L3 VNI
L2 VNI
VLAN 20 / VNI 10020 / SVI 20 / 10.2.20.0/24
L2VNI flow
VLAN 10
vubu2 10.1.10.100
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
vubu3 10.2.20.10
00:50:56:8e:32:e8
vubu4 10.1.11.10
00:50:56:8e:4d:9c
vubu6 10.2.20.11
00:50:56:8e:6b:d8

## Slide 134
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.100
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
L2 VNI
PCAP
15.136.40.98 #6
1/1/22
PCAP
15.136.40.98 #2
1/1/40
8325-1# show mirror 1
Mirror Session: 1
Admin Status: enable
Operation Status: enabled
Comment: both uplinks
Source: interface 1/1/23 both
Source: interface 1/1/24 both
Source: interface rx-filter none
Destination: interface 1/1/40
Output Packets: 1148199
Output Bytes: 127031317

## Slide 135: L3VNI Symmetric IRB

## Slide 136
VSX VTEP2
L1: 192.168.11.5
VSX VTEP1
L1: 192.168.11.3
VLAN 12 / VNI 10012 / SVI 12 / 10.1.12.0/24
VRF1 / VNI 100001
VRF12 / VNI 100002
VLAN 10 / VNI 10010 / SVI 10 / 10.1.10.0/24
VLAN 11 / VNI 10011 / SVI 11 / 10.1.11.0/24
L3 VNI
L2 VNI
VLAN 20 / VNI 10020 / SVI 20 / 10.2.20.0/24
L3VNI flow
VLAN 10 to VLAN 12
vubu2 10.1.10.100
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
vubu3 10.2.20.10
00:50:56:8e:32:e8
vubu4 10.1.11.10
00:50:56:8e:4d:9c
vubu6 10.2.20.11
00:50:56:8e:6b:d8

## Slide 137
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.100
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
L3VNI
PCAP
15.136.40.98 #6
1/1/22
PCAP
15.136.40.98 #2
1/1/40
8325-1# show mirror 1
Mirror Session: 1
Admin Status: enable
Operation Status: enabled
Comment: both uplinks
Source: interface 1/1/23 both
Source: interface 1/1/24 both
Source: interface rx-filter none
Destination: interface 1/1/40
Output Packets: 1148199
Output Bytes: 127031317
Virtual-MAC 02:00:00:00:01:00
Virtual-MAC 02:00:00:00:02:00

## Slide 138
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.100
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
L3VNI Symmetric IRB
PCAP
15.136.40.98 #6
1/1/22
PCAP
15.136.40.98 #2
1/1/40
Virtual-MAC 02:00:00:00:01:00
Virtual-MAC 02:00:00:00:02:00
Echo request
8325-1
VSX VTEP2

## Slide 139
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.100
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
VLAN 11
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
VLAN 2
VLAN 2
PCAP
15.136.40.98 #6
1/1/22
PCAP
15.136.40.98 #2
1/1/40
L3VNI Symmetric IRB
Echo reply
Virtual-MAC 02:00:00:00:01:00
Virtual-MAC 02:00:00:00:02:00
8325-3
VSX VTEP1

## Slide 140: L3VNI – Default route

## Slide 141
VSX VTEP2
L1: 192.168.11.5
VSX VTEP1
L1: 192.168.11.3
VLAN 12 / VNI 10012 / SVI 12 / 10.1.12.0/24
VRF1 / VNI 100001
VRF2 / VNI 100002
VLAN 10 / VNI 10010 / SVI 10 / 10.1.10.0/24
VLAN 11 / VNI 10011 / SVI 11 / 10.1.11.0/24
L3 VNI
L2 VNI
VLAN 20 / VNI 10020 / SVI 20 / 10.2.20.0/24
L3VNI flow for Default route
VRF1 to external networks
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
vlinux5 10.1.12.10
00:50:56:80:53:54
vubu3 10.2.20.10
00:50:56:8e:32:e8
vubu4 10.1.11.10
00:50:56:8e:4d:9c
vubu6 10.2.20.11
00:50:56:8e:6b:d8
SERVICES VRF
Campus
Cores
SERVICES VRF link attach
IVRL on Border Leaf
6300-4
192.168.199.2
AS 65001
AS 65001

## Slide 142
1/1/49
1/1/49
ISL (LAG256)
8325-1
15.136.40.237
L0: 192.168.1.3
L1: 192.168.11.3
8325-2
15.136.40.238
L0: 192.168.1.4
L1: 192.168.11.3
1/1/50
1/1/50
1/1/41
1/1/41
1/1/55
1/1/55
ISL (LAG256)
8325-3
15.136.40.233
L0: 192.168.1.5
L1: 192.168.11.5
8325-4
15.136.40.234
L0: 192.168.1.6
L1: 192.168.11.5
1/1/56
1/1/56
1/1/25
1/1/25
6300-5
15.136.40.245
L0: 192.168.1.1
6300-6
15.136.40.246
L0: 192168.1.2
ESXi: 15.136.40.25
vmnic0
vmnic1
vmnic3
vmnic2
1/0/1
2930-3
1
1
2930-4
2930-2
1
5700-1
15.136.40.196
vmnic6
2930-1
5
1/1/25
1/1/26
1/1/27
1/1/28
1/1/25
1/1/26
1/1/27
1/1/28
1/1/23
1/1/23
1/1/23
1/1/23
1/1/24
1/1/24
1/1/24
1/1/24
1/1/1
1/1/1
1/1/2
1/1/2
49
50
49
50
vmnic0
2
25
26
1/1/37
1/1/37
1/1/7
1
2
1/1/39
1/1/39
1/0/49
1/0/50
192.168.3.0/31
192.168.3.2/31
192.168.3.4/31
192.168.3.6/31
192.168.3.8/31
192.168.3.10/31
192.168.3.12/31
192.168.3.14/31
1/1/7
192.168.0.0/31
192.168.0.2/31
L2 link
L3 link
LAG 1
LAG 2
LAG 37
vubu2 10.1.10.10
00:50:56:8e:61:91
vlinux27 10.1.10.11
00:50:56:86:2d:79
ESXi: 15.136.40.23
ESXi: 15.136.40.24
vlinux5 10.1.12.10
00:50:56:80:53:54
VLAN 10
VLAN 10
VLAN 12
ESXi: 15.136.40.25
vubu3 10.2.20.10
00:50:56:8e:32:e8
VLAN 20
vubu4 10.1.11.10
00:50:56:8e:4d:9c
ESXi: 15.136.40.27
VLAN 11
ESXi: 15.136.40.27
vubu6 10.2.20.11
00:50:56:8e:6b:d8
VLAN 20
1/1/22
PCAP
15.136.40.98 #6
1/1/22
PCAP
15.136.40.98 #2
PCAP
15.136.40.98 #3
PCAP
15.136.40.98 #4
1/1/40
1/1/40
1/1/40
L3VNI flow
for Default route
VLAN 2
VLAN 2
1/3/1
1/8/1
1/3/1
1/8/1
LAG200
8400-2
15.136.40.236
L0: 192.168.2.2
1/3/3
1/3/3
1/1/51
1/1/51
1/3/3
1/3/3
6300-4
15.136.40.244
1/1/9
ESXi: 15.136.40.27
vubu7 : 192.168.3.242/29
vmnic3
1/1/1
192.168.3.240/29
192.168.4.0/31
192.168.4.2/31
8400-1
15.136.40.235
L0: 192.168.2.1
Virtual-MAC 02:00:00:00:01:00
Virtual-MAC 02:00:00:00:02:00
192.168.199.2
8325-3
VSX VTEP1