## Slide 1
ClearPass Deep Dive
Derin Mellor
derin.mellor@hpe.com
+44 7786 114030
Notes: Hello, welcome to ClearPass Network Access Control sales training.
In this training, you will be introduced to the challenges customers face with network access control and how Aruba's ClearPass Network Access Control Solution remedies these challenges.
ClearPass is an essential component of Aruba's 360 Secure Fabric (Aruba’s overall security architecture) and is a market-leading security product with over 7,000 customers worldwide.
In a world of rapidly-expanding networks, based on an increasing quantity and variety of devices, ClearPass performs the crucial roles of discovery and profiling to determine who and what is on the network, what resource access should be given, and what action to take in response to a network threat (like a compromise or attack). ClearPass does this seamlessly by establishing a role and associated set of permissions that follow users and devices across wired, wireless and remote access, providing advance protection no matter how they connect.
Lets take a closer look.

## Slide 2
Agenda
Visibility
  Active Scanning
  Stakeholder Report
  Correcting/Creating Fingerprints
CPDI
Advanced 802.1X Wireless
  Endpoint Repository
  Time Source
  Isolation role
  Machine only + OnGuard
CPG Operator Login
Wired Monitor Mode
Lockdown
Wired DUR v VSA
Colorless Ports
MPSK
  Email notification
TACACS
IPv6
AOB
Notes: Authenticating is only one part of being able to control what is on your network. Just because a user or device is "authenticated", doesn't necessarily mean they are "authorized".
Authorizing users (for example: group membership), and devices (like a smart device or laptop) is essential and is a key ClearPass strength. Authorizing refers to what the user or device is "allowed to do" or "allowed to access". ClearPass does both! ClearPass Policy Manager delivers a precise and consistent role-based access privileges that adapts to the current circumstances.
As shown in the image here, a user with an organization-issued device with strong authentication, is given a wide range of access. The same user with a BYOD device (by policy), will have a reduced set of privileges. This is all configurable with the ClearPass Policy Manger which allows organizations to tune their policies based upon their security priorities, balanced with their goals to provide rich, comprehensive mobile experiences for their users.

## Slide 3: Visibility
Particularly on wired

## Slide 4
Passive Profiling
Relayed DHCP profiling
HTTP profiling – redir-web traffic to CPG portal page
  Easily spoofed
  Useful for more granular differentiation of device type
    eg iPhone v iPad
Infrastructure Information
  Aruba Controller Sensor – uses IFMAP
  Aruba Switch Device Fingerprinting – uses HTTPS
    Needs an local account on ClearPass with API write access
  Cisco Device Sensor – uses RADIUS Accounting
  Flows (netflows, ipfix, sflows)
    How well does this scale?
External device db
  MDM
  Infoblox
  Audit
  IDS/IPS
Notes: Data from a variety of sources show that increasing numbers of vulnerabilities in IT infrastructure are putting businesses and their data at significant risk.
Bring your own device (or: "BYOD"), cloud applications, and wireless mobility all converge to blur the concept of a "traditional perimeter" around the network – creating challenges to enterprise security -- controlling who can get on the network and what they are entitled to do.
And the risks and vulnerabilities are only increasing, as organizations embrace the use of IOT devices. Most of these devices don't utilize any standard set of security defenses and are rarely subjected to security testing or proactive control.

## Slide 5
Active Profiling
SNMP v1, v2c, v3
  Description
  Hostname
  IP Forwarding
  IP addresses
  MAC address
  ARP table
  LLDP Determines whether it is a router
  CDP
  VSA for Cisco and Aruba MIBs
SSH: Limited dialogues
  ClearPass
  Redhat Linux
  Aruba AOS
WMI – Destination TCP port 135
  Hostname
  OS version
  Active services
  Inactive services
  Running processes
  Record details in Endpoint attribute
    %{InstalledApplication:ApplicationName}
NMAP
  Default Scan TCP 135/3389
  Probes most common 1000 ports
  Only probes is response to ping
  Can be very slow!
OnGuard
Only probes on initial scan
Notes: Data from a variety of sources show that increasing numbers of vulnerabilities in IT infrastructure are putting businesses and their data at significant risk.
Bring your own device (or: "BYOD"), cloud applications, and wireless mobility all converge to blur the concept of a "traditional perimeter" around the network – creating challenges to enterprise security -- controlling who can get on the network and what they are entitled to do.
And the risks and vulnerabilities are only increasing, as organizations embrace the use of IOT devices. Most of these devices don't utilize any standard set of security defenses and are rarely subjected to security testing or proactive control.

## Slide 6
`
DHCP
ClearPass
Visibility & Profiling
Passive Monitoring / OnConnect
Switch sends SNMP MAC Notification trap

Device connects

Relay DHCP Request


Record first DHCP fingerprint

Probe device with SNMP, SSH, WMI

Record first positive response as fingerprint

If subsequent fingerprint changes: Potential spoof attack. Set “Conflict” attribute

Record MAC address
DHCP Response
`
SNMP/SSH/WMI
DHCP Request

ClearPass Actions

## Slide 7
Visibility & Profiling
Active Subnet Scan
Particularly useful to identify and monitor static IP addresses
DHCP
ClearPass
Scan subnet for IP address

ICMP
Probes SNMP, SSH and WMI

Reads ARP tables off Access Routers

Record first positive response as fingerprint

If subsequent fingerprint changes: Potential spoof attack. Set “Conflict” attribute

SNMP/SSH/WMI
ClearPass Actions
ARP
table

## Slide 8
Visibility & Profiling
Active Network Discovery Scan
Particularly useful to identify and monitor static IP addresses
DHCP
ClearPass
SNMP scan seed routers IP

ICMP
Reads hostname, LLDP, CDP, router and ARP tables

Probes ICMP responsive IPs using NMAP, SNMP, WMI and SSH

Record first positive response as fingerprint

Repeat above on found routers – down to specified hop depth

`
NMAP/SNMP/SSH/WMI
`
ClearPass Actions
If subsequent fingerprint changes: Potential spoof attack. Set “Conflict” attribute
Scan seed routes

## Slide 9
Define the scan techniques criteria
WARNING
Changing the details will not be applied to existing scans!!!
Have to update each scan
Define the IP range of the scan
Notes: Data from a variety of sources show that increasing numbers of vulnerabilities in IT infrastructure are putting businesses and their data at significant risk.
Bring your own device (or: "BYOD"), cloud applications, and wireless mobility all converge to blur the concept of a "traditional perimeter" around the network – creating challenges to enterprise security -- controlling who can get on the network and what they are entitled to do.
And the risks and vulnerabilities are only increasing, as organizations embrace the use of IOT devices. Most of these devices don't utilize any standard set of security defenses and are rarely subjected to security testing or proactive control.

## Slide 10
Define the type of the scans
Network Discovery
Subnet Scan
Notes: Data from a variety of sources show that increasing numbers of vulnerabilities in IT infrastructure are putting businesses and their data at significant risk.
Bring your own device (or: "BYOD"), cloud applications, and wireless mobility all converge to blur the concept of a "traditional perimeter" around the network – creating challenges to enterprise security -- controlling who can get on the network and what they are entitled to do.
And the risks and vulnerabilities are only increasing, as organizations embrace the use of IOT devices. Most of these devices don't utilize any standard set of security defenses and are rarely subjected to security testing or proactive control.

## Slide 11
NMAP Scan Setup
With NMAP disabled it will still scan these ports
This list can be expanded to have a more focused scan
WARNING
I believe when probing a device is the intervening router responds with ICMP Destination Unavailable:
ClearPass creates endpoint with this IP but empty fingerprint
Notes: Data from a variety of sources show that increasing numbers of vulnerabilities in IT infrastructure are putting businesses and their data at significant risk.
Bring your own device (or: "BYOD"), cloud applications, and wireless mobility all converge to blur the concept of a "traditional perimeter" around the network – creating challenges to enterprise security -- controlling who can get on the network and what they are entitled to do.
And the risks and vulnerabilities are only increasing, as organizations embrace the use of IOT devices. Most of these devices don't utilize any standard set of security defenses and are rarely subjected to security testing or proactive control.

## Slide 12: ClearPass User Experience: Endpoints Details
Do not rely on this Status – very unreliable
Use Accounting tab Status field

## Slide 13
Profiling Issues
Device has to respond to ICMP ping before probing
Subnet scanning large empty subnets very slow
  Reliant on timeouts
  Class-B takes 4-12 hours!!!
If credentials (SNMP, SSH, WMI) are incorrect: Records a null fingerprint!
If profiled and device’s subsequent probes fail: Does NOT raise Conflict
  ie SNMP fingerprinted as printer, hacker attaches spoofed device with SNMP disabled…
Editing underlying scan technique criteria (ie SNMP, SSH, WMI) is not automatically applied to the scanning mechanism (Discovery/Subnet)
  Each scanning mechanism has to be updated
Connected port very inaccurate
  Needs full authentication

## Slide 14
Debug
Enable debug Async-Netd Service
Look at file
  PolicyManagerLogs\async-netd\netprofiler.log
  PolicyManagerLogs\async-netd\netscan.log
    Only seem to update every 30 minutes
  Profiling: PolicyManagerLogs\async-netd\deviceprofiler.log
  PolicyManagerLogs\network-services\snmp-activity.log.0
Take network trace during scan
Notes: Data from a variety of sources show that increasing numbers of vulnerabilities in IT infrastructure are putting businesses and their data at significant risk.
Bring your own device (or: "BYOD"), cloud applications, and wireless mobility all converge to blur the concept of a "traditional perimeter" around the network – creating challenges to enterprise security -- controlling who can get on the network and what they are entitled to do.
And the risks and vulnerabilities are only increasing, as organizations embrace the use of IOT devices. Most of these devices don't utilize any standard set of security defenses and are rarely subjected to security testing or proactive control.

## Slide 15
ClearPass Operator Experience: Visibility
Choosing the cat/family/name shows the matching devices

## Slide 16: ClearPass Operator Experience: Endpoints
Effectively becomes an effective audit of everything on the network
These can all be exported to XML and updated accordingly
Best to only edit few this way!
See Stakeholder report

## Slide 17: Discovered NAS
Appear here if LLDP/CDP indicates it is a NAS (router/switch/ contoroller…
Must have a hostname to import!
Use interface that is used in requests (RADIUS/TACACS) request to ClearPass
NOTE
On importing does not automatically setup the SNMP credentials 
Import into NAD table

## Slide 18: Stakeholder Report
Two Reports
Devices observed during report/poll period/schedule
  Authenticated or profiled
  All devices seen typically in the last month or week
Devices not see during report/poll period/schedule
  Missing?
  All devices not seen typically in the last month or week

## Slide 19
PDF
Stakeholder
Report
Indication SNMP/SSH/WMI credentials incorrect or intervening router response ICMP Destination Host Unavailable
Static IP: Is this excessive? Missing DHCP relaying?
All devices assumed to be static IP until DHCP request seen
Learnt via active scanning (NMAP, SNMP, SSH, WMI)
No active scanning, or RADIUS Accounting Framed IP address
Why Unprofiled?
No matching fingerprint
No matching fingerprint!

## Slide 20
Detailed Endpoint Report
Validate Endpoints are legitimate
  Update status to either Known or Disabled
Import updated report into ClearPass
  Manual update using GIU
  Import updated CSV
    Use Aruba Solution Exchange
    https://ase.arubanetworks.com
  Update using RESTful API
Effectively becomes the network audit
Simple process to move to lockdown: Unknown Endpoints Blocked
Status, MAC
Location attempt
  Invariably found on an uplink
IP, Hostname
Fingerprint detail
Spoof detected
  Fingerprint changes
Accuracy of location unreliable until true authentication
Use Aruba Solution Exchange https://ase.arubanetworks.com/solutions/id/91
To convert this CSV to an XML import file

## Slide 21: Setup Stakeholder Report
Set to handle longer duration
Primarily for “unseen” devices

## Slide 22: Create Stakeholder Reports 6.8.x
Report1 Active Endpoints
Report2 Inactive Endpoints
Adhoc or scheduled report

## Slide 23: Fingerprints

## Slide 24
No Fingerprint – Manually one time correct
WARNING on Testing
If you delete an endpoint leave for 5mins before re-test
My webcam is reported as a Generic:
Correct fingerprint
But if I added a similar device it would still be mis-profiled

## Slide 25
Correct Webcam Profiled
Even thought the Webcam is an exact fit it always prefers the SmartPlug!?
Missing 42
This has been reported to TAC
WARNING
Prior to 6.8.3 this was unreliable
Add fingerprint would override the existing fingerprint!

## Slide 26
Update Webcam fingerprint
The existing fingerprint already has this
The Fingerprint Database shows custom match rules can be deleted
The existing fingerprint already has this

## Slide 27
My Amazon Echo Dot Fingerprinted as Kindle!
Not clear why this is matched!
Clearly this “contain” is not explicit – ie my fields do not match all the fields

## Slide 28
My Amazon Echo Dot Fingerprinted as Kindle!
Echo fingerprint missing this MAC address
Echo fingerprint missing this MAC address
OUI is missing
This can only be corrected by reporting to TAC

## Slide 29
WARNING On Custom Fingerprint
You can then associate this as done in the previous slides
WARNING
Do not associate a blank fingerprint with a device
This will likely match a raft of things!!!

## Slide 30: ClearPass Device Insight

## Slide 31
Collector Placement
NOTE
If asymmetric communications mirror both on to different CPDI SPAN ports and CPDI will rationalize

## Slide 32
Active Scanning Passive Monitoring
Defined segments
  Scheduled scans
Techniques
  NMAP
    Does not require to respond to ping
  SNMP
  SSH
    Dialogues: AOS, ClearPass & RedHat
  WMI
SPAN port traffic analysis
DHCP profiling
Infrastructure flows analysis

## Slide 33: Operator Experience

## Slide 34
Home Page
Unclassified devices
Auto-Classified
Classified Grouping
Use button to load more groups

## Slide 35: New devices appearing
Devices seen in last month
Devices seen in last day

## Slide 36: Find particular device
Can use MAC address, IP address, Hostname
This information will be injected into ClearPass

## Slide 37: Drill down in to device
Cisco switch group size
Status
Online
Idle
Offline
Category filters
Number of Cisco switches

## Slide 38: Drill into device
Drill down in
to the details

## Slide 39: Find all switches with Telnet enabled - 1
Number of Cisco switches with Telnet enabled
To see these devices click the ICON

## Slide 40: Drill into device
Drill down in to the details
Look at details for this switch
Look at details for this switch
Shows a more detailed breakdown with session usage information

## Slide 41: Drill into device
Generate report of devices in this cluster - 1

## Slide 42: Generate report of devices in this cluster - 2

## Slide 43: Create a Tag
Device’s tag information will be injected into ClearPass for refined policy
WARNING
Once applied this can take a few minutes to update

## Slide 44: Generic Groups

## Slide 45: Components of devices are shown
Common fields in”grey”
OUI and Browser User-Agent

## Slide 46: Classify cluster: using generic categories

## Slide 47: Classify cluster: using rules - 1
TCP port 7680 = Pando Media Public Distribution

## Slide 48: Classify cluster: using rules - 2

## Slide 49: Look at User Classified Devices
Look at the User Classified Devices
Devices with TCP 7860 open

## Slide 50: CPDI/ClearPass Integration

## Slide 51: ClearPass & CPDI Integration
WARNING
Enabling this disables ClearPass’ native scanning

## Slide 52: ClearPass & CPDI Integration Better CDPI Visibility

## Slide 53: ClearPass & CPDI Integration Better Visibility in ClearPass
Attributes from CDI
Policy can be built on these

## Slide 54: Review Operation
Example 802.1X Wireless
with Windows PC doing machine and user
and TLS certificates

## Slide 55: Services
NOTE
The service is matched on the first packet received.
TLS v PEAP/MSCHAP/etc are negotiated later is RADIUS exchange
Service Disabled
Service in Monitor mode: Only sends Accept/Reject

## Slide 56: Example Service
A matched authentication source will automatically be authorization source
WARNING
The others will not!
Because of this you may have to explicitly add them as authorization source
NOTE
The service is matched on the first packet received
TLS v PEAP/MSCHAP/etc are negotiated later is RADIUS exchange
Using groups is an effective mechanism to get granular policies
Connection SSID supports all manufacturers

## Slide 57: TLS Authentiation
A matched authentication source will automatically be authorization source
WARNING
The others will not!
Because of this you may have to explicitly add them as authorization source
Using groups is an effective mechanism to get granular policies
Connection SSID supports all manufacturers
This validates based on certificate is not expired
Can’t edit things in [ ]
One exception [Role Mappings]!!!
Copy and adapt
Will use certificiates OCSP URL to real time validate
NOTE If CRL file expires – ClearPass will Reject all associated request!!!
Alert event appears in Events:
CRL for the CA %s has expired. Certificate verifications against this CA will fail till the CRL is…

## Slide 58: Roles and Role Mapping
Passing roles to Enforcement make for better Operator understanding
Totally new device will not exist in the database
Evaluate All: I want to pass roles that explain to the operator why the enforcement policy is assigned
Default is match first!!!
Time at midnight this morning

## Slide 59: Customer AD LDAP – Account Disabled
Returns the DN if the account is disabled
Notes: Disabled AD Account: (&(sAMAccountName=%{Authentication:Username})(!(userAccountControl:1.2.840.113556.1.4.803:=2)))(objectClass=user))

## Slide 60: Direct Roles from Endpoint Repository
Pass Status (Disabled, Unknown, Known) directly into Enforcement Policy
Pass profiled Category directly into Enforcement Policy
Simplify Role Mapping logic by passing some attributes directly
Only use attributes that have clear names – IsProfiled is a bad example True/False
Make sure this is set to 0
Used to be set to 300

## Slide 61: Time Source
Name of attribute within ClearPass
SQL to get specific filter
WARNING
Editing/updating existing filters may to be over-written during upgrade
Create your own filters for more flexibility
These should not be affected by upgrades
Microsoft time is based on Pope Gregory VIII and based on 100 ms steps from 00:00:00 Jan 1st 1601

## Slide 62: Enforcement Policy - 1
First-applicable is deterministic – far easier to understand
Default is match all!!!
Keep the logic simple for easier understanding
Create bespoke reject rule
AccessTracker’s Username will report !!!Guest!!! Fred Blogs
Use the successful machine authentication to make the device known within the Endpoint Repository
Use Drop to force re-transmission of request…
WARNING
Depending on NAS this might not work!!!
Might be easier to apply the correct role – but this usually needs more logic

## Slide 63: Enforcement Policy - 2
Only report to operator once a day
Reject, email operator & set that it’s been “Reported”
Records exactly when it happened
NOTE Role Reported =
Endpoint:Error GREATER_THAN %{Authorization:[Time Source]:FirstThing DT}
Hence will only trigger that day
Email the operator that the device is disabled - discussed later

## Slide 64: Enforcement Policy – Context Profiles
Only applied if NAS in the Controller group
Only applied if NAS in the IAP group

## Slide 65: Enforcement Policy – Cluster Wide Parameters
NOTE
When using newer Context Server enable Post-Auth v2
WARNING
If no UPS on appliance set this to normal or full to minimise db corruption on power outage
This does directly affect appliance performance

## Slide 66: Enforcement Policy – Isolation Portal
Web-redirect to isolation page

## Slide 67: Enforcement Policy – Isolation Portal 2
{assign var=MDM_State value='MDM Enabled'}
{if $_endpoint.$MDM_State == 'false'}
MDM Enabled = False<BR>
{/if}
{/if}
</p>
<p>Network Details<BR>
{if $extra_fields.essid}
NAS name&nbsp{$extra_fields.vcname}&nbsp({$extra_fields.ip})<BR>
Wireless SSID&nbsp{$extra_fields.essid}<BR>
AP&nbsp{$extra_fields.apname}<BR>
{/if}
</p>
</div>
<!--
{dump var=$action export=html}
{dump var=$source export=html}
{dump var=$result.error export=html}
{dump var=$result.message export=html}
{dump var=$timestamp export=html}
{dump var=$site_ssid export=html}
{dump var=$site_wpa_key export=html}
{dump var=$u export=html}
{dump var=$c export=html}
{dump var=$_wpl export=html}
{dump var=$_endpoint export=html}
{dump var=$_user export=html}
{dump var=$_param export=html}
{dump var=$_login_args export=html}
{dump var=$_url export=html}
{dump var=$extra_fields export=html}
-->
<link href="external/font-awesome/css/font-awesome.min.css" rel="stylesheet" type="text/css">
<div style="width: 300px; margin: 0 auto; text-align: center;">
<p><span class="fa fa-user-times" style="font-size: 200px; color: #0885bf;"></span>
<h1 style="margin: 20px 5px;">Isolation!</h1>
<p>There is a problem with your client.</p>
<p>Click <a href=\"https:/clearpass.hpearubademo.com/guest/mac_create.php?mac={$_endpoint.mac_address}&device_name={$_endpoint.profile_device_name}\">here</a> to register this device for the MPSK SSID</p></br>
<p>Please contact IT admin - tell them the following information</p>
<p>MAC address&nbsp{$_endpoint.mac_address}<BR>
ClearPass status&nbsp{$_endpoint.status}<BR>
IP address&nbsp{$_endpoint.profile_ip}<BR>
Hostname&nbsp{$_endpoint.profile_hostname}<BR>
Category&nbsp{$_endpoint.profile_device_category}<BR>
Family&nbsp{$_endpoint.profile_device_family}<BR>
Type&nbsp{$_endpoint.profile_device_name}<BR>
Posture
{if $_endpoint.Posture_Status}
&nbsp{$_endpoint.Posture_Status}&nbspat&nbsp{$_endpoint.Last_Posture}
{else} &nbspUnknown
{/if}
</p>
{if $_endpoint.Source == 'airwatch'}
<p>
Airwatch managed device<BR>
Expires&nbsp{$_endpoint.Expire}<BR>
Username&nbsp{$_endpoint.Username}<BR>
{if $_endpoint.Blacklist == 'true'}
Blacklist = True<BR>{/if}
{if $_endpoint.Compliance != 'Compliant'}
Compiance = {$_endpoint.Compliance}<BR>{/if}
{if $_endpoint.Compromised == 'true'}
Compromised = True<BR>{/if}
Shows available variables
URL to CPG login to enrol this device
Endpoint attributes accessibly using _endpoint variables

## Slide 68: Tune Access Tracker
New 6.8
NAS Name – reliant on RADIUS NAS-Id attribute
New 6.8
Shows what Profiles are applied

## Slide 69: Improved RoleMapping & Enforcement Policy Editing
2) Copy condition
1) Select condition
3) Creates identical condition below…

## Slide 70
Corp Network
NAS
Access router
Corporate
NAC
Device
7) RADIUS Rsp
Accept
1) Device connects
2) AOS initiates EAPoL to device
3) Device responds with certificate
8) AOS applies VLAN to port
4) Converts EAPoL into RADIUS Req TLS
6) ClearPass determines role to assign
5) ClearPass verifies Corp cert, not expired and not in CRL
or OSCP is good
AD
OCSP check
CRL
Db
Wireless 802.1X TLS Authentication

## Slide 71
ClearPass
Service 1
Policy Manager Login Service
Service 5
Aruba Wifi Infrastructure Access Service
Service 19
Wireless 802.1X Auth
Authorization
Authenticate
Cert expired?
OCSP or CRL are good?
Role
Enforcement
Policy
Network Access Server (Controller)
Good
Cert
Role Mapping
Blocked
Spoof
Machine
Condition#1
Blocked
Condition#2
Spoof
Condition#3
Machine Auth Only
Corp VLAN
Yes
RADIUS
Request
Match service
Bad Cert
RADIUS
Reject
RADIUS
Accept+VLAN+dACL /Reject
Internal dACL
Accept
User
ClearPass Processing of 802.1X TLS Auth

## Slide 72: Access Tracker: Corporate PC Login
Tune
Machine login
User login with previous cached machine login
Cached machine login
User login
Assign machine only role
Assign machine & user role
Inject User & IP details into firewall
Default to 24 hours config in ServiceParamPolicyServer

## Slide 73: Access Tracker: Input fields
Tune
If attribute not in Input field can’t be used

## Slide 74: Access Tracker: Output fields
Tune

## Slide 75: Access Tracker: Link to Endpoints
Tune

## Slide 76: AOS

## Slide 77: Machine Only Authentication: Identify the User
These will effectively track machine/user login
How can the username inject into upper-layer???
Could do via syslog???
OnGuard Persistent Agent must be installed
Does not use any license

## Slide 78: Cleanup Intervals
Purge unknown endpoints!
How long do I need to hold an expired guest?

## Slide 79: Optimised CPG Operator Login
Customizable Operator pages

## Slide 80: Staff Guest Operator
Home page
Flexible device enrolment
Only show devices register to this user
Guest management
Allows staff to create guest accounts and enrol device

## Slide 81: Student Guest Operator
Home page
Create Guest account
Enrol devices
Only show devices register to this user
Allows students to you to enrol their devices
Guest account is their unique password

## Slide 82: Student Guest Operator
https://cppm.hpearubademo.com/guest/mac_create.php?mac=000011112222&device_name=Test
Isolation page has link to enrol this device

## Slide 83: Guest Operator Logins service
admin_privileges=MPSK Student Device Registration
admin_privileges=Device Registration

## Slide 84: Guest Operator Logins service
CPG Logs
AccessTracker

## Slide 85: CPG Profiles
Student
Staff
Translation rules will apply the admin_privileges value

## Slide 86: Student Profile - 1

## Slide 87: Student Profile - 2

## Slide 88: Student Forms – mactrac_create_2
Page look
Initial Value=array ( 'generator' => 'GeneratorFromRequest', 'generator_args' => 'device_name',)
Initial Value = 5
Initial Value = 1
This will match URL attribute device_name=xyz

## Slide 89: Student Forms – create_user_3
Page look
Initial Value= 1
Initial Value = sponsor_email
Initial Value = now()
Initial Value = 1y
Initial Value = 5 associates to Student in RoleMapping [Guest Roles]

## Slide 90: Student Forms – mactrac_edit
Page look
Nothing special

## Slide 91: Student Forms – mactrac_list
Page look
Could remove the mpsk and mpsk_enable fields

## Slide 92: Student Forms – guest_users_2
Page look

## Slide 93: Portal page flexibility
Adds more flexibility to URL processing

## Slide 94: Allow Password Display
By default passwords are disabled

## Slide 95: CPG Operator Login with SAML
WARNING
Struggling to get this working on 6.8.x!

## Slide 96
SAML: Customizable CPG Operator Login Page
Could be Azure
ClearPass acting as SAML ServiceProvider for CPG Operator
ClearPass acting as SAML Identity Provider

## Slide 97
SAML IdP: Create Identity Provider

## Slide 98
SAML IdP: Login Service

## Slide 99
SAML SP: Set GuestOperators as a Service
Any browse to a page/form controlled via Guest will be forced to authenticate

## Slide 100
SAML SP: CPG Login Service
mail=
%{Authorization:AD:Email}
Refers to CPG Operator Profiles
Refers to CPG Operator Profiles
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 101
Enable New
Portal Pages
New skins
Use
shortcut
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 102: Wired Monitor Mode Safely Develop Policy

## Slide 103
Monitor Mode – Option 1
Aruba Switches
Safely develop policy for both 802.1X and MAC-Auth
Control at ClearPass
  Switch configured with 802.1X & MAC Auth
  ClearPass
    802.1X in Monitor mode
    MAC Auth using Method=“Allow All” and in Monitor mode
      Always sends basic RADIUS Accept
  Switch must run RADIUS with no precedence (default)
    If endpoints has a 802.1X supplicant will get both 802.1X and MAC Auth request
    Switch will honour RADIUS Accept in preference to RADIUS Reject
      Apply port’s default VLAN
    Default operation
Notes: Authenticating is only one part of being able to control what is on your network. Just because a user or device is "authenticated", doesn't necessarily mean they are "authorized".
Authorizing users (for example: group membership), and devices (like a smart device or laptop) is essential and is a key ClearPass strength. Authorizing refers to what the user or device is "allowed to do" or "allowed to access". ClearPass does both! ClearPass Policy Manager delivers a precise and consistent role-based access privileges that adapts to the current circumstances.
As shown in the image here, a user with an organization-issued device with strong authentication, is given a wide range of access. The same user with a BYOD device (by policy), will have a reduced set of privileges. This is all configurable with the ClearPass Policy Manger which allows organizations to tune their policies based upon their security priorities, balanced with their goals to provide rich, comprehensive mobile experiences for their users.

## Slide 104
Monitor Mode – Option 2
Cisco Switches
Safely develop policy for both 802.1X and MAC-Auth
Control at Switch
Infrastructure ignores RADIUS Response
  Switch configured with 802.1X & MAC Auth
  Switch ports configured with Open Auth
  ClearPass will send necessary RADIUS Rsp
  Switch will ignore RADIUS Rsp
    Applies port’s default VLAN
Interface FastEthernet0/1
authentication open
NOTE
This should not be confused with the Aruba switch’s “open auth” command
This immediately puts the device into the “open auth” VLAN/Role until it gets a RADIUS Response…
Notes: Authenticating is only one part of being able to control what is on your network. Just because a user or device is "authenticated", doesn't necessarily mean they are "authorized".
Authorizing users (for example: group membership), and devices (like a smart device or laptop) is essential and is a key ClearPass strength. Authorizing refers to what the user or device is "allowed to do" or "allowed to access". ClearPass does both! ClearPass Policy Manager delivers a precise and consistent role-based access privileges that adapts to the current circumstances.
As shown in the image here, a user with an organization-issued device with strong authentication, is given a wide range of access. The same user with a BYOD device (by policy), will have a reduced set of privileges. This is all configurable with the ClearPass Policy Manger which allows organizations to tune their policies based upon their security priorities, balanced with their goals to provide rich, comprehensive mobile experiences for their users.

## Slide 105
Monitor Mode – Option 3
All Switches
Safely develop policy for MAC-Auth only
Control at ClearPass
MAC-Auth only
  Switch configured with MAC Auth only
  ClearPass
    MAC Auth using Method=“Allow All” and in Monitor mode
      Always sends basic RADIUS Accept
  Switch will apply port’s default VLAN
Notes: Authenticating is only one part of being able to control what is on your network. Just because a user or device is "authenticated", doesn't necessarily mean they are "authorized".
Authorizing users (for example: group membership), and devices (like a smart device or laptop) is essential and is a key ClearPass strength. Authorizing refers to what the user or device is "allowed to do" or "allowed to access". ClearPass does both! ClearPass Policy Manager delivers a precise and consistent role-based access privileges that adapts to the current circumstances.
As shown in the image here, a user with an organization-issued device with strong authentication, is given a wide range of access. The same user with a BYOD device (by policy), will have a reduced set of privileges. This is all configurable with the ClearPass Policy Manger which allows organizations to tune their policies based upon their security priorities, balanced with their goals to provide rich, comprehensive mobile experiences for their users.

## Slide 106
ClearPass
Service 1
Policy Manager Login Service
Service 5
Aruba Wifi Infrastructure Access Service
Service 18
Wired
MAC Auth
Authorization
Authenticate
Role
Enforcement
Policy
Network Access Server (Switch, Controller, etc)
processes
Role Mapping
Blocked
Spoof
Known
Condition#1
Blocked
Condition#2
Spoof
Condition#3
Known WebCam
Web VLAN
Yes
RADIUS
Request
Match service
All devices
RADIUS
Accept
Web dACL
Accept
WebCam
Yes
ClearPass Processing of MAC Auth
Monitor Mode with “Allow All”

## Slide 107
Monitor Mode
Policy Definition
Allow all connecting devices
Control within Enforcement Policy
Policy Enforcement is processed and reported in AccessTracker but not enforced
Does not act on Enforcement Policy
Just sends Accept/Reject
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 108
ClearPass Access Tracker
SEEL-V2-demo# show port-access clients 1 detailed
Port Access Client Status Detail
Client Base Details :
Port : 1 Authentication Type : mac-based
Client Status : authenticated Session Time : 97 secs
Client Name : 98d6bb0a31f7 Session Timeout : 0 secs
MAC Address : 98d6bb-0a31f7
IP : 169.254.197.55
Access Policy Details :
COS Map : Not Defined In Limit Kbps : Not Set
Untagged VLAN : 1 Out Limit Kbps : Not Set
Tagged VLANs : No Tagged VLANs
Port Mode : 100FDx
RADIUS ACL List : No Radius ACL List
Auth Order : 8021x, Mac-Auth
Auth Priority : 8021x, Mac-Auth
LMA Fallback : Disabled
NOTE: While in Monitor Mode only sends RADIUS Accept/Reject
Roles & Enforcements are processed but not applied
This allows for development of Roles and Enforcements without concern of breaking operation
Switch reports
Port’s default VLAN applied

## Slide 109
ClearPass Reports
Status, MAC
Connected at, Connection status, Disconnected at
Location: Media, NAS, Port/SSID
IP, Hostname
Fingerprint detail
Spoof detected
Volume usage

## Slide 110: Debug

## Slide 111
Nothing Coming Into AccessTracker?
Look in
Password mismatch reported here

## Slide 112
Still Nothing Coming In?
tcpdump of all the interfaces
Only up to 10 minutes
Provides filtering

## Slide 113
RADIUS Erroring
AccessTracker Event will have much more detail
AccessTracker event will typically have a Alert tab
Records the config, event and debug information in a zip file
If Alert tab but LoginStatus=Accept – Only minor issue(s)
WARNING
This significantly increase the load on ClearPass
Most common: Radius Server &
Async network service – for profiling and context servers

## Slide 114
All Logs
Download gzip file
This will be big!
Profiling and Context Server info
RADIUS details

## Slide 115
Aruba Switch
Traditional VSA v DUR
If using traditional mode
  Don’t use order and priority
    No Failed 802.1X VLAN
Notes: Authenticating is only one part of being able to control what is on your network. Just because a user or device is "authenticated", doesn't necessarily mean they are "authorized".
Authorizing users (for example: group membership), and devices (like a smart device or laptop) is essential and is a key ClearPass strength. Authorizing refers to what the user or device is "allowed to do" or "allowed to access". ClearPass does both! ClearPass Policy Manager delivers a precise and consistent role-based access privileges that adapts to the current circumstances.
As shown in the image here, a user with an organization-issued device with strong authentication, is given a wide range of access. The same user with a BYOD device (by policy), will have a reduced set of privileges. This is all configurable with the ClearPass Policy Manger which allows organizations to tune their policies based upon their security priorities, balanced with their goals to provide rich, comprehensive mobile experiences for their users.

## Slide 116
Yes
Typical Aruba switch handling authentications - 1
Incoming Authentication
OpenAuth?
Apply
OpenAuth
role
Start RADIUS Auth
RADIUS
reachable?
Tried all
servers?
Yes
Yes
No
Apply Critical VLAN
Process Auth
No
No
Yes
Default 802.1X & MAC-Auth come out at same time
Use auth-order and priority to change this behaviour
This is applied immediately!
Critical VLAN
defined?
Yes
First defined Data and Voice VLANs applied
If RADIUS recovers these devices will be proactively forced to re-auth
But NOT 802.1X!!!
If using DUR must use Critical User-Role
– see later

## Slide 117
Apply Role/ACL/ VLAN/FilterID
Apply 802.1X auth-vid
Apply Role/ACL/ VLAN/FilterID
Apply MAC-Auth auth-vid
Apply MAC-Auth unauth-vid
Yes
Yes
No
No
Yes
Yes
No
Typical Aruba switch handling
authentications traditional - 2
Accept
Reject
Accept
Reject
Assume both 802.1X and MAC-Auth coming in at around same time
Benefit: Quick response
Weakness: Increased RADIUS load and logs in ClearPass
Process Auth
802.1X
response?
RADIUS
Success?
If Role/
ACL/VLAN/ FilterID
If Role/
ACL/VLAN/ FilterID
RADIUS
Success?
MAC-Auth response

## Slide 118
Apply Role/ACL/ VLAN/FilterID
Apply 802.1X auth-vid
Apply Role/ACL/ VLAN/FilterID
Apply MAC-Auth auth-vid
Apply MAC-Auth DUR initial role
Yes
Yes
No
No
Yes
Yes
No
Typical Aruba switch handling
authentications DUR - 3
Accept
Reject
Accept
Reject
Assuming Priority 802.1XMAC-Auth: Timeout controlled by port’s 802.1X
wait period
= tx-period*retrains
Default 30*4=120s
Set tx-period =5s
Process Auth
802.1X
response?
RADIUS
Success?
If Role/
ACL/VLAN/ FilterID
If Role/
ACL/VLAN/ FilterID
RADIUS
Success?
MAC-Auth response

## Slide 119
Typical Aruba Switch
RADIUS Configuration
dhcp-snooping
dhcp-snooping authorized-server <CPPM-IP>
dhcp-snooping vlan 10-20 30 40 50 60
interface 8
dhcp-snooping trust
exit
ip client-tracker
ip client-tracker probe-delay 15
radius-server host <CPPM-IP> key <pass>
aaa server-group radius "CPPM" host <CPPM-IP>
radius-server host <CPPM-IP> dyn-authorization
radius-server host <CPPM-IP> time-window plus-or-minus-time-window
radius-server host <CPPM-IP> time-window 30
radius-server tracking enabled
radius-server tracking user-name <user> password <pass>
aaa account net start-stop radius server-gr "CPPM"
aaa accounting update periodic 5
aaa port-access 1-5 controlled-direction in
Adds IP address into RADIUS Accounting
RADIUS Accounting to ClearPass
Switch must be within 5min of ClearPass for CoA to work
RADIUS Accounting Interim period
Define ClearPass RADIUS host
Validate ClearPass is working
Need CPPM Service using PAP NAS-Port-Type=5 (Virtual)
Service-Type=7 (NAS-Prompt-User)
User-Name=<username>
Defaults to probes every 300s, 3 retries
If using AD account effectively probes backend system
Helps capture IP of static IP devices
uplink
Force auth on ingress traffic
Notes: If the RADIUS server is not accessible it will not allow the “radius-server host <IP> key <pass>” to be added
To add secondary and tertiary RADIUS server replicate the necessary lines
When pasting config in:
1) Even with “include credentials” password not store on
radius-server tracking user-name <user> password <pass>
radius-server cppm identity <user> key <pass>
2) Can’t just paste in – this needs user interaction
aaa authentication port-access eap-radius server-group "CPPM" authorized

## Slide 120
Port’s MAC address limit
Re-transmit 4 times every 30s
Server response timeout
Port’s default auth VLAN
If quiet device logged out after default 300s For very quiet devices - increase
Typical Aruba Switch Traditional
MAC-Auth RADIUS Configuration
aaa authentication mac-based chap-radius server-group "CPPM" authorized
aaa port-access mac-based 1-5
aaa port-access mac-based 1-5 addr-limit 2
aaa port-access mac-based 1-5 max-request 3
aaa port-access mac-based 1-5 server-timeout 10
aaa port-access mac-based 1-5 auth-vid 50
aaa port-access mac-based 1-5 logoff-period 3600
aaa port-access mac-based 1-5 unauth-vid 60
aaa port-access mac-based 1-5 unauth-period 15
aaa port-access 1-5 critical-vlan data-vlan 10
aaa port-access 1-5 critical-vlan voice-vlan 20
Enable MAC-Auth on these ports
Enable MAC-Auth to ClearPass
No response VLANs
If not defined defaults to first data & voice VLANs defined
Port’s failed auth VLAN
Notes: When pasting config in:
1) Even with “include credentials” password not store on
radius-server tracking user-name <user> password <pass>
radius-server cppm identity <user> key <pass>
2) Can’t just paste in – this needs user interaction
aaa authentication port-access eap-radius server-group "CPPM" authorized

## Slide 121
Port’s MAC address limit
Re-transmit 4 times every 30s
Server response timeout
If quiet device logged out after default 300s For very quiet devices - increase
Typical Aruba Switch DUR
MAC-Auth RADIUS Configuration
aaa authentication mac-based chap-radius server-group "CPPM" authorized
aaa port-access mac-based 1-5
aaa port-access mac-based 1-5 addr-limit 2
aaa port-access mac-based 1-5 max-request 3
aaa port-access mac-based 1-5 server-timeout 10
aaa port-access mac-based 1-5 logoff-period 3600
Enable MAC-Auth on these ports
Enable MAC-Auth to ClearPass
Notes: When pasting config in:
1) Even with “include credentials” password not store on
radius-server tracking user-name <user> password <pass>
radius-server cppm identity <user> key <pass>
2) Can’t just paste in – this needs user interaction
aaa authentication port-access eap-radius server-group "CPPM" authorized

## Slide 122
Typical Aruba Switch
802.1X RADIUS Configuration
aaa authentication port-access eap-radius server-group "CPPM" authorized
aaa port-access authenticator active
aaa port-access authenticator 1-5
aaa port-access authenticator 1-5 tx-period 5
aaa port-access authenticator 1-5 server-timeout 10
aaa port-access authenticator 1-5 auth-vid 10
aaa port-access authenticator 1-5 client-limit 2
tx-period (30s) * retrans (3) - default 120s
Set tx-period=5s: timeout after 20s
default 300s timeout
default auth VLAN
Port’s MAC address limit
Enable 802.1X on these ports
Enable 802.1X
to ClearPass
Notes: When pasting config in:
1) Even with “include credentials” password not store on
radius-server tracking user-name <user> password <pass>
radius-server cppm identity <user> key <pass>
2) Can’t just paste in – this needs user interaction
aaa authentication port-access eap-radius server-group "CPPM" authorized
comprehensive mobile experiences for their users.

## Slide 123
No response from ClearPass!
aaa authentication mac-based chap-radius server-group "CPPM"
aaa authentication port-access eap-radius server-group "CPPM"
aaa authentication mac-based chap-radius server-group "CPPM" authorized
aaa authentication port-access eap-radius server-group "CPPM" authorized
aaa authentication mac-based chap-radius server-group "CPPM" cached-reauth
aaa authentication mac-based 1-8 cached-reauth-period 86400
aaa authentication port-access eap-radius server-group "CPPM" cached-reauth
aaa authentication authenticator 1-8 cached-reauth-period 86400
Leaves device in limbo
Assigns the Critical VLAN/User-Role
Assigns the device’s previous cached VLAN/User-Role
Timeout range 1s - 86 years!!!
Default ?
If no role exists what happens???

## Slide 124
Enable Downloadable User Roles
radius-server cppm identity "<username>" key "xyz"
policy user "PERMIT_ALL"
10 class ipv4 "ALLOW_ALL" action permit
exit
aaa authorization user-role name "Default"
policy "PERMIT_ALL"
reauth-period 3600
vlan-id 10
vlan-id-tagged 20
exit
aaa authorization user-role enable download
aaa authorization user-role initial-role "Default“
aaa port-access 1-5 auth-order authenticator mac-based
aaa port-access 1-5 auth-priority authenticator mac-based
aaa port-access 1-5 critical-auth user-role “PERMIT_ALL“
aaa port-access 1-5 initial-role “PERMIT_ALL"
Generic allow all ACL
Define account used by DUR to HTTPS into ClearPass to pull down role
Role with the generic allow all ACL with tagged and untagged VLANs
Enable DUR
Default sends both 802.1X and MAC Auth at similar time
Prefers Accept over Reject & 802.1X over MAC-Auth
Default local-role for port
Local-role applied if REJECT or no CPPM response
Notes: When pasting config in:
1) Even with “include credentials” password not store on
radius-server tracking user-name <user> password <pass>
radius-server cppm identity <user> key <pass>
2) Can’t just paste in – this needs user interaction
aaa authentication port-access eap-radius server-group "CPPM" authorized
comprehensive mobile experiences for their users.

## Slide 125
Debugging Aruba Switch
Debug messages appear on switch CLI
This will give a raft of events including the EAPoL
debug security port-access authenticator debug event debug destination session debug security radius-server
Remove above commands
undo debug security port-access authenticator undo debug event undo debug destination session undo debug security radius-server
Mirror all traffic from port 1 to port 6
mirror 1 port 6
interface 2
monitor all both mirror 1
exit
Bounce port
int 16 dis
int 16 en
Show interface 16 status
show run int 16
Notes: When pasting config in:
1) Even with “include credentials” password not store on
radius-server tracking user-name <user> password <pass>
radius-server cppm identity <user> key <pass>
2) Can’t just paste in – this needs user interaction
aaa authentication port-access eap-radius server-group "CPPM" authorized
comprehensive mobile experiences for their users.

## Slide 126
DUR v Local Roles via ZTP
DUR highly dynamic
  Also if device limited on memory – older switch
    If running short purged oldest applied DUR
      Could cause issue! Errors in switch log
  To assign DUR must use HPE-CPPM-Role attribute = <role to download>
Static local roles
  Possibly deployed using ZTP (Zero Touch Provisioning)
  To assign local role must use HPE-User-Role attribute = <role name>
Notes: When pasting config in:
1) Even with “include credentials” password not store on
radius-server tracking user-name <user> password <pass>
radius-server cppm identity <user> key <pass>
2) Can’t just paste in – this needs user interaction
aaa authentication port-access eap-radius server-group "CPPM" authorized
comprehensive mobile experiences for their users.

## Slide 127: Lock Down

## Slide 128
Only Allow Known Devices
NAS actions RADIUS Response: Accept/Reject
  Unknown device rejected
  ClearPass
    Reliant on device’s status within Endpoint database
    MAB service: Allow Known
  Cisco: Switch port in OpenAuth disabled
  Aruba: No changes
Default port/SSID VLAN assigned
Notes: Authenticating is only one part of being able to control what is on your network. Just because a user or device is "authenticated", doesn't necessarily mean they are "authorized".
Authorizing users (for example: group membership), and devices (like a smart device or laptop) is essential and is a key ClearPass strength. Authorizing refers to what the user or device is "allowed to do" or "allowed to access". ClearPass does both! ClearPass Policy Manager delivers a precise and consistent role-based access privileges that adapts to the current circumstances.
As shown in the image here, a user with an organization-issued device with strong authentication, is given a wide range of access. The same user with a BYOD device (by policy), will have a reduced set of privileges. This is all configurable with the ClearPass Policy Manger which allows organizations to tune their policies based upon their security priorities, balanced with their goals to provide rich, comprehensive mobile experiences for their users.

## Slide 129: VLAN Switching

## Slide 130
RADIUS Accept with VLAN Details
NAS actions RADIUS Response: Accept/Reject & Applies VLAN to port/vport
  ClearPass
    Reliant on Status within Endpoint database
    MAB service: Allow Known
  Cisco: Switch port in OpenAuth disabled
  Aruba: No changes
Assign VLAN
Notes: Authenticating is only one part of being able to control what is on your network. Just because a user or device is "authenticated", doesn't necessarily mean they are "authorized".
Authorizing users (for example: group membership), and devices (like a smart device or laptop) is essential and is a key ClearPass strength. Authorizing refers to what the user or device is "allowed to do" or "allowed to access". ClearPass does both! ClearPass Policy Manager delivers a precise and consistent role-based access privileges that adapts to the current circumstances.
As shown in the image here, a user with an organization-issued device with strong authentication, is given a wide range of access. The same user with a BYOD device (by policy), will have a reduced set of privileges. This is all configurable with the ClearPass Policy Manger which allows organizations to tune their policies based upon their security priorities, balanced with their goals to provide rich, comprehensive mobile experiences for their users.

## Slide 131
Comware VSA disabled by default
Notes: Authenticating is only one part of being able to control what is on your network. Just because a user or device is "authenticated", doesn't necessarily mean they are "authorized".
Authorizing users (for example: group membership), and devices (like a smart device or laptop) is essential and is a key ClearPass strength. Authorizing refers to what the user or device is "allowed to do" or "allowed to access". ClearPass does both! ClearPass Policy Manager delivers a precise and consistent role-based access privileges that adapts to the current circumstances.
As shown in the image here, a user with an organization-issued device with strong authentication, is given a wide range of access. The same user with a BYOD device (by policy), will have a reduced set of privileges. This is all configurable with the ClearPass Policy Manger which allows organizations to tune their policies based upon their security priorities, balanced with their goals to provide rich, comprehensive mobile experiences for their users.

## Slide 132
Dynamically handling quiet devices
NOTE
Does not look possible via HPE VSA
With DUR if you know the device needs a longer timeout dynamically assign logout period
Default 300s max 9999999s! (115 days)
aaa port-access mac-based 1-5 logoff-period 3600
On the switch you can define a longer logoff period – default 300s
Notes: When pasting config in:
1) Even with “include credentials” password not store on
radius-server tracking user-name <user> password <pass>
radius-server cppm identity <user> key <pass>
2) Can’t just paste in – this needs user interaction
aaa authentication port-access eap-radius server-group "CPPM" authorized
comprehensive mobile experiences for their users.

## Slide 133
Really Quiet Device
Force device to use DHCP with shorter lease
If using static IP
  Possibly get a device to poll it
    eg Comware5130 to poll using a ARP scan script
  Possibly use ClearPass profiling to scan device on regular basis
dis sched job arpscan
Job name: arpscan sys int vl 3711 ip add 10.185.208.3 24 arp scan ip add 10.187.208.10 24 arp scan ip add 10.185.209.3 24 arp scan ip add 10.184.208.4 24 arp scan undo ip add
Notes: When pasting config in:
1) Even with “include credentials” password not store on
radius-server tracking user-name <user> password <pass>
radius-server cppm identity <user> key <pass>
2) Can’t just paste in – this needs user interaction
aaa authentication port-access eap-radius server-group "CPPM" authorized
comprehensive mobile experiences for their users.

## Slide 134: Colorless Ports Demo

## Slide 135
Step1: Device Connects for first time
- ClearPass assigns Profile role
Assigns Profile role
SWITCH# show port-access clients 1
Port Client Name MAC Address IP Address User Role Type VLAN
---- ------------ ------------- --------------- ------------------ ---- ----
1 98d6bb0a31f7 98d6bb-0a31f7 10.137.40.102 *DUR_Wired_Profile… MAC 40
Includes web-redirect for HTTP/S
to ClearPass
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 136
Step2: ClearPass receives device’s DHCP Request - Profiles device
Device category profiled
DHCP fingerprint
HTTP/HTTPS fingerprint
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 137
Step3: Device category change - ClearPass Forces Re-Authentication
Port disconnects for 12s
Forces port bounce
Device forgets IP address
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 138
Step4: Unknown & Profiled Device Connects
- ClearPass assigns Blocked Role
profiled
Assigns Unknown role
SWITCH# show port-access clients 1
Port Client Name MAC Address IP Address User Role Type VLAN
---- ------------ ------------- --------------- ------------------ ---- ----
1 98d6bb0a31f7 98d6bb-0a31f7 10.137.40.102 *DUR_Wired_Unknown… MAC 40
Email security team
Includes web-redirect for HTTP/S
to ClearPass
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 139
Step5a:User Experience
If the device had a browser this is the page they would get
class ipv4 DHCP match udp any any eq 67 exit class ipv4 DNS match udp any host 192.168.137.10 eq 53 exit class ipv4 ClearPass match tcp any host 192.168.137.20 exit class ipv4 HTTP match tcp any any eq 80 exit aaa authentication captive-portal profile "Isol_Page" url http://cppm.hpearubademo.com/guest/isolation.php policy user ISOLATION class ipv4 DHCP action permit class ipv4 DNS action permit class ipv4 ClearPass action permit class ipv4 HTTP action redirect captive-portal exit aaa authorization user-role name Isolation captive-portal-profile "Isol_Page" policy ISOLATION reauth-period 3600 vlan-name Isolation exit
Associated ACL loaded on to NAS
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 140
Step5b: Operator Enrol’s Device
Notification email
Force re-connect
Register the device
Login as suitable operator
Pre-filled
Pre-filled with operator’s name
Pre-filled with device type
Select role to apply
Force re-connect
Form flexibility
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 141
Step6: Known & Profiled Device Connects
Assigns Headless IoT role
SWITCH# show port-access clients 1
Port Client Name MAC Address IP Address User Role Type VLAN
---- ------------ ------------- ------------- --------------- ----- ----
1 98d6bb0a31f7 98d6bb-0a31f7 10.137.50.101 *DUR_Wired_IoT… MAC 50
Different VLAN & IP
Different VLAN & IP
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 142: Configuration

## Slide 143
Services Used
Notes: Visibility into IoT ("things") can be a unique concern. Because of the growth and diversity of IoT devices, accurately identifying IoT can be challenging.
Some IoT devices may use very similar hardware and software, but from a functional perspective, are very different. For example, a thermostat and a video surveillance camera may appear to be similar "smart" devices, but exchange data or access resources on the network quite differently.
In a case like this, ClearPass can create custom device fingerprints so that future IoT devices are correctly identified and appropriately controlled.

## Slide 144
Aruba Switch: Enable Down Loadable User Roles
Requires ClearPass 6.7.8
On receiving RADIUS Accept with DUR and index
  Switch verifies it has this DUR and matching index
  If not makes HTTPS request to ClearPass and pulls it down
  This role is cached on switch
Switch has to trust ClearPass certificate
  Install ClearPass’ signing CA (intermediate) into the switch
crypto pki ta-profile CLEARPASS
copy <sftp|tftp> ta-cert CLEARPASS <sftp|tftp server> <ca-cert-filename>
aaa authorization user-role enable download
radius-server cppm identity <CPPM DUR local account> key <pass>
Enables downloadable user roles
WARINING Disables native VLAN assignment
Requires ClearPass’ HTTPS signing cert installed on switch
Notes: If also using the switch’s native profiling then the “radius-server cppm identity <CPPM API local account> key <pass>” rather than the CPPM DUR local account
To see roles use “show user-role”

## Slide 145
class ipv4 ALLOW_ALL
10 match ip 0.0.0.0 255.255.255.255 0.0.0.0 255.255.255.255
exit
policy user PERMIT_ALL
10 class ipv4 ALLOW_ALL action permit
exit
aaa authorization user-role name DR-ACL
policy PERMIT_ALL
reauth-period 3600
vlan-name Corp
vlan-id-tagged 20
exit
aaa authorization user-role initial-role DR-ACL
aaa port-access 1-5 critical-auth user-role DR-ACL
aaa port-access 1-5 initial-role DR-ACL
Define the ACL you want
Aruba Switch: Role of last resort
NOTE
Default user-role = Denyall
Can’t vlan-named-tagged 16.08.xxxx, works on 16.09.0004
Apply to whole switch
Apply if no response
Apply if rx no rsp from CPPM
Don’t use spaces!

## Slide 146
DUR MAC Auth Policy
NOTE
In my environment roles are also passed from the Endpoint Repository

## Slide 147
Assign server role and initiate SNMP scan
IAP assign IAP tagged VLAN role and initiate SNMP scan
DUR MAC Auth Policy
Device disabled – block role and report
Device spoofed – block role and report
First device’s connection – profile role and full scan
Unknown device connects again - isolate
Unknown device – should be profiled, report to admin
AOS Controller assign Controller tagged VLAN role and initiate SNMP scan
Assign AP role and initiate NMAP scan
Assign Guest role

## Slide 148
Email – Wired Unknown Device

## Slide 149
Email – Wired Unknown Device 2
{
"to": ["derin.mellor@hpe.com"],
"subject": "Unknown Device Connected",
"headers": {"Content-Type": "text/html;charset=UTF-8"},
"message": "<html><head><style>body {background-color:#ffffff;background-repeat:no-repeat;background-position:top left;background-attachment:fixed;}h1{font-family:Arial, sans-serif;color:#000000;background-color:#ffffff;}p {font-family:Arial, sans-serif;font-size:14px;font-style:normal;font-weight:normal;color:#000000;background-color:#ffffff;}</style></head><body><h1><p style='color:#B92D5D;font-size:20px;'>An Unknown device %{Connection:Client-Mac-Address-Colon} connected</p><p>It is located at NAS-IP: %{Connection:NAD-IP-Address}, Port: %{Radius:IETF:NAS-Port-Id}.</br><b>Connection Time:</b>&nbsp%{Date:Date-Time}</br><b>Manufacturer:</b>&nbsp%{Authorization:[Endpoints Repository]:MAC Vendor}</br><b>Hostname:</b>&nbsp%{Authorization:[Endpoints Repository]:Hostname}</br><b>Device Category:</b>&nbsp%{Authorization:[Endpoints Repository]:Category}</br><b>Device OS Family:</b>&nbsp%{Authorization:[Endpoints Repository]:OS Family}</br><b>Device Name:</b>&nbsp%{Authorization:[Endpoints Repository]:Device Name}</p><p>Click&nbsp;<a href=\"https://cppm.hpearubademo.com/guest/mac_create.php?mac=%{Connection:Client-Mac-Address-Colon}&amp;device_name=%{Authorization:[Endpoints Repository]:Device Name}\">here</a> to register your device.</p></br></body></html>"
}
Have to be careful not to include <CR>!!!
Parameters must be visible in the input field

## Slide 150
Email – Wired Unknown Device 3
DEBUG
Also very useful for RESTful API debug

## Slide 151
Email – Wired Unknown Device 3
DEBUG

## Slide 152
AP DUR ACL
AOS DUR ACL
Advanced Wired DUR
Notes: Controller DUR
class ipv4 ALLOW_ALL match ip any any exit policy user PERMIT_ALL class ipv4 ALLOW_ALL action permit exit aaa authorization user-role name DUR_IAP policy PERMIT_ALL reauth-period 14440 vlan-name Management vlan-id-tagged 10,20,30,40,50,60 device port-mode poe-priority critical poe-allocate-by-class admin-edge-port exit exit
AP DUR
class ipv4 DHCP match udp any any eq 67 exit class ipv4 DNS match udp any host 192.168.137.10 eq 53 exit class ipv4 NAT_TRAV match udp any any eq 4500 exit class ipv4 SYSLOG match udp any any eq 514 exit class ipv4 PAPI match udp any any eq 8200 match udp any any eq 8209 match udp any any eq 8211 exit class ipv4 GRE match gre any any exit class ipv4 Update match tcp any any eq 21 match udp any any eq 69 exit policy user PERMIT-AP class ipv4 DHCP action permit class ipv4 DNS action permit class ipv4 NAT_TRAV action permit class ipv4 SYSLOG action permit class ipv4 PAPI action permit class ipv4 GRE action permit class ipv4 Update action permit exit aaa authorization user-role name Corp policy PERMIT-AP reauth-period 14400 vlan-name Management exit

## Slide 153
Proactive Scanning
Duplicate the “OnDemand Endpoint Scan”
Default it does not have the SNMP scan
Notes: .

## Slide 154
Proactive Scanning
To make a specific scan delete appropriately

## Slide 155: MPSK
Handling headless devices

## Slide 156
DUR MAC Auth Policy
1 MPSK SSID – Aruba only
Each device with unique PSK
Or/& many devices with common password
Assumes the users exist in a AD database with email field
Assumes AP tied to specific user
Requires ClearPass V6.8 and above
Requires AOS/IAP 8.4 and above
Does not support RadSec (AOS 6.8.0 and 8.4.0)

## Slide 157
Traditional Workflow
User enrols IoT at ClearPass
  Name and MAC address
  Each gets 8 digit unique password
Connection
  User connects device to MPSK SSID
    Using unique password
  AOS sends RADIUS Request to ClearPass
  ClearPass sends user’s password to AOS
  AOS validates password matches
If password does not match gets ~8 RADIUS Requests
  All rejected

## Slide 158: MPSK Student BYOD IoT
Key requirements
A user password for many devices
Simple mechanism to enrol an IoT device

## Slide 159
User creates his/her MPSK passcode
1) Student login to CPG as an operator
This can be a URL
2) Student creates his/her passcode
3) Student can subsequently login and see/change his/her passcode
Once created the passcode is emailed to this student
Notes: .

## Slide 160: Student Experience - 1
1) Student connects device connects to MPSK SSID using 1-to-Many passcode
ClearPass profiles the device, finds the associated student and emails him/her the details
2) Student follows link to register the device
3) Student login as ClearPass operator service
2) Student follows link to register the device

## Slide 161: Student Experience - 2
5) Student re-connects device to MPSK SSID using their unique passcode
4) Student creates the device
Fields are pre-filled

## Slide 162: Operator Perspective
5) User connects the AppleTV with his/her unique passcode (because my remote is rubbish!!!)
4) AppleTV trying with the old pass!!!
3) User registers the AppleTV
2) ClearPass emails the user associated to this AP the AppleTV details
1) User connect his/her AppleTV to MPSK SSID using the 1-to-Many passcode
ClearPass profiles the device
Might be desirable to have a dedicated enrolling SSID – no need to forget this SSID

## Slide 163: AccessTracker – 1
No profile information
1-2-Many pass returned
Only the AOS role appears
Profiled – CoA Disconnect
Location returns the user’s email
Location determines user’s email
MPSK pass hidden
User connects device using 1-to-Many pass
Reliant on AD having the AP location tied to the user

## Slide 164: Customer AD LDAP – Tie AP location to a user
Based on the NAS location information search the AD for the matching user and their email address
The RADIUS Request will indicate the AP location
Returns the associated user’s email address
Notes: Disabled AD Account: (&(sAMAccountName=%{Authentication:Username})(!(userAccountControl:1.2.840.113556.1.4.803:=2)))(objectClass=user))

## Slide 165: AccessTracker - 2
Email sponsor with details
Record fact – prevent repeat emails
After profiling device reconnects

## Slide 166: Enroll Device
Create registers the device
Auto-filled from URL device_name from Profile
Auto-filled from URL mac
Remind me of “my” user password
Receipt with details

## Slide 167: AccessTracker - 3
No profile information
Profiled – CoA Disconnect

## Slide 168: AccessTracker - 4
Update Known in Endpoints
Disconnect session – essential on AOS

## Slide 169: AccessTracker - 5
Passcode is visible!!!
Critical if you want to inject into upperlayers

## Slide 170: MPSK BYOD with Browser User Experience
Unique password per device

## Slide 171: User Experience - 1
1) User connects to the MPSK SSID using 1-to-Many passcode
2) User login to CPG as an operator
Login portal page appears
Could be a could authentication source Azure

## Slide 172: User Experience - 2
Auto-populated from URL
Auto-populated from Profile’s Device Name
What is displayed can be optimised
User enrols the device
Receipt shows the device’s unique login
User accepts details – can this be auto-accepted?

## Slide 173: User Experience - 3
Receipt with password and instructions emailed to the user

## Slide 174: User Experience - 4
User follows instructions on receipt

## Slide 175: MPSK Configuration

## Slide 176: Setup Service
Use template

## Slide 177: Setup Email
MPSK passwords are emailed to the user
Test within the CPGConfiguration ReceiptEmail Receipt
Has better error messages

## Slide 178
Tune MPSK Service
Disabled/Expired
Isolate with redirect to unknown page
Isolate with redirect to unknown page
Isolate with redirect to unknown page
Isolate + redirect to unknown page & email user
Isolate + redirect to unknown page & email operator
User’s password

## Slide 179
Location
Create LDAP search
AD’s user Stud1 room has a specific AP
Search AD for user with this AP
Notes: (&(physicalDeliveryOfficeName=%{Radius:Aruba:Aruba-Location-Id})(objectClass=user))

## Slide 180: Device references the user’s password
No profile information
Get users passcode for device
WARNING: You have to export the create MPSK pass-code profile and edit and re-import!

## Slide 181
MPSK Enrolment Service
Make known in Endpoint Repository
Force reconnect

## Slide 182: MPSK Config - 1
Changes applied to all these forms
Password complexity
Button on Create Device for MPSK.
mspk_enable field checkbox
Customize the fields in the “Create New Device” form – suggest copying and edit the copy
Always generates MPSK.
mpsk_enable field hidden
Not used!!!
Button on Create Device for MPSK.
mspk_enable field checkbox

## Slide 183: Specify the SSID to be used by the receipt - 1
Chances are this already references the Guest SSID
Replace this variable with the SSID
<li{$smarty.capture.li_1}>Connect to the wireless network: <span style="color:#{$g_email_inst_bold|escape};">
<strong><em>SSID_Name</em></strong>
</span>
</li>

## Slide 184: Specify the SSID to be used by the receipt - 2
Change the font to courier to minimise character misinterpretation

## Slide 185: Informing owner device will expire soon
Pass the email from PolicyManager using the ClearPass:User-Email-Address option
Put in a suitable operator’s account to capture the unknown accounts
This option should work as it exists in the Guest User Repository with a Type=Device

## Slide 186: AOS Configuration

## Slide 187: AOS Configuration - 1
TeamX_IOT

## Slide 188: AOS Configuration - 2

## Slide 189: AOS Configuration - 3
Create the necessary roles

## Slide 190: Correct the AOS Policy - 1
Add ClearPass as CoA server
Make sure you set this server’s shared secret

## Slide 191: Correct the AOS Policy - 2
Remove
Add

## Slide 192: Correct the AOS Policy - 3
Add
Add

## Slide 193: AOS/IAP
Create the roles that will be applied
Add appropriate security requirements

## Slide 194: MPSK Bulk Import

## Slide 195: Create a CSV
If you miss out the mpsk field it will auto-create it
The role must exist
Using MPSK
Becomes the Device Name
Default password length 8 characters

## Slide 196: Import Devices
If any field headers report FieldX then you have a typo on the filed name

## Slide 197: Infrastructure Management

## Slide 198
Aruba Switch
TACACS+ Configuration
aaa accounting commands stop-only tacacs
aaa accounting exec start-stop tacacs
aaa accounting system stop-only tacacs
aaa authentication console login tacacs
aaa authentication console enable tacacs
aaa authentication ssh login tacacs
aaa authentication ssh enable tacacs
tacacs-server host <CPPM> key <pass>
When ClearPass not accessible will revert switch’s local accounts
Notes: Authenticating is only one part of being able to control what is on your network. Just because a user or device is "authenticated", doesn't necessarily mean they are "authorized".
Authorizing users (for example: group membership), and devices (like a smart device or laptop) is essential and is a key ClearPass strength. Authorizing refers to what the user or device is "allowed to do" or "allowed to access". ClearPass does both! ClearPass Policy Manager delivers a precise and consistent role-based access privileges that adapts to the current circumstances.
As shown in the image here, a user with an organization-issued device with strong authentication, is given a wide range of access. The same user with a BYOD device (by policy), will have a reduced set of privileges. This is all configurable with the ClearPass Policy Manger which allows organizations to tune their policies based upon their security priorities, balanced with their goals to provide rich, comprehensive mobile experiences for their users.

## Slide 199
TACACS
Configuration
ClearPass TACACS Service
ClearPass Assigned Profile
Notes: Authenticating is only one part of being able to control what is on your network. Just because a user or device is "authenticated", doesn't necessarily mean they are "authorized".
Authorizing users (for example: group membership), and devices (like a smart device or laptop) is essential and is a key ClearPass strength. Authorizing refers to what the user or device is "allowed to do" or "allowed to access". ClearPass does both! ClearPass Policy Manager delivers a precise and consistent role-based access privileges that adapts to the current circumstances.
As shown in the image here, a user with an organization-issued device with strong authentication, is given a wide range of access. The same user with a BYOD device (by policy), will have a reduced set of privileges. This is all configurable with the ClearPass Policy Manger which allows organizations to tune their policies based upon their security priorities, balanced with their goals to provide rich, comprehensive mobile experiences for their users.

## Slide 200
TACACS Authentication

## Slide 201
TACACS Accounting & Audit
Look at this

## Slide 202
TACACS Issues
Current version does not send TACACS Reject!
  Sends TACACS Accept with priv=0
Some devices will allow access!
Fix should appear in next major release

## Slide 203: IPv6 Support

## Slide 204: ClearPass support for IPv6
IPv6 ClearPass GUI
  Including Policy Manager, CPG and Insight
IPv6 Guest captive portal
IPv6 RESTful API into ClearPass
IPv4 with PostAuth (v2) with IPv6 address
  Ability to inject in to upstream device
  IPv6 RadSec (eduroam) – 6.8.3Pv6
Supported
Roadmap
In bold next major release
IPv6 RADIUS Request
IPv6 RADIUS Accounting
IPv6 TACACS+
IPv6 RADIUS DM/CoA
IPv6 RADIUS Proxying (eduroam)
IPv6 RADIUS Accounting Proxying
  Injection into upper-layer devices
IPv6 ClearPass clustering
IPv6 RESTful API from ClearPass
IPv6 Profiling
  Including DHCP, SNMP, SSH, WMI and NMAP
IPv6 AirGroup

## Slide 205: Certificate distribution

## Slide 206
Challenges
Onboard too reliant on underlying operating system
Deploy using MDM with SCEP or EST
Maybe Device Provisioning Protocol will fix in the future?

## Slide 207: ClearPass Operational Health Check

## Slide 208
Review cluster operation
ClearPass AccessTracker is a great tool
BUT
When arrival of events above a couple per minute - operation can miss important information
Reliant on user complaints!
Use the Insight database to identify suspicious behaviour

## Slide 209
Review cluster operation: Insight Report
Load across cluster
Distribution across cluster

## Slide 210
More Detail
To get more detail we have to connect to Insight’s database
I use freeware pgAdmin4 to interface with this
Set your appexternal password

## Slide 211
Setup pgAdmin4

## Slide 212
Review cluster operation
Access License Usage over Time
SQL in notes
Notes: SELECT * FROM cppm_license WHERE node_ip = '10.200.33.54' AND app_name = 'Access' AND timestamp >= '2019-01-13 23:59:59' AND timestamp < '2019-02-13 23:59:59' ORDER BY timestamp ASC

## Slide 213
Review cluster operation
Detailed breakdown of errors
SQL in notes
Notes: SELECT count(cppm_system_events.level), source, level, category, action, description FROM cppm_system_events WHERE timestamp > (current_date - interval '1' month) AND cppm_system_events.level != 'INFO' GROUP BY source, level, category, action, category, description ORDER BY count DESC LIMIT 10

## Slide 214
Review cluster operation
Failed RADIUS Authentications
per Service
Similar reports can be generated for TACACS
SQL in notes
Notes: SELECT auth.service, COUNT(*) AS Total, COUNT(*) FILTER (WHERE error_code = 0) as Success, 100*(COUNT(*) FILTER (WHERE error_code = 0))/COUNT(*) AS Percent_Success, COUNT(*) FILTER (WHERE error_code != 0) as Failed, 100*(COUNT(*) FILTER (WHERE error_code != 0))/COUNT(*) AS Percent_Failed FROM auth WHERE timestamp > (current_date - interval '1' month) GROUP BY auth.service ORDER BY percent_failed DESC

## Slide 215
Review cluster operation
Null Service
SQL in notes
Notes: SELECT count(*) AS Matches, auth.mac, auth.username, cppm_error_codes.error_code_str, CASE WHEN auth.nas_port_type='19' THEN 'Wireless' WHEN auth.nas_port_type='15' THEN 'Wired' WHEN auth.nas_port_type='05' THEN 'VPN' ELSE auth.nas_port_type END AS Media, nads.name, auth.nad_ip, nads.location, auth.nas_port_id, auth.ssid, auth.ap_name, endpoints.device_category, endpoints.device_family FROM public.auth JOIN nads ON auth.nad_ip = nads.ip JOIN endpoints ON auth.mac = endpoints.mac JOIN cppm_error_codes ON auth.error_code = cppm_error_codes.error_code WHERE auth.timestamp > (current_date - interval '1' month) AND auth.service IS NULL GROUP BY auth.mac, auth.username, auth.nas_port_type, cppm_error_codes.error_code_str, nads.name, auth.nad_ip, nads.location, auth.nas_port_id, auth.ssid, auth.ap_name, endpoints.device_category, endpoints.device_family ORDER BY Matches DESC LIMIT 10

## Slide 216
Review cluster operation
Drill into specific device
SQL in notes
Similar reports can be generated for TACACS
Notes: SELECT auth.timestamp, auth.mac, auth.username, auth.auth_method, auth.auth_status, CASE WHEN auth.nas_port_type='19' THEN 'Wireless' WHEN auth.nas_port_type='15' THEN 'Wired' WHEN auth.nas_port_type='05' THEN 'VPN' ELSE auth.nas_port_type END AS Media, auth.nas_identifier, auth.nad_ip, auth.nas_port_id, auth.service, cppm_error_codes.error_code_str FROM public.auth JOIN nads ON auth.nad_ip = nads.ip JOIN endpoints ON auth.mac = endpoints.mac JOIN cppm_error_codes ON auth.error_code = cppm_error_codes.error_code WHERE auth.mac='e8393591ae90' ORDER BY session_id ASC LIMIT 100

## Slide 217
Review cluster operation
Top 10 Failed RADIUS Authenticationd
SQL in notes
These invariably are failing too often
Each should be investigated
Similar reports can be generated for TACACS
Notes: SELECT count(*) AS Failed, auth.mac, auth.service, CASE WHEN auth.nas_port_type='19' THEN 'Wireless' WHEN auth.nas_port_type='15' THEN 'Wired' WHEN auth.nas_port_type='05' THEN 'VPN' ELSE auth.nas_port_type END AS Media, nads.name, auth.nad_ip, nads.location, auth.nas_port_id, auth.ssid, auth.ap_name, cppm_error_codes.error_code_str FROM public.auth JOIN nads ON auth.nad_ip = nads.ip JOIN cppm_error_codes ON auth.error_code = cppm_error_codes.error_code WHERE auth.timestamp > (current_date - interval '1' month) AND auth.error_code != 0 GROUP BY auth.mac, auth.nas_port_type, nads.name, auth.nad_ip, nads.location, auth.nas_port_id, auth.ssid, auth.ap_name, error_code_str, auth.service ORDER BY Failed DESC LIMIT 10

## Slide 218
Review cluster operation
Top 10 Successful RADIUS Authentications
SQL in notes
These invariably are authenticating too often
Each should be investigated
Similar reports can be generated for TACACS
Notes: SELECT count(*) AS Success, auth.mac, auth.service, CASE WHEN auth.nas_port_type='19' THEN 'Wireless' WHEN auth.nas_port_type='15' THEN 'Wired' WHEN auth.nas_port_type='05' THEN 'VPN' ELSE auth.nas_port_type END AS Media, nads.name, auth.nad_ip, nads.location, auth.nas_port_id, auth.ssid, auth.ap_name, endpoints.device_category, endpoints.device_family FROM public.auth JOIN nads ON auth.nad_ip = nads.ip JOIN endpoints ON auth.mac = endpoints.mac WHERE auth.timestamp > (current_date - interval '1' month) AND auth.error_code = 0 GROUP BY auth.mac, auth.nas_port_type, nads.name, auth.nad_ip, nads.location, auth.nas_port_id, auth.ssid, auth.ap_name, auth.service, endpoints.device_category, endpoints.device_family ORDER BY Success DESC LIMIT 10

## Slide 219
To boldly split infinitives
Derin